## Slide 1: Imaging cryogenic detectors for space based astronomy
J. van der Kuur1, L. Gottardi2, H. Akamatsu2, P. Khosropanah2, R. den Hartog2, R. Hijmering2, D. Audley2, B. Jackson1
1) SRON Netherlands Institute for Space Research, Landleven 12, 9747AD Groningen
2) SRON Netherlands Institute for Space Research, Sorbonnelaan 2, 3584CA Utrecht

## Slide 3: XMM X-ray observatory
In orbit since december 1999
CCD detectors
Grating spectrometers
Energy resolution limited at high energies (20eV @ 2.1keV)
X-ray astronomy requires ΔE < 3eV @ 6keV
Notes: Astronomers interested in the intensity and color of light.

## Slide 4: Cryogenic microcalorimeter operating principle
T = 100mK

## Slide 5: Thermometer sensitivity TES
Superconducting phase transition near Tc
Strong dependence resistance - temperature
Tc tuned by proximity effect
Normalized sensitivity (α=(dR/R)/(dT/T)):
  Si thermistor ~ α=1-5
  TES ~ α=100

## Slide 6
X-ray pixel micrograph
Development of high-filling factor and high QE pixels array
250x250um sputtered Bi on electroplated Au
TiAu TES with uniform current distribution

## Slide 7: Optical coupling scheme
Absorber 200x200 μm
TES
Horn
Spherical Backshort
NEP ~ 2 10 -19 W/√Hz

## Slide 8: 38x38 bolometer array
NEP = 2*10-19 W/rtHz
Notes: These are some of the prototypes already fabricated to demonstrate the feasibility of achieving 10-19W/rt Hz at 100mK. Low A/L in the legs is required. If the legs are zig zag, then the ballistic phonons have a better chance of being scattered.

## Slide 9: Summary detector properties
property | value
Number of pixels | ~4000 (64 x 64)
Pixel size | 250 μm x 250 μm
Energy range | 0.2 – 12 keV
Energy resolution | < 2.5 eV
Detector operating temperature | 100 mK
Cooler operating temperature | 50 mK
Heat lift @ 50mK | 1 μW
Target application | X-ray astronomy
Further uses | Material analysis, non-proliferation, infrared bolometers

## Slide 10: Thank you