## Slide 1
FCC Detectors and Experiments
Topical Lectures ‘Physics at future accelerators’
NIKHEF, June 8th, 2018
W. Riegler, CERN
Future Circular Collider (FCC) is an integral conceptual design study for post-LHC particle accelerator options in a global context. It is exploring the potential of hadron and lepton circular colliders, performing an in-depth analysis of infrastructure and operation concepts and considering the technology research and development programs that would be required to build a future circular collider. A conceptual design report will be delivered before the end of 2018​, in time for the next update of the European Strategy for Particle Physics. This talk will give an overview of the FCC studies and present aspects of experiments and detectors at such machines.

## Slide 2
Large Hadron Collider at CERN, Geneva, 14TeV pp collisions
27km
8.3T dipoles
p=0.3xRxB
1983 First concept
2009 First physics
2025 Luminosity upgrade
2035 End of exploitation

## Slide 3
27km
8.3T Dipoles
Large Hadron Collider at CERN, Geneva, 14TeV pp collisions

## Slide 4
ATLAS, CMS, ALICE, LHCb

## Slide 5
ATLAS, ALICE

## Slide 6
CMS, LHCb

## Slide 7
July 4th 2012

## Slide 8
The Standard Model of Particle Physics

## Slide 9
91 Persons got Nobel Prices related to the development of the Standard Model
59 Experiment
33 for Standard Model Experiments
13 for Standard Model Instrumentation and Experiments
3 for Particle Physics Instrumentation
1 for Relativity Experiment (Michelson)
9 for Quantum Mechanics Experiments
32 Theory
23 for Standard Model Theory
9 for Quantum Mechanics Theory
Some very biased statistics from an experimentalist

## Slide 10
Scope of FCC Study
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)
 main emphasis, defining infrastructure requirements
~16 T  100 TeV pp in 100 km
~100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee) as potential first step
p-e (FCC-he) option, integration one IP, e from ERL
HE-LHC with FCC-hh technology (LHC Ring 816T, 1428TeV)
CDR for end 2018

## Slide 11
M. Mangano, Oct. 2017

## Slide 12
M. Mangano, Oct. 2017

## Slide 13
M. Mangano, Oct. 2017

## Slide 14
M. Mangano, Oct. 2017

## Slide 15
Conceptual Design Report
Required for end 2018, as input for European Strategy Update
Common physics summary volume
Three detailed volumes FCChh, FCCee, HE-LHC
Three summary volumes FCChh, FCCee, HE-LHC
7 – High Energy LHC Comprehensive
Accelerator
Injectors
Infrastructure
Refs to FCC-hh, HL-LHC, LHeC
6
High Energy LHC
Summary
1 – PHYSICS
Physics opportunities across all scenarios
5 – Lepton Collider Comprehensive
Accelerator
Injectors
Technologies
Infrastructure
Operation
4
Lepton
Collider
Summary
Experiment
3 – Hadron Collider Comprehensive
Accelerator
Injectors
Technologies
Infrastructure
Operation
2
Hadron
Collider
Summary
Experiment
eh

## Slide 16
Total crossection and Minimum Bias Multiplicity show only a modest increase from LHC to FCC-hh.
The crossection for interesting processes shows however significant increase !
Interesting stuff is sticking out more !!
Going from pileup of 140 at HL-LHC to pileup of 1000 at FCC does however reduced this possible advantage for triggering.
Crossections for key processes

## Slide 24
New features:
Overall length 97.75 km
Economy length 2.25 km
Injections upstream side of experiments
Avoids mixing of extraction region and high-radiation collimation areas
Taking this layout as fixed
(for CDR preparation)
Two high-luminosity experiments (A & G)
Two other experiments combined with injection (L & B)
Two collimation insertions
  Betatron cleaning (J)
  Momentum cleaning (F)
Extraction insertion (D)
Clean insertion with RF (H)
Compatible with LHC or SPS as injector
FCC-hh new layout

## Slide 25
Implementation - new footprint baseline
Optimisation in view of accessibility surface points, tunneling rock type, shaft depth, etc.
Tunneling
Molasse 90%, Limestone 5%, Moraines 5%
Shallow implementation
~ 30 m below lakebed
Reduction of shaft length and technical installations
One very deep shaft F (RF or collimation), alternatives being studied, e.g. inclined access

## Slide 26
FCC-hh integration
  Basic layout following LHC concept
  6 m inner tunnel diameter
  Main space allocation:
    1200 mm cryo distribution line (QRL)
    1480 mm installed cryomagnet
    1600 cryomagnet magnet transport
    >700 mm free passage.

## Slide 27
HE-LHC integration aspects
  Working hypothesis for HE LHC design:
  No major CE modifications on machine tunnel and caverns
  Similar geometry and layout as LHC machine and experiments
  Maximum magnet cryostat external diameter compatible with LHC tunnel ~1200 mm
  Classical 16 T cryostat design based on LHC approach gives ~1500 mm diameter!
Strategy: develop a single 16 T magnet, compatible with both HE LHC and FCC-hh requirements:
  Allow stray-field and/or cryostat as return-yoke
  Optimization of inter-beam distance (compactness)
   Smaller diam. also relevant for FCC-hh cost optimization

## Slide 28
Cryogenic beam vacuum system
One of the most critical elements for FCC-hh
Absorption of synchrotron radiation at ~50 K for cryogenic efficiency (5 MW total power)
Provision of beam vacuum, suppression of photo-electrons, electron cloud effect, impedance, etc.
FCC Beamscreen prototype for test at ANKA:
External copper rings for heat transfer to cooling tubes

## Slide 29
Beam and Luminosity Evolution
During the beams are in collision the instantaneous value of the luminosity will change:
The beam evolution with time is obtained by solving a system of four differential equations (dominant effects only shown here, more included in simulations):
with
: revolution freq.
: no. bunches/beam
: β-function at IP
: no. particles/bunch
: geom. emittances
: bunch length
: total cross-section
: IBS growth rate
: rad. damping rate
Intensity
Hor. Emittance
Ver. Emittance
Bunch Length
J. Jowett, M. Schaumann,
FCC week Washington 2015

## Slide 30
Effects on the Emittance – a new regime
Intra-Beam Scattering (IBS)
(Synchrotron) Radiation Damping
Emittance Growth
Emittance Shrinkage
Growth rate dynamically changing with beam properties:
Damping rate is constant for a given energy:
IBS is weak for initial beam parameters, but increases with decreasing emittance .
Multiple small-angle Coulomb scattering within a charged particle beam.
A charged particle radiates energy, when it is accelerated, i.e. bend on its circular orbit.
Fast emittance decrease at the beginning of the fill,
until IBS becomes strong enough to counteract the radiation damping.

## Slide 31
Ultimate example, 25ns, no luminosity levelling
8fb-1/day
Turn-around time
Developed model including most relevant effects
Improvement with more detail planned
Reach 8fb-1/day with ultimate for 25ns spacing
    5ab-1 per 5 year run
Beam is burned quickly
  A reason to have enough charge stored
X. Buffat, D.S..
pp Luminosity evolution during a fill

## Slide 32
Pb-Pb Luminosity evolution during a fill
FCC-hh is also a very powerful Heavy Ion collider !

## Slide 33
Draft Schedule Considerations
20
22
24
26
28
30
32
34
38
40
Civil Engineering FCC-hh ring
Dipole short models
16 T dipole indust. prototypes
16 T dipoles preseries
16 T series production
SC Magnets
CE FCC-ee ring + injector
FCC-hh
FCC-ee
HE-LHC
Strategy Update 2026 – assumed project decision
Installation HE-LHC
LHC Modification
42
Technical Design Phase
36
Installation + test FCC-ee
Installation + test FCC-hh
CE TL to LHC
LHC Removal
Dipole long models
Injector

## Slide 34
Exploration + Higgs as a tool for discovery
How to specify detectors for such a machine ?
ATLAS and CMS are general purpose detectors that were benchmarked with the ‘hypothetical’ Higgs in different mass regions with tracking up to η=2.5.
The Higgs is also key benchmark for the FCC detectors, with highly forward boosted features (100TeV, 125GeV Higgs)
FCC detectors must be ‘general general’ purpose detectors with very large η acceptance and extreme granularity.
Physics at a 100 TeV Hadron Collider

## Slide 35
Physics at a 100 TeV Hadron Collider

## Slide 36
Physics at a 100 TeV Hadron Collider

## Slide 37
Physics at a 100 TeV Hadron Collider

## Slide 38
Detector Specifications

## Slide 39
FCC week 2016: Twin Solenoid 6T, 12m bore, Dipoles 10Tm

## Slide 40
Twin solenoid with dipoles (min. shaft diameter 27.5m)
Partially shielded solenoid with dipoles
Unshielded solenoid with dipoles
Twin solenoid with balanced conical solenoid
Magnet systems under consideration
Unshielded solenoid with balanced conical solenoid

## Slide 41
6T, 12m bore solenoid, 10Tm dipoles, shielding coil
65 GJ Stored Energy
28m Diameter
>30m shaft
Multi Billion project
New Reference Design
4T, 10m bore solenoid, 4T forward solenoids , no shielding coil
14 GJ Stored Energy
Rotational symmetry for tracking and trigger !
20m Diameter (≈ ATLAS)
15m shaft
≈ 1 Billion project

## Slide 42
Reference detector for the CDR
4T 10m solenoid
Forward solenoids
Silicon tracker
Barrel ECAL Lar
Barrel HCAL Fe/Sci
Endcap HCAL/ECAL LAr
Forward HCAL/ECAL LAr
This is a reference detector that ‘can do the job’ and that is used to define the challenges.
The question about the specific strategy for detectors at the two IPs is a different one.

## Slide 43
CDR will discuss performance with forward dipoles
B
B
B
B
B
B
B
B
compensation
compensation

## Slide 44
Comparison to ATLAS & CMS

## Slide 45
Comparison to LHCb & ALICE

## Slide 46
70m
80m
Q1 TAS Shield
66m
Cavern Length
L*=40m  Distance between Q1&Q1 = 80m
TAS = 3.5m  Distance between TAS & TAS = 70m
TAS Shielding in Tunnel = 2m  Cavern Length = 66m
Cavern length of 66m is compatible with the opening scenario of the present detector.
Shield TAS Q1

## Slide 47
ATLAS Cavern
50m
30m
35m
12.6m diameter
18m diameter
ATLAS shafts and cavern, with cavern length increased from 50-70m will accommodate the reference detector
A cavern width of 35m would also accommodate the FCC-ee experiments assuming the present footprint with IP shift of 10m.

## Slide 48
Service Cavern
50m distance from main cavern to ensure <5mT field and to allow easier construction.
Placing the service cavern closer requires an iron shield between cavern and service cavern.

## Slide 49
Central tracker:
  first IB layer (2.5 cm ): ~1.2 1010 cm-2s-1
  external part: 3 106 cm-2s-1
  Barrel muon chambers: ~300 cm-2s-1 to ~500 cm-2s-1
Charged Particle Fluence @ L=30x1034cm-2s-1
  Endcap Muon Chambers: 104 cm-2s-1

## Slide 50
Muon Systems
ATLAS muon system HL-LHC rates (kHz/cm2):
MDTs barrel: 0.28
MDTs endcap: 0.42
RPCs: 0.35
TGCs: 2
Micromegas und sTGCs: 9-10
<10kHz/cm2
r>1m rate<500kHz/cm2
<0.5kHz/cm2
LHCb
HL-LHC muon system gas detector technology will work for most of the FCC detector area

## Slide 51
Central tracker:
first IB layer (2.5 cm ): ~5-6 1017 cm-2
external part: ~5 1015 cm-2
Forward calorimeters:
  maximum at ~5 1018 cm-2 for both the EM and the HAD-calo
  1016 cm-2 at R=2 m
1 MeV neutron equivalent fluence for 30ab-1

## Slide 52
Comparison to ATLAS & CMS
2.7
3.0
2.5
The forward calorimeters are a very large source of radiation (diffuse neutron source).
In ATLAS the forward calorimeter is inside the endcap calorimeter, in CMS the forward calorimeter is inside enclosed by the return Yoke.
For the FCC, the forward calorimeter is moved far out in order to reduced radiation load and increase granularity.
 A shielding arrangement is needed to stop the neutrons to escaping into the cavern hall and the muon system.

## Slide 53
Tracker Radius 1.6m, Length 32m

## Slide 54
Magnetic Field Options

## Slide 55
Magnetic Field, Tracking
Forward solenoid adds about 1 unit of η to full lever arm acceptance.
B-field non uniformities deteriorate the tracking by 35-45% with respect to a constant field of 4T, which has negligible impact on performance.

## Slide 56
Tracker Performance

## Slide 57
Parametrized Tracking Performance

## Slide 58
HL-LHC average distance between vertices at z=0 is
≈ 1mm in space and 3ps in time.
For 6 times higher luminosity at FCC-hh (an HE-LHC) this would become
≈ 170μm in space and 0.5ps in time.
x=0.8mm, X0=35.28cm (Be), p=1GeV
r = 2.5cm
Δz
θ0
η
Beam
Beampipe
Pileup of 1000 (25ns Bunchcrossing)
Even having a perfect tracking detector, the error due to multiple scattering in the beampipe for η > 1.7 is already larger than the average vertex distance !
Timing, very clever new ideas needed …

## Slide 59
Vertexing at Pileup of 1000, Timing
Effective pileup – number of vertices assigned at 95% CL to a track of a given momentum.

## Slide 60
Tracking

## Slide 61
Track Parameters
https://arxiv.org/abs/1805.12014

## Slide 62
Relation to two simple Geometries

## Slide 63
Track of known functional form
with (M+1) unknown parameters ai
Given the measurement values yn in the N+1 detector planes, how can we find the best estimates for ai and what are their errors ? E.g. if σn are the position measurement errors in plane yn we have to minimise
In case we have other sources of measurement errors that could also be correlated …
Fitting a linear combination of known functions

## Slide 64
In case we have other sources of measurement errors that could also be correlated …
Where Wmn is a ‘weight matrix’ that still has to be defined. For Wmn = σn 𝛿mn we get the previous expression.
The above relation can also be written in Matrix Form:
Fitting a linear combination of known functions

## Slide 65
Find ai sich that 𝜒2 is minimized
The is the best estimate for ai given the measurements yi
Next question:
What is the variance of ai for a given (known) variance of the measurement values yi
We need to know the covariance matrix of yi
Fitting a linear combination of known functions

## Slide 66
Error Propagation
Let’s assume two random variable y0 and y1 to be distributed according to
The average, variance and correlation of y0 and y1 are given by
Cy is the ‘Covariance’ Matrix of y0 and y0.
In case y0 and y1 are uncorrelated, the covariance matrix is diagonal

## Slide 67
Error Propagation
Let’s assume a function a0 (y0, y1). We want to know the variance of a0 if y0 and y1 are distributed according to p(y0, y1)
If a0 (y0, y1) is not varying significantly in the region around the average values of y0, y1 we can expand the function around the average values

## Slide 68
Error Propagation
Let’s now assume a vector of functions ai (y0, y1). If we want to know the variances and correlations in case y0 and y1 are distributed according to p(y0, y1) we proceed accordingly
And in general

## Slide 69
Continuing from before:
Fitting a linear combination of known functions
Last question: What is the best choice of W that minimizes the variances ?
The answer is given by the Gauss-Markov Theorem stating that which results in

## Slide 70
Track of known functional form
with (M+1) unknown parameters ai
Fitting a linear combination of known functions

## Slide 71
Covariance Matrix for position resolution and multiple scattering
Assuming a Gaussian distribution for the position resolution and for the multiple scattering angle we have:
In case there are N+1 equidistant and equal layers between x=0 and x=L with the same position resolution σ and multiple scatterin angle σ⍺ we have

## Slide 72
Covariance Matrix for position resolution and multiple scattering
If multiple scattering is negligible we have:
If multiple scattering dominates over position resolution:

## Slide 73
Straight line track
Independent of N !
Two layers as good as N layers !

## Slide 74
r = 2.5cm
θ0
η
Beam
Beampipe
Beampipe + first tracking layer define the vertex resolution at low pT.
Vertex resolution

## Slide 75
Parabolic track, position resolution

## Slide 76
Parabolic track, multiple scattering, momentum resolution

## Slide 77
Parabolic track, multiple scattering, angular resolution

## Slide 78
Parabolic track, multiple scattering, d0 resolution

## Slide 79
Track Parameters

## Slide 80
10 layers
10um position resolution
L=1m
B=4T
Momentum resolution
With 3% per layer, multiple scattering dominates the momentum resolution up to 100GeV/c !

## Slide 81
Track Parameters

## Slide 82
Track Parameters

## Slide 83
Track Parameters

## Slide 84
d0 resolution
3 layers
5um position resolution
first layer at 4cm
1.5% X0 per layer
Up to 10GeV/c, multiple scattering dominates

## Slide 85
Calorimetry

## Slide 90
Calorimetry
Barrel HCAL in Fe/Sci similar to ATLAS Tilecal
Barrel ECAL, Endcap ECAL/HCAL, Forward ECAL/HCAL are in LAr technology, which is intrinsically radiation hard.
Silicon ECAL and ideas for digital ECAL with MAPS are being discussed.

## Slide 91
Barrel HCAL Single Particle and Jet Resolution

## Slide 92
Calorimeter Granularity

## Slide 95
Muon system performance estimate
We assume a constant magnetic field inside the coil radius L1.
The measurement points in the tracker of radius L0 are equidistant and have all the same resolution σ0.
The measurement point at L1 has a position error σ1 that is given by the multiple scattering inside the calorimeters
(σy in the following).
The formula for the momentum resolution is given in the next slide.
L1
L0
LCalo
Three ways to measure the muon momentum
Tracker only with identification in the muon system
Muon system only by measuring the muon angle where it exits the coil
Tracker combined with the position of the muon where it exists the coil
pt=3.9GeV enters muon system
pt=5.5GeV leaves coil at 45 degrees

## Slide 96
2) Muon System standalone by measuring the angle of the muon when exiting the coil
1) Inner Tracker of radius L0 with N+1 equidistant layers of resolution σ0
3) Combined
Muon system performance estimate

## Slide 97
Tracker only with identification in the muon system
Muon system only by measuring the muon angle where it exits the coil
Tracker combined with the position of the muon where it exists the coil
Muon Systems
1)
2)
3)
With 50μm position 70μRad angular resolution resolution we find (η=0)
<10% standalone momentum resolution up to 3TeV/c
<10% combined momentum resolution up to 20TeV
All within reach of ‘standard’ muon system technology

## Slide 98: Muon Detector Layout – Optimised with the Simulation
Barrel and outer endcaps:
2 x 4 layers of 2.8 m long drift tubes (axial in barrel, radial in outer endcaps) with 1.4 m multilayer distance provide 40 µm spatial resolution, 60 µrad angular resolution, 100% tracking efficiency up to the maximum background rates. Monolithic sMDT construction, no optical alignment of multilayers needed. Chambers well accessible.
2.8 m
1.4 m
6 m
20 m
2.8 m
2 m
RPC

## Slide 99
Muon Standalone Performance

## Slide 100
Trigger/DAQ
Example: ATLAS Phase2 calorimetry will be digitized at 40MHz and sent via optical fibers to L1 electronics outside the cavern at 25TByte/s to create the L1 Trigger.
Muon system will also be read out at 40MHz to produce a L1 Trigger.
Reading out the FCC detector calorimetry and muon system at 40MHz will result in 200-300 TByte/s, which seems feasible.
40MHz readout of the tracker would produce about 800TByte/s.
Question:
Can the L1 Calo+Muon Trigger have enough selectivity to allow readout of the tracker at a reasonable rate of e.g. 1MHz ?
Un-triggered readout of the detector at 40MHz would result in 1000-1500TByte/s over optical links to the underground service cavern and/or a HLT computing farm on the surface.

## Slide 101: ATLAS & CMS @ HL-LHC (2025-2026)
10-20 GB/s
Storage
Level 1
HLT
5-10 kHz (2MB/event)
40 GB/s
Storage
Level 1
HLT
10 kHz (4MB/event)
 PEAK OUTPUT 
40 MHz
0.5-1 MHz
Hardware trigger to reduce events rate by factor 40

## Slide 102
40 MHz
40 MHz
5-40 MHz
20 kHz (0.1 MB/event)
2 GB/s
Storage
Reconstruction
+
Compression
50 kHz
75 GB/s
50 kHz (1.5 MB/event)
 PEAK OUTPUT 
No Hardware trigger, all data into HLT !
ALICE & LHCb in LS2 (2019-2020)

## Slide 103
http://www.livescience.com/23074-future-computers.html
“If the doubling of computing power every two years continues to hold, then by 2030 whatever technology we're using will be sufficiently small that we can fit all the computing power that's in a human brain into a physical volume the size of a brain”,
explained Peter Denning, distinguished professor of computer science at the Naval Postgraduate School and an expert on innovation in computing.
"Futurists believe that's what you need for artificial intelligence. At that point, the computer starts thinking for itself.“
Computers will anyway by themselves figure out what to do with the data by 2035.
Moore‘s Law

## Slide 104
Strategic R&D
The ATLAS/CMS Phase2 TDRs are being prepared. R&D for Phase2 is coming to an end.
The FCC CDR will be finished by end of 2018.
Strategic detector R&D plans must be discussed now, and put in place by 2019, that push and develop technology towards the next step.
FCC-hh and HE-LHC have very similar detector technology requirements in terms of resolution and radiation hardness.
FCC-hh, FCC-ee, FCC-eh have similar sensor technology requirements in terms of resolution and material budget.
Key technologies are radiation hard silicon sensors, radiation hard Monolithic Active Pixel Sensors (MAPS), Large scale integrated CMOS sensors, high speed low power optical links, radiation hard calorimetry, high precision timing detectors, large scale muon systems, and related electronics etc.

## Slide 112
A 100TeV hadron collider with 100km circumference and 16T dipoles is being studied as the next machine to push the energy frontier.
A peak luminosity of 30x1034 cm-2s-1 at 25ns bunchcrossing results in a pileup of ≈ 1000.
An integrated luminosity of 20-30 ab-1 results in a fluence of ≈ 1016-1018 1MeVneq/cm2 in the tracker volume and the forward calorimeters.
A general purpose reference detector is being studied to set the scale of the challenges for performing experiments at this machine.
We think that detectors can be built that can extract all the physics potential from such a machine, but a high profile R&D programme for detectors and electronics technologies has to be conducted.
Summary