## Slide 1: Development of a GridPix readout for a TPC at the International Linear Collider
Cornelis Ligtenberg, Y. Bilevych, K. Desch, H. van der Graaf, M. Gruber, F. Hartjes, K. Heijhoff,
J. Kaminski, N. van der Kolk, P.M. Kluit, G. Raven, L. Scharenberg, T. Schiffer, S. Schmidt, J. Timmermans
2 November 2018, NNV Annual meeting, Lunteren

## Slide 2: The International Linear Collider
20 km first stage at 250 GeV
The ILC is a proposed Linear electron-positron collider with polarized beams
A first stage as a 250 GeV Higgs factory
Extendable to higher energies of 500+ GeV
Clean environment allows for precise detectors and measurements

## Slide 3: Some physics goals of the ILC
What is the origin of EWSB?
How can the Higgs bosons be so light?
Are there more Higgs bosons?
What is dark matter made of?
LHC (3 ab-1)
LHC + ILC 250 GeV ( 2 ab-1)
LHC + ILC 250 GeV + ILC 500 GeV (4 ab-1)
https://arxiv.org/pdf/1710.07621.pdf

## Slide 4: The International Large Detector
ILD is a detector concept for ILC
The ILD uses a TPC as the central tracker to measure the momentum of particles
TPC (gaseous detector) advantages
  Minimal material budget and very homogenous Little scattering
  Many hits per track effective track finding
  Particle identification by dE/dx
  Cost effective
TPC

## Slide 5: Readout technologies for ILD TPC
Pads with GEMs or Micromegas for amplification Detect charge spread
Pixels readout with integrated aligned amplification grid (Gridpix)
detect each single electron
Maximal possible information from track
Track
-Edrift
e-
e-
e-
e-
e-
e-
e-
e-
e-
Ionisation in gas
Amplification
and detection at readout plane
e-
e-
e-
e-
e-
e-
e-
e-
e-
55 µm

## Slide 6: Detector setup at Bonn test beam (2017)
A Timepix3 based Gridpix with SPIDR readout
  Simultaneous data-driven detection of time and time over threshold (charge) allows for timewalk corrections
  Higher rates and more precise (1.56 ns time resolution) compared to its predecessor Timepix1
2.5 GeV electrons
@Bonn
Detector with guard and field shaper
See also paper on this testbeam: https://doi.org/10.1016/j.nima.2018.08.012

## Slide 7: Map of Timepix3 hits
Successfully measured a large number of hits
The chip and grid have some small defects
beam
Wrinkle in grid
Broken column

## Slide 8: Single hit resolution in pixel plane
Single hit resolution in pixel plane:
Depends on:
pixel size
Diffusion from fit
Note that:
A hit resolution of 250 µm is 25 µm for a 100-hit track ( 1 cm track length)
At 4 T ,
( expected)
B T

## Slide 9: Deformations in pixel plane and drift direction
For applications in a large TPC, systematic deviations must be well under control
Each bin displays mean of residuals from 4×4 pixels at expected position
The RMS of the mean residuals is 7 µm in the pixel plane, and 21 µm (0.3 ns) in the drift direction Overall grid quality is very good

## Slide 10: Particle identification by dE/dx
Find the energy loss (dE/dx) by truncated sum:
Merge 83 single chip events together to make one track of 1 meter
Count the number of hits per intervals of 20 pixels
Reject the top 10% of intervals with the most hits and sum the other 90% into a truncated sum
There is a 8.8𝜎 separation between a 2.5 GeV electron and minimum ionizing particle
The resolution (RMS/mean) is 4.1% for an effective track length of 1 m ( ILD TPC effective track length)
Scale electron track to MIP
Electron: 0.7
MIP: 1.0
0.7)

## Slide 11: Quad module development
Developed a 4-chip module with all services under the active area
Active area coverage is 70% (Through-silicon via technology might increase this)
Can be used as a building block to cover arbitrarily large TPC areas
Cooling channels
Stump
LV-
regulation
Guard
Flex
Cold carrier plate
Wirebond
PCB
Quad base plate
Quad
Quad without guard
Test Box

## Slide 12: Quad tested with electron beam at Bonn (2018)
Also tested in another test beam with 2.5 GeV electrons at the ELSA Facility in Bonn on 4-5 October 2018
Analysis just started…
Improved Quad setup in test beam at Bonn
Preliminary

## Slide 13: Performance of a GridPix TPC at ILC
From full DD4HEP (Geant4) simulation, momentum resolution can be determined
Momentum resolution is 20% better (scaled from 100% coverage)
ATLAS inner detector barrel
DELPHI all trackers barrel
Realistic tiling with quad module
Coverage 59%
Momentum resolution for a 50 GeV muon
50 GeV muon track with pixel readout

## Slide 14: Conclusions
The ILC can do measurement on the Higgs boson with great precision
With a GridPix readout the ILD TPC performance can be improved
A GridPix based on the Timepix3 chip was reliably operated in a test beam setup and has a resolution only limited by diffusion
A Quad module is built and data from a test beam is now under investigation

## Slide 15: Backup

## Slide 16: Run parameters and selection
Use run with the highest single electron efficiency (close to 1)
Use basic selection cuts to find clean tracks (69% efficiency)
Drift velocity for T2K gas from Magboltz was 78.9 µm/ns (consistent with data)
Run 347 | 
Duration | 60 min.
Triggers | 4 733 381
Vgrid | 350 V
Edrift | 280 V/cm
Rotation | 17 degr. 0 degr.
Threshold | 800 e

## Slide 17: Time walk correction
Time walk error: time of arrival depends on signal amplitude
Time walk can be corrected using Time over Threshold (ToT) as a measure for signal strength
First order correction fitted and applied:
Residual distribution improved
Higher order corrections were also tried but did not yield further improvements
Blum, Particle detection 2008

## Slide 18: Single hit resolution in drift direction
( expected)
Single hit resolution in drift direction
Depends on
from fit
Diffusion from fit
Because of a large time walk error in hits with a low signal strength, an additional ToT cut (>0.60 µs) was imposed
B T

## Slide 19: Mean residuals from test beam
distortions of 60 µm
residuals are below 30 µm
Mean residual above 100 µm
damaged
Not enough hits
Too small number of hits in first and last 8 columns (at edge)
Mean residual above 100 µm for columns 8-16, 240-248
From column 16-240, residuals are below 30 µm
Bottom right is damaged
Top left has distortions of 60 µm
damaged
For applications in a large TPC, systematic deviations must be well under control
Each bin displays mean of residuals from 4 × 4 pixels
1 mm from the edges distortions are below 30 µm

## Slide 20: Distortions at the edges due to variation of guard voltage
In the deformation plot, the attraction of hits to the guard is visible near the edges
The Projection of selected bins 1-3.5 mm from the edge, shows that deformations are below +-50 µm for +- 10 V
This image is a GIF with 2s/frame
Mistuned Guard voltage

## Slide 21: Chip placement requirements in Quad design
To design a precise module with multiple chips, the electric field behavior at edges is studied with simulations
Hit deviations are calculated for different distances between chip edges
For the top curve with 2 pixels (110 μm) distance, deviations < 20 µm are found > 1 mm from the edge
Larger distances must be bridged with a guard structure
The Quad module is designed for these stringent requirements on chip placement:
  chip-chip distance < 100 µm
  guard height precise at 20 µm level
x corresponds to chip edge
chip
chip

## Slide 22: Energy loss resolution by cluster counting
With the pixel granularity ionization clusters can be partially resolved
This gives the possibility to improve the dE/dx resolution by cluster counting
Various algorithms were tried
Weighted mean distance between hits is a good measure of dE/dx
Use (actual/Poisson)-fluctuation as weights
2.7% resolution or 9.2 𝜎 separation between MIP and 2.5 GeV electron

## Slide 23: Outlier rejection

## Slide 24: Scatter at last telescope plane (2017)
Telescope setup was not optimal in 2017: detector was not between planes
Multiple scattering of 0.7 mrad at last telescope plane
Only a reliable intercept with 10 µm error from the telescope
Scatter caused broadening of residual distribution
Telescope
TPC

## Slide 25: Simulation of ILD TPC with pixel readout
To study the performance of a large pixelised TPC, the pixel readout was implemented in the full ILD DD4HEP (Geant4) simulation
Changed the existing TPC pad readout to a pixel readout
Adapted Kalman filter track reconstruction to pixels
Pads
Pixels
22 electrons / hit
200 hits / track
1 electron / hit
10 000 hits / track
See also LCTPC-WP meeting 11-05-17, (The problem with pulls is solved)
50 GeV muon track with pixel readout