## Slide 1: Faster, smaller, more and better
Martin Fransen,
Detector R&D
Developments in the field of pixel detectors

## Slide 2: Faster, smaller, more and better
Developments in the field of pixel detectors
On behalf of:
Martin van Beuzekom
Harry vd Graaf
Navrit Bal
Kevin Heijhoff
Robbert Geertsema
Peter Bosch
Marjolein Heidotting
Hella Snoek
Daniel Hynds
Kazu Akiba
ET:
Bas vd Heijden
Peter Jansweijer
Guido Visser
Henk Peek
Frans Schreuder
Vladimir Gromov
Arseniy Vitkovskiy
Charles Ietswaard
CT:
Vincent v Beveren
Henk Boterenbrood
ASI:
Kiavash Matin
Bram Bouwens

## Slide 3
ASIC pixel matrix to read out:
Segmented ‘vacuum’ (Membrane)
Segmented gas (Gridpix)
Segmented liquid (XENON?)
Segmented solids (Si, GaAs, …)
Applications: Tracking, (X-ray) imaging
Pixel detectors

## Slide 4
Timepix:
Single hits
Time information
Data driven
Medipix:
Hit counting
Frame based
Pixels measure charge
Timepix and medipix chips
Vout
Time
Detection threshold
Signal processing
And digitizing
Data out
Pixel input stage

## Slide 5
Timepix4 by CERN and Nikhef:
Large(st) chip (28 mm x 25 mm)
About 230 kpix, was 65 kpix
0.2 ns time bin, was 1.6 ns
Four side ‘tile-able’, was 3 sided
350 Mhits/cm2/s, was 40 Mhits
….
….
160 Gbps data out
Expected mid 2019
Guess who are going to build the readout system.
New generation: Timepix4
Chip connections
(through the silicon)
Pixel electronics matrix
Area: 512x448 pixels

## Slide 6
Control PC (the ‘chief’)
Master of Timepix4 readout system
Control board (the ‘brain’):
Controls up to 8 TPX4 chips
‘slow’ readout of one TPX4 @ 10 Gb/s
Timing (the ‘conductor’):
Improved white rabbit, <100 ps timing and sync.
DAQ (the ‘brawn’):
Big boys FPGA + workstation. >1TB/min/chip
Timepix4 readout system (Nikhef)

## Slide 7
Spectral X-ray imaging
Spectral CT
‘dark field’ imaging
‘Visible’ photon counting
New photocathode
New charge amplifier
Fast & precise timing
Timepix3 timing performance
3D silicon
what we do with the (old) pixel chips

## Slide 8
Spectral X-ray imaging
5 - 35 keV full spectrum
X-ray tubes emit a broad spectrum
Density gradient?
16-20 keV Band
Nope!

## Slide 9
Joint project proposal:
Institutes:
NKI (Dutch cancer institute)
Nikhef
CWI (our neighbours)
Industry:
ASI (Nikhef spin-off)
XRE (Ghent univ. spin-off)
Spectral CT tumour recognition
FleX-ray
collaboration
Absorption arb. units
Prevent ‘excessive’ surgery!
X-ray absorption of different parts in sample
X-ray photon energy
Real tumour
Conventional X-ray
Conventional+spectral

## Slide 10
Scattered X-rays for imaging
Coded aperture
Grazing incidence optics
‘Improve’ on the pin-hole concept
Combine information of:
X-ray absorption
(Compton) scattering
Fluorescence
More information and/or less dose
ATTRACT project proposal (Nikhef & Cosine)
X-ray ‘dark field’ imaging
Inspired by
astrophysics

## Slide 11
Next generation high luminosity experiments
High spatial and time resolution
Fast(er) ASICs:
Timepix3, VeloPix
Timepix4
Faster sensor:
Thin, Low Gain Avalanche Detector (LGAD), 3D
Membrane
Fast timing
3D sensor
2D sensor

## Slide 12
Using Timepix3 telescope, test:
3D silicon
Thin silicon (50 μm)
Pixel to pixel timing variations
Timepix3 tests @ CERN beam line

## Slide 13
Timepix3 tests @ CERN beam line
14 mm
timing variation across Timepix3
min-max = 3 ns ( >> resolution)
-> correction essential
structure due to routing (crosstalk)
power distribution
55 μm pixel, top view
3D sensor side view
Charge versus position in 3D sensor
much lower charge in pillars
Less charge -> worse timing
Much interest for TPX3 systems:
ASACUSA (anti proton experiment)
Univ of Liverpool (proton therapy)
LHCb
Lepcol
…….

## Slide 14
Laser set-up at Nikhef
Laser to systematically cross check beam data
Submicron positioning in X, Y and Z
Currently limited by laser min. pulse length and spot size
  (considering to upgrade the laser)
Counts

## Slide 15
Questions?