## Slide 1: The gaseous QUAD pixel detector
Yevgen Bilevych, Klaus Desch, Jean-Paul Fransen, Harry van der Graaf, Markus Gruber, Fred Hartjes, Bas van der Heijden, Kevin Heijhof, Charles Ietswaard, Dimitri John, Jochen Kaminski, Peter Kluit, Naomi van der Kolk, Auke Korporaal, Cornelis Ligtenberg, Oscar van Petten, Gerhard Raven, Joop Rövekamp, Lucian Scharenberg, Tobias Schiffer, Sebastian Schmidt and Jan Timmermans
VCI2019 - 15th Vienna Conference on Instrumentation

## Slide 2: Pixel TPC
Single chip Quad Module TPC plane
2017 2018 2019

## Slide 3: GridPix technology
Pixel chip with integrated Grid (Micromegas-like)
InGrid post-processed @ IZM
Grid set at negative voltage (300 – 600 V) to provide gas amplification
Very small pixel size (55 µm)
detecting individual electrons
55 µm
50 µm
dyke
Aluminium grid (1 µm thick)
35 µm wide holes, 55 µm pitch
Supported by SU8 pillars 50 µm high
Grid surrounded by SU8 dyke (150 µm wide solid strip) for mechanical and HV stability

## Slide 4: Pixel chip: TimePix3
256 x 256 pixels
55 x 55 µm pitch
14.1 x 14.1 mm sensitive area
TDC with 610 MHz clock (1.64 ns)
Used in the data driven mode
  Each hit consists of the pixel address and time stamp of arrival time (ToA)
  Time over threshold (ToT) is added to register the signal amplitude
  compensation for time walk
  Trigger (for t0) added to the data stream as an additional time stamp
Power consumption
  ~1 A @ 2 V (2W) depending on hit rate
  good cooling is important
Sensitive area
2+3 mm
14.1 mm

## Slide 5: Single chip test in test beam Bonn (June 2017)
Detector with guard and field shaper
Published paper on 2017 testbeam: https://doi.org/10.1016/j.nima.2018.08.012
@Bonn
--------- Mimosa telescope ---------
ELSA: 2.5 GeV electrons
Tracks referenced by Mimosa telescope
Gas: Ar/CF4/iC4H10 95/3/2 (T2K)
Electrons: ~100 e/cm
Ed = 280 V/cm, Vgrid = -350 V

## Slide 6: TimePix3 time walk correction
Time walk error: time of arrival depends on signal amplitude
Residual distribution improved
Higher order corrections did not yield further improvements
(Blum, Particle detection 2008)
Correction using Time over Threshold (ToT) as a measure of signal strength

## Slide 7: Single hit resolution in transverse direction
( expected)
B T
Single hit resolution in pixel plane:
Depends on:
pixel size
Diffusion from fit
Note that:
A hit resolution of 250 µm is 25 µm for a 100-hit track ( 1 cm track length)
At 4 T ,

## Slide 8: Single hit resolution in longitudinal direction
( expected)
Single hit resolution in drift direction
Depends on
from fit
Diffusion from fit
The additional ToT cut (>0.60 µs) was applied to avoid large time walk errors
B T
Single hit resolution in longitudinal direction

## Slide 9: Pixel dE/dx performance
dE/dx resolution with truncated mean
  From the single chip tracks; 1 m long tracks are made;
  nr of electrons counted in slices of 20 pixel and reject 10% highest slices
  Distances along track are scaled by 1/0.7 to get an estimation for the dE/dx of a MIP
  Resolution is 4.1% for a 2.5 GeV electron and 4.9% for a MIP
Separation S = (Ne − NMIP)/σe
8σ MIP-e separation for a 1 meter track
A pixel readout can in principle within the resolution (diffusion) separate primary from secondary clusters. dE/dx can be measured by cluster counting and performance separation enhanced.

## Slide 10: Deformations in pixel plane (XY) and drift direction (Z)
XY
Z
The RMS of the mean residuals is 7 μm in the pixel plane and 21 μm (0.3 ns) in the drift direction in the selected region
How can we make an even better detector?
  Improve the quality (homogenity) of the InGrid; redesign the dike and edges
  Go to a large areas keeping the field distortions (at edges) minimal -> QUAD

## Slide 11: QUAD design and realization
Guard
TPX3
TPX3
TPX3
TPX3
COld
CArrier
Four-TimePix3 chips
All services (signal IO, LV power) are located under the detection surface
The area for connections was squeezed to the minimum
Very high precision 10 μm mounting of the chips and guard
QUAD has an sensitive area of 68.9%
DAQ by SPIDR
39.6 x 28.38 mm
series of QUADs

## Slide 12: QUAD test beam in Bonn (October 2018)
ELSA: 2.5 GeV electrons
Tracks referenced by Mimosa telescope
QUAD sandwiched between Mimosa planes
  Largely improved track definition
Gas: Ar/CF4/iC4H10 95/3/2 (T2K)
Ed = 280 V/cm, Vgrid = -300 V
Typical beam height above the chip: ~1 cm
Field cage
QUAD
@Bonn
Preliminary results will be presented here
40 mm

## Slide 13: QUAD time walk results
Time walk correction works well
Applied for all analysis results
Preliminary
Preliminary

## Slide 14: QUAD single hit resolution
DT = 419 μm/√cm
DL = 259 μm/√cm
Transverse
Longitudinal
Preliminary
Preliminary

## Slide 15: QUAD edge deformations
Small deformations due to
  Dead zone between chips
  Grounded region between chips
Are corrected by:
  fitted correction function
  adding proper guard wire electrode
Preliminary
Grounded region

## Slide 16: QUAD deformations in transverse plane (XY)
After applying fitted edge corrections
RMS of the mean residuals are 26 μm over the whole QUAD
Preliminary
Preliminary
XY

## Slide 17: Next: QUAD as a building block
Guard wires not yet installed
Cooling channels
8-QUAD module

## Slide 18: Conclusions
Since 2017 three TimePix3 wafers were successfully equipped with an InGrid
A single chip GridPix detector from this production was reliably operated in a test beam in 2017
  Single electron detection => the resolution is primarily limited by diffusion
  Systematic uncertainties are low: < 10 µm in the pixel plane
  dE/dx resolution for a 1 m track is 4.1%
  Preliminary results from a recent 2018 QUAD test beam were presented
  Data quality and resolutions are similar to the single chip test beam results
Small edge deformations at the boundary between two chips are observed
  We will add guard wires to the module
A production of 14 QUADs is finished
  QUADs are installed in an 8-QUAD module