## Slide 1: GridPix developments
Cornelis Ligtenberg, H. van der Graaf, K. Heijhoff, P.M. Kluit, N. van der Kolk, G. Raven, J. Timmermans
Y. Bilevych, K. Desch, M. Gruber, F. Hartjes, J. Kaminski, T. Schiffer
Nikhef Jamboree 16 – 17 December 2019

## Slide 2: The international linear collider
20 km first stage at 250 GeV
TPC

## Slide 3: TPC with GridPix readout
Track
-Edrift
e-
e-
e-
e-
e-
e-
e-
e-
e-
Ionisation in gas
Amplification
and detection at readout plane
e-
e-
e-
e-
e-
e-
e-
e-
e-
55 µm pixels
Conventional 6 mm sized pads
GridPix
Readout surface 10 m3
Chip surface 2 cm3
Challenge: Cover large area with small chips

## Slide 4: Quad module development
Coverage of end plate with quad modules
58% coverage

## Slide 5: Quad results and outlook
8 Quad (32 chip module) to be tested soon
Hit resolution per ionisation electron

## Slide 6: Backup
Simulated e+e- -> Zh -> e+e-h

## Slide 7: GridPix technology
GridPix is a type of micro-pattern gaseous TPC readout
The GridPix based on a Timepix3
  55 µm × 55 µm pixels
  Digital simultaneous registration of Time of Arrival (1.56 ns) and Time over Threshold
  An aligned Aluminium amplification grid is added by photolithographic postprocessing techniques
Single ionization electrons are detected with high efficiency
  The maximum possible information from a track is acquired
  dE/dx by cluster counting
50 µm
35 µm
55 µm
1 µm

## Slide 8: Simulation of ILD TPC with pixel readout
To study the performance of a large pixelised TPC, the pixel readout was implemented in the full ILD DD4HEP (Geant4) simulation
Changed the existing TPC pad readout to a pixel readout
Adapted Kalman filter track reconstruction to pixels
Pads
Pixels
22 electrons / hit
200 hits / track
1 electron / hit
10 000 hits / track
Picture by Cornell
6 mm
55 µm
50 GeV muon track with pixel readout
Continuous
3D tracking

## Slide 9: Performance of a GridPix TPC at ILC
Momentum resolution of the TPC for a 50 GeV muon
From full simulation, momentum resolution can be determined
Momentum resolution is 15% better (with realistic coverage and delta’s)
Realistic tiling with quad module
58% coverage

## Slide 10: Some physics goals of the ILC
What is the origin of EWSB?
How can the Higgs bosons be so light?
Are there more Higgs bosons?
What is dark matter made of?
LHC (3 ab-1)
LHC + ILC 250 GeV ( 2 ab-1)
LHC + ILC 250 GeV + ILC 500 GeV (4 ab-1)
https://arxiv.org/pdf/1710.07621.pdf

## Slide 11: Single chip results (2017)
A GridPix based on the Timepix3 chip was reliably operated in a test beam setup with 2.5 GeV electrons at ELSA (Bonn)
T2K gas and Edrift = 280 V/cm, Vgrid = -350 V
The resolution is primarily limited by diffusion
Systematic uncertainties are low: < 10 µm in plane
Energy loss resolution (dE/dx) by electron counting is 4.1 % per meter
Published paper on this testbeam doi:10.1016/j.nima.2018.08.012
Electron
MIP
Hit resolution
B T

## Slide 12: The quad module
A four chip module sized 39.6 mm 28.38 mm
The quad module has all services under the active area
  Can be tiled to cover arbitrarily large areas.
Area for connections IO was minimized
  Maximises active area ( 68.9% )
To maintain a homogenous electric field wire bonds are covered by a central guard
High precision < 20 μm mounting of the chips and guard
Cooling channels

## Slide 13: Test beam measurements (2018)
2.5 GeV electrons at the ELSA accelerator in Bonn, Germany
T2K gas with Edrift = 280 V/cm, Vgrid = -350 V
Events are triggered by a scintillating plane
6 plane mimosa telescope with 18.4 μm × 18.4 μm sized pixels
180 o

## Slide 14: Time walk correction
Time walk error: time of arrival depends on signal amplitude
Time walk can be corrected using Time over Threshold (ToT) as a measure for signal strength
First order correction fitted and applied:
Distribution of residuals becomese more Gaussian after the time walk correction

## Slide 15: Hit resolution in the drift direction
Single hit resolution in drift direction
Depends on
from fit
Diffusion from fit
Because of a large time walk error in hits with a low signal strength, an additional ToT cut ( > 0.60 µs) was imposed

## Slide 16: Hit resolution in the pixel (precision) plane
Single hit resolution in pixel (precision) plane:
Depends on:
pixel size 55 µm
Diffusion from fit
B T
Scattering on guard
Note that:
A hit resolution of 250 µm is 25 µm for a 100-hit track ( 1 cm track length)
At 4 T , expected
At 2 T , expected

## Slide 17: Deformations in the pixel (precision) plane
Investigation of systematic deviations over the pixel plane
Each bin displays mean of residuals from 4 × 4 pixels
Primarily due to electric field distortions
Correction of deformations with 4 fitted Cauchy functions per chip:
Without correction

## Slide 18: Deformations in the pixel (precision) plane
Investigation of systematic deviations over the pixel plane
Primarily due to electric field distortions
Each bin displays mean of residuals from 4 × 4 pixels
Correction of deformations with 4 fitted Cauchy functions per chip:
With correction

## Slide 19: Deformations in pixel plane and drift direction
Each bin displays mean of residuals from 4 × 4 pixels
The RMS in the center of the chip is 9 µm (pixel plane after correction) and 14 µm (drift direction), which indicates small systematic errors
Corrected x deformations
Pixel (precision) plane
z deformations
Drift direction

## Slide 20: 8 quad module development
8 quad test box with (32 chips)
Simultaneous read out through one SPIDR board using a data concentrator
Field wires added to improve electric field, and reduce deformations
New field wires

## Slide 21: 8 quad module development
Laser test indicate a reduction in electric field deformations with field wires
Early 2020 test beam planned at DESY with 1 T magnetic field
Preliminary
Uncorrected residuals from quad test beam
Uncorrected residuals from laser test with field wires