## Slide 1: Pixel TPC for CEPC
LCWS 2019 Sendai:
For one of the CEPC experiments there is interest in a pixel TPC
  Discussed with Huirong Qi https://agenda.linearcollider.org/event/8217/contributions/44627/
CEPC workshop Beijing:
  Kees Ligtenberg https://indico.ihep.ac.cn/event/9960
In this LCTPC workshop
  Huirong Qi presented the CEPC plans
Picture IHEP

## Slide 2: CEPC Pixel TPC: introduction
At a circular collider CEPC there is place for different experiments, one of them could use a TPC as the main tracker
Why is a pixel TPC a serious and realistic option?
    For Higgs and top running no problem for all TPC read out technologies
    For W running probably no issue either
    Running at the Z with high luminosities and high rates is however problematic for current micromegas and pad technologies. Tracks will overlap in the read-out plane and the occupancy at low radii will become too high
Running at the Z with a pixel TPC?
  Large potential in terms of rate capabilities
  Pattern recognition profits from high granularity of 55x55 μm2 pixels
Will go through different aspects of CEPC Z running
  Rates and occupancies
  Distortions in a pixel TPC from primaries and Ion Back Flow
    Could one apply a gating device to reduce IBF?

## Slide 3: CEPC Pixel TPC: Z running
The conditions for CEPC running
  High(est) luminosity CEPC L = 32-50 (17-32) 1034 cm-2s-1 at 2 T from CDR.
    CEPC Ring length 100 km with 12 000 bunches and a hadronic Z rate of 10-15 (5-10) k Hz (cross section 32 nb). Beam structure rather continuous 25 ns spacing.
    Note that this Luminosity gives about 60-120 (30-60) G Zs per running year
  Time between Z interactions 120-60 (200-100) μs
  TPC drift takes 30 μs
  So events are separated in the TPC
High rate capabilities of the GridPix pixel chip TPX3
  Bonn test beam was 5 kHz electrons for a quad
  Link speed 80 Mbps per chip (256x256x 55 x 55 μm2)
  Test beam 2018 1.3M hits/s per chip could be read out
  In 2019 the link speed doubled to 2.6M hits/s per 1.42x1.42 cm2.

## Slide 4: CEPC Pixel TPC rates
  Rates primary electrons in a Pixel TPC
  Using a simple simulation program the primary Z hit rate in the pixel TPC is calculated as a function of the radius.
  The rate amount to 300 k hits/s/chip at a radius of 40 cm.
  This is a rate the current quad and read out can easily handle.
  The test beam showed we can handle up to 2.6M hits/s per chip (1.42x1.42 cm2). So about a factor 10 higher than what is needed.
  Occupancy rate 40/s (256*256 pixels)
    With 0.1 ms read out< 0.004 (10kHz)

## Slide 5: CEPC Pixel TPC: Z running
Summary of Z rates @ L = 32 1034 cm-2s-1 and occupancies
  Data is produced at a large rate of 300 k hits/s/chip (at R=40 cm)
  In the test beam it has been demonstrated that the TPX3 can handle a rate that is a factor 10 higher
  Occupancies are less than 1% at low radii
  One needs to design a DAQ system to collect all data
Pattern recognition will be no problem
  The occupancies in the pixel plane are low. The time between the Z interactions is large 120 μs. The time will be measured by each pixel. The resolution is dominated by longitudinal diffusion. It amounts to less than about 20 nsec. Different Z events can be easily separated in time.

## Slide 6: CEPC Pixel TPC backgrounds and distortions
  Important to estimate the charge in the TPC as it can cause distortions
    Physics events like Zs
    Other backgrounds γγ background and incoherent pairs from beam-beam interactions that produce hits
      At ILC beam-beam effects are dominant over the physics interactions.
      However TLEP and FCCee studies show that e.g. γγ background are very small at the Z. Also the incoherent pair production (backup slides) is several orders smaller than at the ILC.
      As Adrian Vogel (DESY-thesis-08-036) in his thesis showed the detector -machine design is important to reduce the number of back scattered photons. See plot below.

## Slide 7: CEPC Pixel TPC: distortions from Zs
  Rate estimates for primary electrons and charge and distortions from primary ions due to Zs (back of the envelop)
    Assume that the ions stay 0-300 ms before reaching the mid plane of the TPC. With a rate of 10-15 kHz one will accumulate 3000 - 4500 Zs; This gives 30 tracks producing 104 primary electrons and ions. TPC volume: Inner radius 40 cm; outer 180 cm; 400 cm length; so volume 3.8 107 cm3. Charge density = 9-13 108/3.8 107 cm3 = 23-34 e/cm3. This is smaller than the charge at the ILC for 3000 bunches from beam-beam background (slide 9).
    Here the studies were performed assuming no Ion Back Flow. Ions are produced in the gas amplification stage. A fraction of them will flow back into the TPC drift volume. For a Gridpix detector this is O(0.1%). A precise measurement will be performed in 2020.

## Slide 8: CEPC Pixel TPC charge and distortions
  Charge from primary ions due to Zs (back of the envelop)
  At ILC this accumulated charge in the TPC bkg leads to distortions of max 5 μm. See next slide for details. Here no ion back flow IBF=0 is used.
  The CEPC study presented by Huirong Qi (backup) gives a larger number of up to 80 μm with IBF=5 and a lower luminosity.
  The distortions will depend on the IBF number of the device. With IBF = 1.5 (gas gain 1500 and IBF fraction 0.1%), the distortions are maximally 13 μm.

## Slide 9: ILC beam-beam primary ions in TPC
So deformations for a primary charge distribution (x 30) are less than 5 μm
Studies from Keisuke Fuji https://agenda.linearcollider.org/event/5504/contributions/24543/attachments/20144/31818/PositiveIonEffects-kf.pdf)

## Slide 10: CEPC Pixel TPC gating
  Possible CEPC triggered gating scheme
    Time between Z collisions is 120 μs. So one can think of gating
    Make a GEM gating device a la ILD (see picture) but now at 1-5 mm above the grid
  Gating in a triggered mode;
    if a hadronic Z interaction in TPC start gating “stop the ions”.
  Gate length of e.g. 30-60 μs would stop the ions in Z triggered mode
    the price is dead time, reduced efficiency
    One will start “leveling” if gate close time = 20 μs -> efficiency 66-85%
  This might work and will reduce IBF and distortions
NB: ILC gating can exploit bunch structure: Gate opens 50 μs before the first bunch and closes 50 μs after last bunch. Close time between bunches 200 ms. Device 1 cm above grid.
Yumi Aoki @ LCWS2019

## Slide 11: CEPC Pixel TPC NO gating
  Depending on the IBF, the distortions could also be measured and corrected for
  Due to the large Z data set it will be possible to correct for the distortions in a timely manner. Suppose one has distortions that correspond to IBF = 15 (applying a safety factor 10). The maximum deviation will be 130 μm at small radii. It is realistic to assume that one can measure this number with a precision of 13 μm (factor 10) using the vertex detector.
  This means that one can reach the precision requirements of the ILD TPC: the systematics in the bending plane will be less than 10-20 μm
  NB for the W and Higgs runs it is important to install and use a gating device

## Slide 12: CEPC Pixel TPC Summary
  A pixel TPC can handle the large data rates during CEPC Z running. The pixel occupancies are low and the pattern recognition will have no problem to separate events and find the tracks.
  Estimates have been presented for deformations coming from charges from primary Z events and Ion Back Flow. The maximum at small radius is 13-130 μm (safety factor 10).
    The IBF can be reduced by applying a triggered gating device
    With and without gating, the deformations can be corrected for and controlled at a level of the tracking requirements of the ILD TPC; systematics in bending plane: less than 10-20 μm
    For the W and Higgs runs it is important to apply a gating device
A pixel TPC is a realistic option at the CEPC and provides:
  High precision tracking in the transverse and longitudinal planes
  dE/dx by electron and cluster counting
  Excellent two track resolution
  Digital readout that can deal with high rates

## Slide 13: CEPC Pixel TPC
Huirong Qi
backup

## Slide 14: CEPC Pixel TPC
CEPC Oxford
https://indico.cern.ch/event/783429/contributions/3379893/attachments/1830789/2998159/CEPC_Backgrounds_Oxford_Zhu.pdf
backup

## Slide 15
backup

## Slide 16: Pixel TPC for TLEP/FCCee
  Distortions from primary ion from Zs have been performed by Schwemling for a TPC at TLEP/FCCee https://indico.cern.ch/event/467955/
  Note here the Z rate is 16 kHz so
  similar to CEPC at 50 1034 cm-2s-1.
  Studies are more detailed – use Pythia plus distortion program from Keisuke Fuji- than a back of envelop calculation.
  NB IBF is not zero but put to 1.
  The number of ions/cm is not 100 but only 40. So a bit low.
backup

## Slide 17: CEPC Pixel TPC
here L = 17 1034 cm-2s-1
Huirong Qi
This is based on
physics events
No beam-beam
Deviations due to
primary ions should
be factor 5 smaller
In my calculations
L = 32-50 1034 cm-2s-1 at 2 T.
backup