## Slide 1: Pixel TPC research plans
    GridPix improvement of resistivity TPX3 layer SiN
    Ion Back Flow measurement Quad
    Negative Ion Pixel TPC tests
    TimePix4 potential
    Test beams 8-Quad module
Yevgen Bilevych, Klaus Desch, Sander van Doesburg, Jean-Paul Fransen, Harry van der Graaf, Markus Gruber, Fred Hartjes, Bas van der Heijden, Kevin Heijhoff, Charles Ietswaard, Dimitri John, Jochen Kaminski, Peter Kluit, Naomi van der Kolk, Auke Korporaal, Cornelis Ligtenberg, Oscar van Petten, Gerhard Raven, Joop Rövekamp, Tobias Schiffer and Jan Timmermans

## Slide 2: GridPix improvement of resistivity TPX3 layer SiN
  In the post processing a resistive layer is put on the TP3 chip
  This protects the device from sparks
  In the quad beam tests it was found out that the SiN layer charges up at very high rates (10 kHz)
  Yevgen is investigating how to reduce significantly the resistivity of the SiN layer; this will reduce the charge up
  Different trial samples will be made in 2020
  Production of TPX3 wafers with InGrids @ IZM Berlin
  Bonn will have a new Silicon Lab Summer 2020

## Slide 3: Ion Back Flow measurement Quad
  Ion Back Flow are the ions created in the avalanche process that flow back in the TPC volume
  For the use of a pixel TPC at the CEPC it is important to know and reduce the Ion Back Flow (IBF)
  It is in general known that a Grid Pix has a low IBF probability O(0.1%)
  It is possible to measure the IBF using the Quad. One can extrapolate this number to the current operation point at a gain of 2000. This will be done beginning 2020

## Slide 4: Negative Ion pixel TPC
  There is another application for a pixel TPC using negative ions
    The idea for a NITPC was presented by Martoff et al. in NIMA A 440 (2000) 355
    Use a gas CS2 (SF6) here negative ions are formed. They drift slowly to the read-out plane. These gasses have a very small diffusion coefficient: high resolution - interesting for pixels
    NITPC with GEM read-out experiment for dark matter searches Drift IIb
  Fred started to look whether one could use Ar-CS2 98.8/1.2 gas mixture and run it at atmospheric pressure.
    Indeed signals were observed with a 90Sr source for a V grid -370 V. Similar signal as the standard T2K gas.
  Will proceed in 2020 to test a single chip
    measure the diffusion “very thin” laser tracks …

## Slide 5: TimePix 4 potential
  Advantages of the Timepix4 (see also Fred his talk)
    Larger area than TPX3 about factor 3.5
    Better connectivity more space
    Lower power consumption (0.55 W/cm2) than TPX3
    Possible use of Through Silicon Vias (TSVs)
      Current Quad coverage is about 69% could reach > 90%
  Start with TPX4 when available; surface is equivalent to Quad
    Can use simpler PCB (significant cost reduction)
    Don’t need multiplexer to combine TPXs
  Several years effort: need to get some steps approved in running of 2020
    Will organize a brainstorm meeting with Bonn, Nikhef R&D
    Support will be easier with ILC approved or CEPC funding

## Slide 6: Test beams 8-Quad module
  It is important to test the 8-Quad module in a test beam
  The multiplexer that combines the signals from different quads needs to be operated and commissioned
    Expect this to happen beginning 2020
  Probably we will perform a pre-test for the test beam, either at DESY running parasitically, or in Bonn before the Summer
  The ultimate test beam in DESY is now scheduled for August 2020
    We will take data with a silicon telescope that will allow us to measure the deformations for a module (see Critical Items … https://agenda.linearcollider.org/event/8362/contributions/45065/)