## Slide 1: A pixel TPC readout for a detector at a future e+e- collider
Cornelis Ligtenberg, H. van der Graaf, F. Hartjes, K. Heijhoff, P.M. Kluit, N. van der Kolk, G. Raven, J. Timmermans
Wednesday 22 January 2020
Physics@Veldhoven
Y. Bilevych, K. Desch, M. Gruber, J. Kaminski, T. Schiffer

## Slide 2: What are the research goals?
Picture by MissMJ, Wikipedia
The standard model of particle physics
Higgs boson is the only scalar (spin 0 particle)
Some questions:
What is the origin of the Higgs mechanism?
How can the Higgs bosons be so light?
Are there more Higgs bosons?
We need Higgs precision measurements

## Slide 3: Why do we need a new collider?
Proton picture by DESY
The LHC collides the composite proton
Collision energy is unknown
Large backgrounds (noise)
Collisions of the fundamental electron
Energy is precisely known
Ideal for precision measurements

## Slide 4: The international linear collider
20 km first stage as a Higgs factory at 250 GeV
Pictures from ILC CDR

## Slide 5: Detection of Higgs bosons
Higgs production process:
Higgs bosons and bosons are detected through their decay products
Detectors are organised as shells around the interaction point
The time projection chamber measures the trajectory of charged particles
e-
e+
Time projection chamber
h
Z

## Slide 6: The time projection chamber
Track
-Edrift
e-
e-
e-
e-
e-
e-
e-
e-
e-
Ionisation in gas
Amplification
and detection at readout plane
e-
e-
e-
e-
e-
e-
e-
e-
e-
55 µm pixels
Conventional mm sized pads:
detection of distributions
GridPix: finer granualrity and sensitive to single ionisation electrons

## Slide 7: Quad module development
A quad module was developed

## Slide 8: Experimental test setup
The quad module was tested with an electron beam at the ELSA accelerator in Bonn
October 2018

## Slide 9: Hit resolution
Hit resolution depends on diffusion and resolution at zero drift
The hit resolution is 250 µm per ionization electron
A track has about 100 hits / cm
B T
Scattering on guard
Drift distance to readout chip
Resolution

## Slide 10: Systematic error in over the pixel plane
Investigation of systematic deviations over the pixel plane
The color represents the distortions
The primary cause is electric field distortions
Correction of deformations with fitted Cauchy functions
Without correction

## Slide 11: Systematic error in over the pixel plane
Investigation of systematic deviations over the pixel plane
The color represents the distortions
The primary cause is electric field distortions
Correction of deformations with fitted Cauchy functions
With correction

## Slide 12: Extrapolation to a large detector
50 GeV muon track with pixel readout
Simulation
Expected momentum resolution
20% improvement

## Slide 13: Conclusions
A quad module with new pixel TPC readout technology has been designed and built
Simulations show a 20% improvement in momentum resolution of a pixel TPC readout over a conventional pad readout
A pixel readout can help study Higgs bosons with great precision
A larger 32 chip prototype is already advanced and will be tested soon

## Slide 14: Backup
Simulated e+e- -> Zh -> µ+µ-h (250 GeV)

## Slide 15: Status of ILC
By Keisuke Fuji (KEK)
3 December

## Slide 16: Some physics goals of the ILC
What is the origin of EWSB?
How can the Higgs bosons be so light?
Are there more Higgs bosons?
What is dark matter made of?
LHC (3 ab-1)
LHC + ILC 250 GeV ( 2 ab-1)
LHC + ILC 250 GeV + ILC 500 GeV (4 ab-1)
https://arxiv.org/pdf/1710.07621.pdf

## Slide 17: Quad results and outlook
October 2018
Preliminary
Uncorrected residuals from quad test beam
Uncorrected residuals from laser test with field wires
New field wires
8 Quad (32 chip module) to be tested with beam soon

## Slide 18: Quad module development
Coverage of end plate with quad modules
58% coverage

## Slide 19: GridPix technology
GridPix is a type of micro-pattern gaseous TPC readout
The GridPix based on a Timepix3
  55 µm × 55 µm pixels
  Digital simultaneous registration of Time of Arrival (1.56 ns) and Time over Threshold
  An aligned Aluminium amplification grid is added by photolithographic postprocessing techniques
Single ionization electrons are detected with high efficiency
  The maximum possible information from a track is acquired
  dE/dx by cluster counting
50 µm
35 µm
55 µm
1 µm

## Slide 20: Simulation of ILD TPC with pixel readout
To study the performance of a large pixelised TPC, the pixel readout was implemented in the full ILD DD4HEP (Geant4) simulation
Changed the existing TPC pad readout to a pixel readout
Adapted Kalman filter track reconstruction to pixels
Pads
Pixels
22 electrons / hit
200 hits / track
1 electron / hit
10 000 hits / track
Picture by Cornell
6 mm
55 µm
50 GeV muon track with pixel readout
Continuous
3D tracking

## Slide 21: Performance of a GridPix TPC at ILC
Momentum resolution of the TPC for a 50 GeV muon
From full simulation, momentum resolution can be determined
Momentum resolution is 15% better (with realistic coverage and delta’s)
Realistic tiling with quad module
58% coverage

## Slide 22: Systematic error in over the pixel plane
Investigation of systematic deviations over the pixel plane
Primarily due to electric field distortions
Each bin displays mean of residuals from 4 × 4 pixels
Correction of deformations with 4 fitted Cauchy functions per chip:
Without correction

## Slide 23: Systematic error in over the pixel plane
Investigation of systematic deviations over the pixel plane
Primarily due to electric field distortions
Each bin displays mean of residuals from 4 × 4 pixels
Correction of deformations with 4 fitted Cauchy functions per chip:
With correction

## Slide 24: A TPC at the CEPC?
The CEPC CDR plans for a detector with a TPC
A GridPix TPC can deal with the high beam rates at the CEPC
The CEPC with L = 32 1034 cm-2 s-1 will produce Z bosons at 15 kHz
Link speed of Timepix3 (in Quad) is 80 Mbps: 2.6 MHits/s per 1.41 × 1.41 cm2
Excellent time resolution: time stamping of tracks < 1.2 ns
Power consumption 2W/chip depending on hit rate
Rough estimations at L = 32⋅1034 cm-2 s-1 indicate primary ionisation causes accumulated charge at an ILC250 level distortions < 5 µm
Ion backflow (IBF) can give a lot of additional charge, so IBF must be controlled
Picture IHEP

## Slide 25: A negative ion TPC?
A negative Ion TPC has potentially a smaller diffusion than a TPC based on drifting electrons
Currently NITPCs are used in dark matter searches
Pixel read out – due to the fine granularity - allows to exploit high resolution regime
CS2- and SF6- are commonly used
What happens is that the track creates ionization; electron plus a positive ion; the electron is then captured by the CS2 and SF6 and forms a negative ion. This negative ion then drifts to the cathode.
Near the readout plane the electric field is so strong that the electron is stripped off and starts a “standard” avalanche. The critical field density where this happens (SF6 ) is E/n = 100 x 10-17 V cm2.

## Slide 26: Single chip results (2017)
A GridPix based on the Timepix3 chip was reliably operated in a test beam setup with 2.5 GeV electrons at ELSA (Bonn)
T2K gas and Edrift = 280 V/cm, Vgrid = -350 V
The resolution is primarily limited by diffusion
Systematic uncertainties are low: < 10 µm in plane
Energy loss resolution (dE/dx) by electron counting is 4.1 % per meter
Published paper on this testbeam doi:10.1016/j.nima.2018.08.012
Electron
MIP
Hit resolution
B T

## Slide 27: The quad module
A four chip module sized 39.6 mm 28.38 mm
The quad module has all services under the active area
  Can be tiled to cover arbitrarily large areas.
Area for connections IO was minimized
  Maximises active area ( 68.9% )
To maintain a homogenous electric field wire bonds are covered by a central guard
High precision < 20 μm mounting of the chips and guard
Cooling channels

## Slide 28: Test beam measurements (2018)
2.5 GeV electrons at the ELSA accelerator in Bonn, Germany
T2K gas with Edrift = 280 V/cm, Vgrid = -350 V
Events are triggered by a scintillating plane
6 plane mimosa telescope with 18.4 μm × 18.4 μm sized pixels
180 o

## Slide 29: Time walk correction
Time walk error: time of arrival depends on signal amplitude
Time walk can be corrected using Time over Threshold (ToT) as a measure for signal strength
First order correction fitted and applied:
Distribution of residuals becomese more Gaussian after the time walk correction

## Slide 30: Hit resolution in the drift direction
Single hit resolution in drift direction
Depends on
from fit
Diffusion from fit
Because of a large time walk error in hits with a low signal strength, an additional ToT cut ( > 0.60 µs) was imposed

## Slide 31: Hit resolution in the pixel (precision) plane
Single hit resolution in pixel (precision) plane:
Depends on:
pixel size 55 µm
Diffusion from fit
B T
Scattering on guard
Note that:
A hit resolution of 250 µm is 25 µm for a 100-hit track ( 1 cm track length)
At 4 T , expected
At 2 T , expected

## Slide 32: Deformations in pixel plane and drift direction
Each bin displays mean of residuals from 4 × 4 pixels
The RMS in the center of the chip is 9 µm (pixel plane after correction) and 14 µm (drift direction), which indicates small systematic errors
Corrected x deformations
Pixel (precision) plane
z deformations
Drift direction

## Slide 33: 8 quad module development
8 quad test box with (32 chips)
Simultaneous read out through one SPIDR board using a data concentrator
Field wires added to improve electric field, and reduce deformations
New field wires

## Slide 34: 8 quad module development
Laser test indicate a reduction in electric field deformations with field wires
Early 2020 test beam planned at DESY with 1 T magnetic field
Preliminary
Uncorrected residuals from quad test beam
RMS: 32 µm
Uncorrected residuals from laser test with field wires
RMS: 17 µm

## Slide 35: Detection of Higgs bosons
Higgs production process:
Higgs bosons and bosons are detected through their decay products
Detectors are organised as shells around the interaction point
The time projection chamber measures the trajectory of charged particles
e-
e+
Z
h
Time projection chamber