## Slide 1: Pixel TPC Ion feedback
https://indico.cern.ch/event/843086/attachments/1958227/3253556/L3_signals_in_particle_detectors_riegler_2019.pdf
(Modified) Ramo Shockley theory

## Slide 2: Modeling the Ion feed back
Calculate the induced current on the cathode plate using the technique described by Riegler
  Make electron and ion sheets at different z distances
Cathode
Ion sheet
Electron sheet
Anode
Height (z) 4 cm
Witdh (x) 8
(y) 17 cm

## Slide 3: Induced Charge on cathode
From the potential

## Slide 4: Induced Charge on cathode
Generated sheet of electrons and ions at z values: primaries
z 10 mm
20 mm
30 mm
Short times: electrons+ions
long times: ions

## Slide 5: Ion Components
There are four processes for ions:
1) Charge induction from the primary ions on the cathode qprimary
2) Charge induction from the avalanche ions on the grid qprimary x gas gain
3) Charge induction from the grid on the cathode
4) Charge induction from ions that pass through the grid; this is the ion feedback we want to measure qprimary x gas gain x efficiency pass grid
The time structure of processes
1
4
2+3
time
charge
negative
negative
-
+
Charge is induced on the grid and then compensated

## Slide 6: Ion backflow measurements
From the thesis of Max Chefdeville; chapter 7 Figure 7.5
Gap = distance grid above pixels For us 50 μm so look at 46 gap
Field ratio = E gap / E drift For us 250 V/cm and 250 over 50 μm = 200
Reading off the plot gives 2-3%
So to reduce the IBF one should use a
lower drift field; but then the total drift
time gets longer. This means that also
more ions are accumulated.
One could think of using a gas with
faster drifting ions.