## Slide 1: HV tuning update
Bouke Jung (bjung@nikhef.nl), Alexandre Creusot (creusot@apc.in2p3.fr), Maarten de Jong (mjg@nikhef.nl)
Nikhef KM3NeT group meeting
2020/03/13

## Slide 2
Recap
Move to HV-tuning procedure based on gain-estimates
  Motivated by theory (see doxygen):
Implementation through fit or interpolation of linearized data
  Extract high-voltage settings from database
  Extract gain-estimates from JFitToT output
Outliers in gain-estimates need to be inspected
Database integration via Json

## Slide 3
HV fit
Nominal Gain (G = 1.0)
HV-fitting routine is being implemented in JFitHV (updates in Jpp git branch fitToT_full_spectrum)
  DB-interfacing has been implemented
  Automatically retrieves (HV,G)-data for all PMTs in user-specified list of data-files
Initial results are promising
  Clear linear behavior on log-log scale for most PMTs
A couple of issues
Minimum fit-range (G = 0.3)

## Slide 4
HV fit
Nominal Gain (G = 0.9)
HV-fitting routine is being implemented in JFitHV (updates in Jpp git branch fitToT_full_spectrum)
  DB-interfacing has been implemented
  Automatically retrieves (HV,G)-data for all PMTs in user-specified list of data-files
Initial results are promising
  Clear linear behavior on log-log scale for most PMTs
A couple of issues
  Deviation from linear behavior at high or low |HV| for some PMTs
  Fit-range bounds for gain-estimate in JFitToT
Maximum fit-range (G = 2.0)
Minimum fit-range (G = 0.3)

## Slide 5
ToT-fits for increasing HV
N.B: These are animated gif files

## Slide 6
Solutions
Making the ToT-fit work for all possible HV-settings is asking too much…
  For the specific purpose of HV-tuning, set fit-range to region surrounding ToT-distribution peak
The datapoints directly surrounding the optimal gain (= 1.0) tell the most about the optimal high voltage setting
  Switch to linear interpolation/extrapolation

## Slide 7
Remaining anomalous ToT-fits
Extremely high HV
Thresholdband and PunderAmplified too low to account for large peak at 5ns
Large secondary contribution at 10ns
Normalization does not account for large relative fraction of 5ns- and 10ns-peak counts
  Causes fit to unduly scale down model contribution by increasing its spread

## Slide 8
Remaining anomalous ToT-fits
Extremely low HV
Thresholdband and PunderAmplified too low to account for large peak at 5ns
Model contribution nearly indistinguishable from 10ns-peak contribution

## Slide 9
Remaining anomalous ToT-fits
Discovered one PMT (808483678.5) with anomaly in first and second bin
Output from JCalibrateToT
  Some artefact in the triggering?

## Slide 10
Planning
Set up a bash script to automatically extract the gain-estimates and find the optimal HVs using a set of user-specified raw data files
  Prognosis: √
Implement DB-integration (via JSon)
  Prognosis: today/tomorrow
Document remaining anomalous ToT-fits on ELOG and git
  Prognosis: today
Analyze results with recent (L0-)data using the provided bash script
  Prognosis: weekend/start of next week
Adjust TIME_OVER_THRESHOLD_NS to optimal gain-setting
  Prognosis: tomorrow/weekend (non-critical)