## Slide 1: Pixel TPC
Single chip Quad Module TPC plane
2017 2018 2019

## Slide 2: Study of events with many hits
We will use run 1811 Vgrid = 350 V and Vdrift = 350 V/cm to study events with many hits.
Here a detailed study of event 22 is presented. What happens is that a full quad – so 4 chips – fully light up. All rows and columns fire. This is typical.

## Slide 3: Study of events with many hits
Here the drift time (time pixel – t trigger) chips number and time over threshold
There is a train of hits in chips 0-3. Length is 40 msec.
Drift time (ms) chip nr ToT (count =25 ns)

## Slide 4: Study of events with many hits
Here the the event display for the start of the train -86 till -82 msec
After ToT > 6 cut
All rows start to fire
(for the same column)
The process is initiated
by 267 hits with a ToT
above 6

## Slide 5: Study of events with many hits
Here a zoom of the time structure.
The full train has a length of 40 msec. Each 0.5 msec a spike of 4000 hits is produced.
The process is initiated by 267 hits with a ToT above 6 and a mean ToT of 35.
The spikes correspond to spidertimes; 14, 15 etc.
The ToA is the same for all the hits in the spike for spidertime == 14
The second spidertime the ToA is one spike but 31 counts (x 25 nsec) later.

## Slide 6: Study of events with many hits
Geometrically speaking (display slide 4) one starts with the colums on the left (all rows fire) of the four chips of the quad and then for each spidertime one moves to the right. In the end all columns have fired.
The most likely interpretation is that an alpha or other particle produces locally a lot of charge say 267 electrons.
The chips draws current to process the data and this affects the threshold voltage. This causes the neighbours to fire etc. This propagates to the whole quad, because the power is distributed per quad.
The readout sequence of the TPX3 chip then determines the time order of the hits.

## Slide 7: Rate of events with many hits
// Vgrid -340
chip 0 rate of large events 0.0707196 all four rate 0.0707196
chip 4 rate of large events 0.0545906 all four rate 0.0545906
chip 8 rate of large events 0.0483871 all four rate 0.044665
chip 12 rate of large events 0.0434243 all four rate 0.0434243
chip 16 rate of large events 0.00992556 all four rate 0.00992556
chip 20 rate of large events 0.0248139 all four rate 0.0248139
chip 24 rate of large events 0.016129 all four rate 0.016129
chip 28 rate of large events 0.0198511 all four rate 0.0111663
// Vgrid -350
chip 0 rate of large events 0.1067 all four rate 0.1067
chip 4 rate of large events 0.0905707 all four rate 0.0905707
chip 8 rate of large events 0.0806452 all four rate 0.0781638
chip 12 rate of large events 0.0459057 all four rate 0.0459057
chip 16 rate of large events 0.0210918 all four rate 0.0210918
chip 20 rate of large events 0.0372208 all four rate 0.0372208
chip 24 rate of large events 0.0148883 all four rate 0.0148883
chip 28 rate of large events 0.028536 all four rate 0.0210918
Data Sr source with new gas envelop
Measured rate in intervals of 400 ms
V grid(V) 340 350
chip 0 – 16 0.04-0.07 (0.04-0.11)
16 - 32 0.01-0.03 (0.02-0.04)
Dead time train 40 msec / 400 msec
Efficiency loss dead time 0.2-1.1 %

## Slide 8: Solutions to events with many hits
The ultimate solution to the presence of events with many hits lies in the powering of the chips (Fred reminded me about this).
In the current quad design the digital and analog power supply are connected.
This is not a good idea, because small variations in the power consumption of the chip (e.g. because the chip start processing the data) cause ripples on the voltage. This affects the threshold of the pixels and causes all channels to fire simultanuously.
Therefore we expect that the separation of the digital and analog power will solve this issue.

## Slide 9: Reduction of the rate with many hits
On 27 May we performed a study to see how one could reduce the large event rate based on ideas from Jan.
For this we took runs at different thresholds 70, 65, 60 and 55.
It turned out that running at a slightly higher threshold of 60 cnts reduces the large event rate to about 10 events in the two concentrators in 1000 secs.
The grid voltage in this test run was put to 350 V.
This is a better and more comfortable operating point.
So we decided to use tthreshold 60 cnts as the default setting for the DESY testbeam.