## Slide 1: Software structure at Nikhef
DATA STORAGE:
/data/lepcol/common/BonnTelescopeTestJune17
/testbeam_bonn_october18
Prepared /testbeam_DESY_june21
Arawana DAQ and monitoring TPX3 software:
/project/lepcol/common/arawana/
Firmwares laser_setup_software localSPIDR2 sophy1.4.6 user
gastpx3home localSPIDR localstore2localSPIDR spidr3-software
Analysis software Kees /project/lepcol/users/cligtenb
Peter /project/lepcol/users/s01/arawanaSoftware

## Slide 2: Remote desktop and data taking
Levaard
arawana
Si telescope
PC-19-023
Switch
Control room
Remote hut
In hall
outside magnet
SLOW CONTROLS
Windows
DAQ TPX3
Linux
DAQ Si
Linux
Windows
Linux
Elrits
HV, Gas, stager and
run control (tunnel to arawana)
SPDR controls (2)
DAQ running
root file production

## Slide 3: Levaard Slow controls
Gas system: Measures and controls gas flow temperature of the 8-quad and O2 meter
HV system: controls the HV on the grid, guard etc. measures currents
Run control is used to start a run
- first start PUTTY and tunnel to arawana
- on arawana ./rundaq.sh (starts the daq in run control mode)
it should give a binding socket (if not ˆC and redo)
check on arawana chips: spidrchipids 192.168.1.10
if not 32 chips do: spidrreset 192.168.1.10
- from the panel Connect (to arawana) and then Configure
check the arawana PUTTY window to check that you are connected
after configure still have 32 chips in the readout
- if OK give run number and Start run
- After (e.g.) 60 s Stop run
- the bytestream is now closed and we can decode it (next slides)

## Slide 4: Software on elrits
On Elrits we open a remote desktop on arawana
1) We can see on arawana the LOGFILES
DATA files
2) And observe/monitor the USB outputs from the two SPDR systems
3) Start standalone test runs an arawana (commissioning)
4) start the program to produce a ROOT file for a given run and link
Elrits is also used to store - transfer from arawana - locally the data that we took on arawana:
elrits /localstore/TPX3/DATA
/ROOT

## Slide 5: Data and Software on arawana
Data structure on arawana:
/localstore2/TPX3/DATA/LOGFILES/arawana*.log
TPX3/DATA/LINK0/Runxxxx/*.dat
TPX3/DATA/LINK1/Runxxxx/*.dat
TPX3/DATA/TIMESTAMP/Runxxxx/*.dat
DAQ program on arawana:
/localstore/TPX3/spidr3-software/Telescope/DAQ_Concentrator
Running DAQ program standalone test for 10 secs
// cd /localstore2/TPX3/DATA/LOGFILES
Tpx3daq_concentrator -s "" -i 1 -p 2 -m -t 10
NB: This will create a dummy run number 1111 and write data
For a real run we will use run control from levaard

## Slide 6: Data and Software on arawana
Bytestream decoding program
/home/gastpx3/source init_laser_setup_software.sh
/localstore/TPX3/laser_setup_software/make_concentrator_tree.*
It produces a root file with histograms and ntuple (tree) on arawana:
/localstore2/TPX3/ROOT
Produce root file for run 1801 and link (concentrator) 0
cd /localstore/TPX3/laser_setup_software
./make_concentrator_tree -r 1801 -l 0 >&1 | tee out_1801_0.log
// name of the root file: run1801_0.root
This root file should be transferred to elrits, where it can be further analysed

## Slide 7: Analysis/Monitoring Software on elrits
elrits /localstore/TPX3/ROOT
/software
MaskAndTrim.C and .h
- runs over one root file and analyses the histograms in the root file
- Noise level per chip (and per pixel)
- Can be ran to produce files per chip with masked pixels
that are input to the DAQ maskPixels()
/localstore/TPX3/localCONFIGS/Module/ W0023_J09_dacs.txt W0023_D06_trimdacs.txt
root –l <return> > .L MaskAndTrim.C++ <return> > MaskAndTrim t <return> > t.LoopM() <return>
rootCommands.mes
- open root file root –l ../ROOT/filename
- one can browse the histograms TBrowser t
- or analyse the ntuple hits (use commands in file) and make selections
In the directory /software/detailedSoftware more detailed software is kept but this needs updating to be useful for testbeam monitoring