## Slide 1: Data analysis and DESY test beam timing
Investigated the rejection of events where a whole quad is lightning up.
If the total number of hits in a quad exceeds 20k, the quad is masked.
This removes effectively the high ToT spikes (above a tot value of 58).
Except in quad 7 where these high ToT still occur at the 10% level.
Quad 7 has als lower ToT values than all the other quads.
To remove these hits the ToT is required to be above 58.
Chip 11 has a short and was therefore masked.
Software related puzzle slide 3 onwards:
Why is the timing of the trigger wrt the concentrator problematic in the 5 GeV high rate data and OK for the the low rate 6 GeV data?

## Slide 2: Data analysis run 6969 ToT
We run 500 events for the B field 1 T and p=6 GeV (low trigger rate)
Hits are selected after a cut on the drfit time (next slide)

## Slide 3: Data analysis run 6969 and timing
Redid ntuple production using -600 nsec tzero offset to assign the hits to the trigger. Previously this was > 100 msecs.
This too large offset made that at high trigger rates hits were often assigned to the wrong trigger number.
Hits for event viewing (and ToT plots) are selected after a cut on the drift time >-600 < 400 nsec (t drift = t hit – t trigger)

## Slide 4: Data analysis run 6969 hitmap

## Slide 5: Data analysis run 6969 event 0
Inside time window
All

## Slide 6: Data analysis run 6969 event 1
Inside time window
All

## Slide 7: Data analysis run 6969 events
Inside time window Event 2
Inside time
Window
Event 3

## Slide 8: Data analysis run 7010
This is a 5 GeV high rate data set with rotated magnet.
Therefore a more crucial test of the timing.
Redid ntuple production using -600 nsec tzero offset to assign the hits to the trigger. Again 500 triggers/events.
Large stats in time window so looks good!

## Slide 9: Data analysis run 7010 event 0
Inside time window
All

## Slide 10: Data analysis run 7010 event 1
Inside time window
All

## Slide 11: Data analysis run 7010 events
Inside time window
Event 2
Inside time window
Event 3

## Slide 12: Conclusions
Rerunning the ntuples for runs 6969 and 7010 using the new timing offset gives excellent results in the low and high rate data sets.
Event displays show clearly that there is a large beam activity in between the triggers; there is a pulse train of electrons that cause this background.
A timing cut ( tdrift between -600 to 400 ns) can reduce this background; but e.g. the high rate data show that even then more electrons are crossing the pixel TPC.
Using the Si telescope hits one expects to select a clean single electron sample that can be used for performance studies.