## Slide 1: Data analysis and alignment
In order to run larger productions the software on arawana for the reading of the bytestream and the ntuple production was moved to stoomboot.
On the area /data/lepcol/ testbeam_DESY_june21/TPX3/ all the TPX3 bytestream data is available.
After a few days the following setup script worked
export ATLAS_LOCAL_ROOT_BASE=/cvmfs/atlas.cern.ch/repo/ATLASLocalRootBase
alias setupATLAS='source ${ATLAS_LOCAL_ROOT_BASE}/user/atlasLocalSetup.sh'
setupATLAS
lsetup "root 6.20.06-x86_64-centos7-gcc8-opt”
cd /project/lepcol/users/s01/arawanaSoftware/laser_setup_software
make
This compiles the bytestream converter (etc.) By running:
./make_concentrator_tree runnr –l 0 > conc0.log
./make_concentrator_tree runnr –l 1 > conc1.log
For each concentrator a rootfile is made /data/lepcol/ testbeam_DESY_june21/TPX3/ROOT

## Slide 2: TPX3 Data sets ROOT
/data/lepcol/testbeam_DESY_june21/TPX3/ROOT
run6906_0.root run6953_0.root run6969_0.root run7009_0.root run7010_0.root
run6906_1.root run6953_1.root run6969_1.root run7009_1.root run7010_1.root
These data are from different runs under different conditions (B field and momenta) and can be used for event studies.
In order to reduce the files size during the production a cut on the drift time at +- 1000 nsec is put (no cut on ToT). So only “in time” TPX3 hits are written out.
If needed ntuples for more runs can be produced.
A Root script for analysis/event studies can be found on: /project/lepcol/users/s01/Analyse.C Analyse.h
Results: https://indico.nikhef.nl/event/3207/

## Slide 3: Silicon Telescope analysis and alignment
The bytestream data of the telescope can be found on
/data/lepcol/testbeam_DESY_june21/Telescope
Already during the testbeam period in June, Gerhard installed the telescope software and produced a first alignment.
Last week Gerhard and I sat together and installed the software under my area.
/project/lepcol/users/s01/Telescope with directories analysis corryvreckan eudaq
The code uses the corryvreckan package from MIT developed for testbeam setups. The general broken lines GBL package developed at DESY is used for fitting.
The package decodes the bytestream, performs clusterization, describes the telescope with planes (measurements and scatterers), performs a first stage straight line matching between the hits in the inner and outer plane and feeds this to the GBL fit. Selections are applied and histograms are filled with e.g. residuals.

## Slide 4: Setup description (part)
.
[TLU_0]
material_budget = 4.99882e+217
orientation = 0,0,0
orientation_mode = "xyz"
position = 0,0,0mm
role = "auxiliary"
time_resolution = 1ms
type = "tlu"
[ScatteringPlane_Kapton]
number_of_pixels = 1024, 1024
material_budget = 0.0004
orientation = 0,0,0
orientation_mode = "xyz"
pixel_pitch = 55um,55um
position = 0,0,55mm
spatial_resolution = 4um,4um
time_resolution = 1ms
type = "timepix3"
[MIMOSA26_0]
mask_file = "maskfiles/maskLD68/MIMOSA26_0/mask_MIMOSA26_0.txt"
material_budget = 0.00075
number_of_pixels = 1152, 576
orientation_mode = "xyz"
pixel_pitch = 18.4um,18.4um
position = -29.668um,-50.721um,0
orientation = -0.237663deg,-0.226548deg,-0.509474deg
spatial_resolution = 3.2um,3.2um
#spatial_resolution = 6um,6um
time_resolution = 115us
type = "mimosa26"
Define measurement and scattering planes (detectors MIMOSA, TLU)
The alignment is part of it
Added the kapton scattering plane (dummy TPX3 plane)

## Slide 5: Alignment situation
.
Run 6902 was aligned by Gerhard B=0
Run 6903 6905 also OK B = 0
Run 6937 OK B = 0
Run 6944 OK B = 0
Run 7019 After interventions (changes axis) OK
Telescope alignment is very robust (OK > 1 week of data taking and interventions)

## Slide 6: Alignment with B field
.
Run 6952 has problems due to the straight line model of GBL
- Pattern recognition opened to make matching better
- Tested to add an scattering/Bending with X0=5 plane
Works but …. the curvature inside the Telescope already
gives large residuals (> 25 microns)
GBL can also fit a helix (curved track). For that one needs to configure the code and calculate the Jacobian for track propragation inside a homogeneous B field.
Currently under test.
- added a configuration to run with B field