## Slide 1: Refitting the plane rotations B=0T field data
In order to get good residuals, the planes had to be rotated in the B = 1 T data wrt the B = 0 field data.
MIMOSA26_0 B=0 -0.237663deg,-0.226548deg,-0.509474deg
B=1 1.18511deg,0.617419deg,-0.546716deg
MIMOSA26_1 B=0 0.950365deg,0.0589001deg,-0.781744deg
B=1 1.71068deg,0.497614deg,-0.777848deg
MIMOSA26_3 B=0 -7.59209deg,-3.96808deg,0.0561499deg
B=1 -7.46312deg,-3.71741deg,0.0810735deg
MIMOSA26_4 B=0 -7.78793deg,-4.01162deg,0.251758deg
B=1 -7.8627deg,-4.08141deg,0.224428deg
MIMOSA26_5 B=0 7.59776deg,3.74256deg,0.0428572deg
B=1 7.87038deg,-0.588829deg,-0.0336899deg

## Slide 2: Alignment B=0.5T run 6963
With B field angle -0.0175
from 1T data
Free fit gives
-0.0193

## Slide 3: Alignment B=0.5T run 6963
With B field angle -0.0175

## Slide 4: Alignment B=1T run 6986
With B field angle -0.0175
from fit to 1T data (these)

## Slide 5: Alignment B=1T run 6986
With B field angle -0.0175
from fit to 1T data (these)

## Slide 6: Why are plane rotations needed?
B Field inhomogeneities?
In the meeting Jan proposed to study whether B field inhomogeneities could cause these rotations.
The fit was update to include 5 parameters for the B scales.
Scale plane 0 and 1 was fixed at 1
In between planes 1-2, 2-3, 3-4 and 4-5 the value was free.
Run 6986 B=1T
B field scale 01 1 scale 12 1.00322 scale 23 0.995699 scale 34 1.00414 scale 45 0.986115
Run 6963 B=0.5T
B field scale 01 1 scale 12 1.12293 scale 23 0.976624 scale 34 1.00482 scale 45 0.930879
Conclusion the B scale values are slightly different from zero, but we still need to rotate the planes to get good residuals.

## Slide 7: Why are plane rotations needed?
Could this be a Lorentz angle effect?
In the silicon sensor the charge is collected on several strips, and the strip width is correlated to the angle of the track and the Lorentz angle of the electrons in the silicon. The expected effect should be rather small because the CMOS sensor is only 25 microns thick. The charge is also collected from a small region of a few microns.
The fit was adopted to included a general angular correction (for B field = 0). The fit gave a 3 microns displacement in z. The fit for the Lorentz angle gave zero with the errors.
Conclusion the Lorentz angle cannot cause the observed plane rotations.

## Slide 8: .. the plane rotations …
Currrent hypothesis is that the planes move due to the large field.
Probably this is related to the way the silicon sensors are fixed to the support frame. They are hanging on a rails and fixed in one fixed point with a screw.
Concerning the aligment process. The sensor are aligned one by one leaving free dx, dy (dz fixed) and three directions.
This means that ‘all’ effects are fully absorbed in this plane. So if plane 1 is not shifted or rotated, it will move to compensate for the shifts and rotations of the other planes.
This means that one has to iterate the aligment till the process converges.
The problem is that the fit of the rotations do not really converge properly, one needs many (>10) iterations.

## Slide 9: Unbiased Alignment
In order to get some idea of the origin of the plane rotations two problems in the procedure were found:
1) The standard procredure of fitting the position residuals per plane one by one (0,1,3,4,5), leaving free the positions in x and z needs iterations and converges quickly in three iterations, but can have biases. As explained earlier plane 2 == reference.
2) The procedure for the rotations angles: three Euler angles per plane doesnot converge properly.
To solve the second problem the 6 Euler angles in plane 0 and 1 are fitted together. In planes 3-5 all 9 angles are left free. This leads to a fast convergence in two iterations.
A more unbiased alignment procedure is followed:
  Only the B=0 field data is used
  First the errors in planes 3-4 are put to mm in order not to biases the fit results in planes 0-1

## Slide 10: Unbiased Alignment
  The position residuals in plane 0, then 1 are fitted (3 iterations)
  The then positions in 0 and 1 are fixed and the rotations are fitted in planes 0 and 1 (2 iterations)
  This gives an unbiased alignment of planes 0-3
  Then the errors in planes 3-5 are put to their nominal values
  After that the planes 3-5 are aligned in position (3 iterations)
  Finally, the 9 Euler angles of planes 3-5 are fitted (2 iterations)
  This gives detector that is fully aligned wrt the reference plane.
  Note that this can only be done with straight lines (B=0 field)
  The results for angles etc. are different from the Table on slide 1.
  One can then fit all the B=0 field data with a curved fit and plot the residuals. This in order to comapre later to the B=0.5 and 1 T data sets.

## Slide 11: Alignment B=0 T run 6905

## Slide 12: Alignment B=0 T run 6905

## Slide 13: Procedure for Alignment in B field
  Starting point is the B=0 field positions and rotations.
  First, the positions of planes 0,1,3,4,5 are fitted in three iterations
  Secondly, the 6 Euler angles in planes 0-1 and subsequently the 9 Euler angles in 3-5 are fitted in two iterations.
  From the fits it is clear that rotations are need in all planes.
  The shifts in positions are smaller but non zero.
  The results of this procedure is shown in the following plots and Table.

## Slide 14: Alignment B=0.5 T run 6963
With B field angle -0.0175

## Slide 15: Alignment B=0.5 T run 6963
With B field angle -0.0175

## Slide 16: Alignment B=1 T run 6986

## Slide 17: Alignment B=1 T run 6986

## Slide 18: Alignment results
plane B pos x pos y pos z euleryz eulerxz eulerxy
(T) (um) (um) (mm) (deg) (deg) (deg)
MIMOSA26_0 0 -25.984 -45.495 0.04 2.10264 -1.18419 -0.454928
0.5 -28.721 -44.259 0.04 0.54671 1.68123 -0.53371
1.0- 27.749 -41.764 0.04 1.3865 3.97541 -0.53222
MIMOSA26_1 0 -199.698 121.753 23.94 2.00295 -0.386747 -0.751205
0.5 -200.336 122.324 23.94 -1.54412 -1.51209 -0.782374
1.0 -198.976 122.956 23.94 1.50705 2.24359 -0.788562
MIMOSA26_3 0 -154.309 53.843 369.81 -23.0476 -3.10262 0.167991
0.5 -156.498 50.197 369.81 -14.6385 -3.64779 0.180253
1.0 -154.733 46.909 369.81 -8.48052 -5.42585 0.354432
MIMOSA26_4 0 63.521 176.188 392.27 -23.476 -3.18977 0.360047
0.5 61.565 175.247 392.27 -14.8068 -3.18112 0.351739
1.0 61.257 175.773 392.27 -8.34479 -4.67344 0.505291
MIMOSA26_5 0 -40.305 -19.455 415.84 23.4629 3.01622 0.174065
0.5 -28.377 -12.54 415.84 14.6509 0.577541 0.236001
1.0 -27.935 -10.875 415.84 8.06444 0.989785 0.423359

## Slide 19: Interpretation of the alignment results
The shift in position are largest for plane 5: 13 and 9 um (x y)
Other planes also move e.g. plane 0: 3 and 4 um plane 3: 2 and 7 um
Rotations in euleryz and eulerxz are far larger and have more impact on the residuals. Eulerxy is rather stable and has a smaller impact.
Concerning planes 3-4-5:
There is a pattern for euleryz: “-angle – angle +angle”
The angle is large: 23, 14 and 8 degrees (B=0,0.5,1 T); with a linear trend.
The eulerxz is more stable but still changes by 2 degrees.
In planes 0-1 euleryz changes by 3.5 degrees and xz by 5 degrees.
In Summary: shifts due to the field are observed in planes (up to 13 mu)
Rotation changes due to the field are large up to 15 degrees in the last three planes, in the first planes they go up to 5 degrees.
Puzzle: the B=0 data gives too large values for euleryz.