## Slide 1
Peter Kluit
Nikhef Annual meeting 15 December 2016
Lepton Collider program

## Slide 2
The International Linear Collider
The physics case will be discussed at vista 25

## Slide 3
Lepton Collider program
the people involved…
Kees Ligtenberg PhD
sep 2016 ILC simulations
Kevin Heijhoff PhD
oct 2016 pixel TPC Bonn/Nikhef
Harry van der Graaf
Fred Hartjes
Jan Timmermans
Gerhard Raven
Stergios Tsigaridas
Peter Kluit
Wouter Bos Master student

## Slide 4
Lepton Collider program
the Quad team & Bonn…
University of Bonn group
Yevgen Bilevych, Klaus Desch, Jochen Kaminiski, Kevin Heijhoff, Tobias Schiffer,
Lucian Scharenberg, Christof Krieger, Sebastian Schmidt, Andrea Fürstenberg
Ruud Kluit, Auke Korporaal,
Patrick Werneke,
Charles Ietswaard,
Bas van der Heijden et al

## Slide 5
Made in 2015 proposal for a Lepton Collider
program to the WAR:
  we currently don’t know which machine will be built (and when)
  most interested physicists will only work part time
  focus the R&D on the pixel readout of the TPC in ILC/ILD
  modest resources for TPC module
  request 2 PhD students
The director has given follow up on this and launched an “initiatief programma”
close Collaboration with Bonn
2 PhD students (one shared with Bonn)
Made an OPP proposal that was granted to build a quad (4 chips)
a first step towards a TPC module (100 chips)
What happened @ Nikhef?
ILD detector
TPC end plate
modules DESY

## Slide 6: Nikhef-Saclay Octopuce GridPix
GridPix chip (1x1) 14 x 14 mm
Octopuce (2x4) 28 x 56
Module (≈100)
2nd generation of chip
Since 2015/2016 we have a TimePix 3 chip

## Slide 7
Test beam DESY performance
Module 1 is in great shape
320 V and B=1 T z = 1cm
Resolution 100 μm per hit. (ExB) Deformations at the edges of the board are under control and systematics per chip less than 20 μm. This is good enough for a TPC (Jan & Peter).
all
100 μm
about 40 hits per fully crossed chip

## Slide 8: TimePix 3 single chip with Bonn/IZM InGrid
with InGrid
zoom on grid
Sparking and the protection layer 4 μm SixNy
- Origin of sparks and detector failure was tracked down to cracks in protection layer. A careful cleaning and monitoring process was developed at IZM.
Extensive sparks tests have been done at Bonn taking more than a million sparks without detector failure.
At CERN also sparking tests in a hadron beam have beam successfully performed (Stergios, Kevin & Fred)

## Slide 9: TimePix 3 single chip laser tests
Laser spots each ≈1 mm scan the single chip detector
Deformations at the edges are due to the not yet optimally matched Guard potential
TimePix 3 allows for a precise time of arrival measurement
Kevin, Fred @ Nikhef

## Slide 10: Pixel TPC simulations
Kees, Peter
ttbar event display
single muon event
Pixel read out ≈15 000 hits
pad read out ≈250 space points
Full ILD simulation using DD4HEP and fast pixel digitization
On the way to
e.g. H ττ
physics studies