## Slide 1: Pixel TPC testbeam results
Yevgen Bilevych, Klaus Desch, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
Lepton Collider 31 January 2022
8 Quad Module

## Slide 2: Pixel TPC
(TimePix1) TPX3 chip Quad Module TPC plane
(2007-14) 2017 2018 2019
(Octopuce)

## Slide 3
DESY testbeam Module Analysis
Preliminary results for Run 6969-72 B=1 T p =6 GeV
Tracks are preselected using the Mimosa Telescope
Very loose matching with Telescope track
Alignment of the 8 quad module from B=0 run 6916:
  local frame xy and z (drift) positions; angles dx/dy and dz/dy
  Adjusted t0 and x per chip (no rotation inside module)
Time slewing applied using ToT:
  dt (ns)= 18.6/ (0.1577+ToT(ms))
Drift velocity (E=280 V/cm) 78 mm/ns
A local fit is performed to the track hits using errors:
  sxy = 180 mm and sz =450 mm (slight dependence on ToT)

## Slide 4
DESY testbeam Module Analysis
z global
x global
z global
y global
y local
y local
x local
z local drift
Track fit with curvature q/p free
Track hits 657
c2xy = 315/654
c2z = 493/559
(with asymmetric tail and outlier removal applied)

## Slide 5
DESY testbeam Module Analysis
sxy = 180 mm and sz =450 mm (assigned error) 2.2 M hits
Run 6969-72 B=1 T p =6 GeV
<mean> 4.9 mm

## Slide 6
DESY testbeam Module Analysis
Run 6969-72 B=1 T p =6 GeV
One chip was disconnected
Neighbouring chip in x was masked. Can be recuperated but needs distortion correction.
Mix of 4 runs where the module was displaced in x (3) and z (1)
Beam has small angle wrt module

## Slide 7
DESY testbeam Module Analysis
Track selection:
more than 100 hits in concentrator 0 and 1
more than 50% of the hits should be on the tracks
3694 selected tracks
large number 603 hits / track
module or tracklength 157.96 mm
Run 6969-72 B=1 T p =6 GeV
outlier removal in xy applied

## Slide 8
DESY testbeam Module Analysis
Run 6969-72 B=1 T p =6 GeV
Fitted resolution in 1 mm slices with gaussian core
Not clear that the chip alignment inside the module in xy is (now) better than 50 mm.
NB we use all but two chips
The z resolution is larger than for the quad:
Could be due to the fact that we don’t use the silicon track
Or time jitter in the distribution of the clock; Or t0 calibration
z edges near 0 and 15 mm are biased in z (‘geometrical’ cuts)
ToT > 0.6 ms
B=1 T
DT = 110 mm
sxy0 = 70 mm 55 mm/ 12
DL = 200 mm
sz0 = 350 mm 35 mm

## Slide 9
DESY testbeam Module Analysis
Tracking precision:
position 11 mm (xy) 20 mm (z)
angle 0.18 mrad (dx/dy) 0.43 mrad
module tracklength = 157.96 mm
The 1T B field reduces the diffusion and the tracking precision in xy is improved substantially
Run 6969-72 B=1 T p =6 GeV

## Slide 10
DESY testbeam Module Analysis
Run 6969-72 B=1 T p =6 GeV
Mean residuals xy over the module plane
Mean residuals z

## Slide 11
DESY testbeam Module Analysis
Preliminary results for Run 6916-18 B=0T p =6 GeV
Tracks are preselected using the Mimosa Telescope
Very loose matching with Telescope track
Alignment of the 8 quad module from B=0 run 6916:
  local frame xy and z (drift) positions; angles dx/dy and dz/dy
  Adjusted t0 and x per chip (no rotation inside module)
Time slewing applied using ToT:
  dt (ns)= 18.6/ (0.1577+ToT(ms))
Drift velocity (E=280 V/cm) 78 mm/ns
A local fit is performed to the track hits using errors:
  sxy = 450 mm and sz =540 mm (slight dependence on ToT)

## Slide 12
DESY testbeam Module Analysis
z global
x global
z global
y global
y local
y local
x local
z local drift
Track fit with curvature q/p free
Track hits 1046
c2xy = 412/1044
c2z = 687/979
(with asymmetric tail and outlier removal applied)

## Slide 13
DESY testbeam Module Analysis
sxy = 450 mm and sz =540 mm (assigned error) 2.5 M hits
Run 6916-18 B=0 T p =6 GeV
<mean> 14 mm

## Slide 14
DESY testbeam Module Analysis
Run 6916-18 B=0 T p =6 GeV
One chip was disconnected
Neighbouring chip in x was masked. Can be recuperated but needs distortion correction.
Mix of 3 runs where the module was displaced in z
Beam has small(er) angle wrt module

## Slide 15
DESY testbeam Module Analysis
Track selection:
more than 100 hits in concentrator 0 and 1
more than 50% of the hits should be on the tracks
2853 selected tracks
large number 847 hits / track
module or tracklength 157.96 mm
Run 6916-18 B=0 T p =6 GeV
outlier removal in xy applied

## Slide 16
DESY testbeam Module Analysis
Run 6916-18 B=0 T p =6 GeV
Fitted resolution in 1 mm slices with gaussian core
Not clear that the chip alignment inside the module in xy is (now) better than 50 mm.
NB we use all but two chips
The z resolution is larger than for the quad:
Could be due to the fact that we don’t use the silicon track
Or time jitter in the distribution of the clock; Or t0 calibration
z edges near 0,15,25,35 mm are biased in z (‘geometrical’ cuts)
ToT > 0.6 ms
B=0 T
DT = 300 mm
sxy0 = 70 mm 55 mm/ 12
DL = 200 mm
sz0 = 350 mm 35 mm

## Slide 17
DESY testbeam Module Analysis
Tracking precision:
position 16 mm (xy) 20 mm (z)
angle 0.36 mrad (dx/dy) 0.43 mrad
module tracklength = 157.96 mm
Run 6916-18 B=0 T p =6 GeV

## Slide 18
DESY testbeam Module Analysis
Run 6916-18 B=0 T p =6 GeV
Mean residuals xy over the module plane
Mean residuals z