## Slide 1: Pixel TPC testbeam results
Yevgen Bilevych, Klaus Desch, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
Lepton Collider 11 July 2022
8 Quad Module

## Slide 2
DESY testbeam low and high rate
After the analysis of the low rate data taken at 6 GeV (e.g. B = 0 run 6916) data look at the high rate data sets for B = 0 e.g. run 6932 and 6933.
Suffered from (very) low efficiency in selections
The general picture track reconstruction after improvements
Run triggers TPX3 TPX3+Mimosa tighter matched
tracks tracks tracks
6 GeV 1k 191 176 166
5 GeV 10k 673 436 108

## Slide 3
DESY testbeam low and high rate
Trigger situation
The efficiency of the trigger is not very high 30-50%. It also provides triggers of soft particles outside the TPX3 and Telescope acceptance.
This is not a problem but explains the low selection numbers.
Beam situation
The low rate 6 GeV data are quite clean and the selected momenta range is limited. The high rate 5 GeV has a large momentum range and the events in the TPX3/Telescope have more splashes and additional low(er) momentum tracks. This gives more background in particular in the B=0 runs.

## Slide 4
DESY testbeam low and high rate
Timing situation
The trigger is passed to the TLU and the time stamp is recorded in the TLU data stream. The output of the TLU goes to a NIM module that is connected to the TPX3 SPIDR. The TPX3 SPIDR injects a time stamp in the TPX3 time stamp data stream.
A second TPX3 SPIDR reads out the concentrators and TPX3 chips. The two TPX3 SPIDRs are synchronized.
The TLU and the TPX3 SPIDR(s) are not synchronized.
The timestamps from the TLU and TPX3 can be compared and one clearly observes that the times are offsetted and the clocks run at a slightly different speed.
By comparing the timestamps one can conclude that the streams are the same within a bin of 25 nsec.

## Slide 5
DESY testbeam low and high rate
Some details about the TLU Timing situation
The TLU records a trigger time stamp and also records the additional triggers that come in. In the high rate data the number of additional incoming triggers varies between 0 and 10.
For synchronization with the TPX3 the additional triggers are discarded. After that the times of TLU and TPX3 lie within a 25 nsec bin. For each run we can check this using the data (using the ntuple).
Clearly we wanted this to be with < 1 ns. Jan suspects that a wrong output was used that puts everything in a 25 nsec TLU clock cycle of 40 MHz.
Unfortunately, this limits the z track position in the TPX3.
However, it still means that timing is good up to 25 nsec and that is by far good enough to match TPX3 with Mimosa hits.

## Slide 6
DESY testbeam low and high rate
Low effciency questions:
Are we loosing Mimosa hits (clusters)?
Disussing possible efficiency losses with Uwe Kramer the following study was done. Currently, the clusters are collected with a window of -115ms to 230ms of the trigger: the sliding window of the Mimosa read out. By running the code in the metronome mode (fixed time 345ms), one is sure that all clusters end up in the data. Comparing the two ways of running showed that all clusters end up in the data and none are ‘lost’.
So we are convined that all Mimosa clusters are made.

## Slide 7
DESY testbeam low and high rate
Low effciency questions:
What happens in the telescope track reconstruction?
In the current procedure the telescope tracks are built requiring 5 out 6 planes on the track. All track combinations are stored in the track collection (also subsets).
To be sure about this, I wrote a complete track finding algorithm using as an input the clusters and the TPX3 track as a seed.
This code can be used to cross check the standard Telescope track finding.
What is clear in the high rate data sets is that the Mimosa clusters are rather scattered by the multiple scattering of the track.
In order to ensure reconstruction the momentum of the track for multiple scattering is put to 500 MeV. In the track General Broken Lines (GBL) fit the multiple scattering is fitted out. NB previously we have put e.g. a value of 5 GeV for the 6 GeV data.
We are convinced that all telescope tracks are found (be it with large multiple scattering). At high rate there are more TPX3 tracks/particles that scatter.