## Slide 1: Pixel TPC testbeam results
Yevgen Bilevych, Klaus Desch, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
Lepton Collider 19 December 2022
8 Quad Module

## Slide 2
DESY B=0 testbeam high stats
The B=0 field runs 6916 6917 6934 6935
p (GeV) 6 6 5 5
(x,z) 1,1 1,2 0,2 2,2
Last meeting showed alignment inconsistencies that are understood:
  Solved after correcting the pneumatic displacement in x from 20 to 19.7 mm
  In z ‘time jumps’ between 6916-17 and 6934-35 runs
    This is due to threshold change in the chip settings (affects time and z)
  One cannot simply assume that 6916 and 6917 are the same; z has changed and this affects angles. Further the E field may be slightly inhomogenous and have small distortions in e.g. x ( drift time) vs z
In these studies a careful alignment was performed for the 4 runs by adjusting
  mean x(z) dx(z)/dcolumn dx(z)/drow column=local x row=local y
  mean x(z) and dx((z)/drow are geometrical (shifts/rotation)
  dx(z)/dcol is a deformation: in z e.g. caused by a tilt in z of the chip
  in x caused by a misalignment (or mistune of the guard V) of the E field

## Slide 3
DESY B=0 run 6916-17-34-35
xy: Mean corrected residual wrt telescope track
z: Mean corrected residual wrt TPX3 track
Maximum scales
are 0.1 mm
One chip was disconnected
Guard gives 4 vertical white bands
The small middle horizontal white line is the area between the chips
The two broader white lines are not covered by the Telescope acceptance

## Slide 4
DESY B=0 run 6916-17-34-35
In blue/red concentrator 0/1

## Slide 5
DESY B=0 run 6916-17-34-35
“bin”
size 20 (colums) by 40 (rows) pixels
> 1000 entries
(expected) column number 15-240
Quad uses 4x4
> 800 entries
mean residuals xy and z per “bin” for the module
rms xy 0.041 mm rms z 0.026 mm
core 0.031 0.024 |value|<0.1 mm
stat rms xy 0.008 rms z 0.010
Fit method xy and z rms 0.011 (refit data in 2 z slices)
Except chips 8,10,24 rms xy 0.046 z 0.019 …

## Slide 6
DESY B=0 run 6916-17-34-35
Module layout xy
concentrator 0
Mean residuals per bin for each chip

## Slide 7
DESY B=0 run 6916-17-34-35
Module layout xy
concentrator 1
Mean residuals per bin for each chip

## Slide 8
DESY B=0 run 6916-17-34-35
Module layout z
concentrator 0
Mean residuals per bin for each chip

## Slide 9
DESY B=0 run 6916-17-34-35
Module layout z
concentrator 1
Mean residuals per bin for each chip

## Slide 10
Conclusions module
Precision results for the whole module were shown for the B=0 data
The 2D module deformation (mean residual) plot looks good
The rms of the distribution in xy and z is larger than e.g. the quad
For the core we found 31 mm (xy) and 24 mm (z)
For the quad full area 13 mm (xy) and 19 mm (z)
Note that the statistics is much lower than for the quad
Secondly, no deformation correction is applied to the data as was done for the quad (Cauchy shape)