## Slide 1: DESY ToT puzzles
Follow up of the low efficiency, low ToT puzzle
In Bonn 26 January 2023 Fred inspected the quad with chips 28 till 31.
The HV is properly distributed.
Is there some issue with the threshold setting?
This was studied in the following slides 6 September 2021.
In addition I made plots to see wether in general the threshold is different for the chips inside the different quads. See next slide.

## Slide 2: DESY ToT puzzles
Noise Threshold per chip in counts
Noise Threshold per chip inside quad (0-4)
- mean per quad + mean all chips
Conclusion is that there is no statistically significant pattern inside quad

## Slide 3: DESY ToT puzzles
DESY testbeam thresholds = this noise threshold plus offset that is 60,60 for concentrator 0,1 (for runs 6926-end concentrator 1 was raised to 65)
Most likely cause is that we need to check the noise threshold settings for the chips.
The noise level can vary wrt power distribution and cooling and Temperature.
It could be that the thresholds were too high for chips 28-31.
Estimated threshold change needed to achieve high efficiency
(based on the LCTPC slide included in the next slide)
Chip 8 -15
Chip 10 -15
Chip 14 -15
Chip 28 -25
Chip 29 -35
Chip 30 -25
Chip 31 -35
NB these are neighbours of chip 11 with the short after the repair the thresholds don not have to be adjusted

## Slide 4
DESY testbeam Module Analysis
Chips 28-31 (one quad) lower ToT and less hits
Clear correlation gain – ToT – efficiency
Need to design a possibility to adjust the HV of individual chips
Preliminary
Chip 11 disconnected
Per chip: Time over Threshold and TPX3 hits on track
Runs 6909, 6916-17, 6934-35 B=0 T p =6,5 GeV

## Slide 5: DESY ToT puzzles
Hardware related puzzles
What is the cause of the (largely) different ToT values for the chips?
  Is this due to the electronics of the TPX3 chip?
  Is it due to the gain differences? And due to the height varations of the pillars of the Grid
Here the plot for the ToT and mean ToT per chip for run 6969. After removing the large events where the quad lights up.

## Slide 6: DESY ToT puzzles
Is it the difference in the mean ToT due to the different thresholds in the chips?
No as shown in the plots below

## Slide 7: DESY ToT puzzles
Is it the difference due to a different electronics response for the different chips?
The testpulse data – where we inject a signal and scan the fine threshold and count the number of hits - show no clear different behaviour for chips 29, 30 or 31.

## Slide 8: DESY ToT puzzles
Is it the mean ToT constant over the surface of the three chips 29-31?
There are large systematic
variations of +- 2

## Slide 9: DESY ToT electronics calibration
ToT calibration plots from Kees for the 4 chips of the Bonn testbeam quad
The per pixel variations of the (electronics) ToT is 6.5% RMS
https://indico.cern.ch/event/267425/attachments/477859/661149/Timepix3_final.pdf
Chip 0
Chip 1

## Slide 10: DESY ToT electronics calibration
ToT calibration plots from Kees for the 4 chips of the Bonn testbeam quad
Systematics around 1000e is about 10%
Chip 2
Chip 3

## Slide 11: ToT conclusions
The per chip variations in the ToT calibration are not due to electronics gain differences (that can only produce up to 10% variations)
They are also not correlated to the position of the chip on the wafer (see talk by Jan 23 August https://indico.nikhef.nl/event/3207/)
They also not correlated to the thresholds
The low ToT values for chip 28-31 could be due to the power distribution of the multiplexer. The power is more critical for this quad as more channels go over threshold together (hurray events)
The variations between the chips and the variations over the chip of +- 2 counts could be due to variations of the charge up of the protection layer