## Slide 1: EIC information
The DAQ computer Arawana has login gastpx and pwd Gastpx
The Slow Controls Computer Levaard uses Labview
login pwd @dministrat0r (so zero r)
We took data in DESY with Ed=280 V/cm
The grid was put at Vgrid = 340 V
The surrounding guard (yellow) 355 V
The guard (white) was put at 359 V
The guard wires were put at 380 V
Guard and Guard wires
The guard (white area) sits about 1 mm above the grid. The guard wires (red) 50 mm CuBe are not connected to the guard; about 200 mm above it. The layout can be seen on the next slide.

## Slide 2: 8-QUAD module with field cage
in red guard wires
in white guard
In yellow surround guard
wetransfer_foto-s-testbox_2023-04-14_1217.zip

## Slide 3: Prepared boxes
Dimensions in cm (no margin)
length depth height
45 47 81
Wooden box should be
50 x 50 x 85 cm3

## Slide 4: List of items to be transported to US
- 32 chip Gridpix detector with protection box and concentrators
- main SPIDR board with adaptor
- trigger SPIDR with adaptor
- computer DAQ Arawana (linux)
- cables to connect detector/trigger/DAQ system
- Mini HVs + one MiniHV powersupply with cables
- High speed CAN to USB interface
- computer Slow Controls Levaard (windows)
- USB cables to connect slow controls
The equipment is used for a testbeam experiment.
The equipment is loaned on a cost recovery basis of 37 000 euro.
Loan period 1 June 2023 till 1 June 2025

## Slide 5: Wooden transport box
- Dimensions 54+6 cm height x 54 cm depth x 89 cm length
- Weight 60 kg
- Insured value 37 keuro
Commercial value;
2 computers commercial value 500 US$
electronics Xilinx board and SPIDR 2000 US$