## Slide 1
To keep in mind: ’16’ unit, consisting of (seamless!) integration of 4 Quads:
common CoCa
possibly using only two dStrings: each dString is a double-length
Quad string (aka an Octo string)

## Slide 2
Wire bonding board: top view
Hapje eruit aan N en Z zijde voor: - positionering WBBoard op Central CoCa
- pillars voor Guard electrode
- doorvoer HV Grid, HV Guard
Side View, looking N
‘canal’ guard electrode
geometrie, positie en potentiaal
door LepCol te bepalen.

## Slide 3
Optimal Long T structure(s)
Grid @ 775 μm (z) -400 V
Chip 700 μm (z) height
Guard
size Chip (x) 256*55 μm
The long T structure (as proposed by Fred Hartjes) extends over till the grid starts. So the long T covers the area that has “ground or undefined on the chip” and stops where the grid defines the HV. This looks to me the most optimal configuration.
The z distance of the structure should come from the MT/ET.
The overlap is defined by the chip edge and where the grid starts. The total T length is defined by the minimal distance between chips including the bonds. The guard could be designed in a similar way as shown in picture.
distChip/2
z
Long T structure
x overlap 200 μm
dz = 300 μm

## Slide 4
Design with a long T structure
.
chip
grid
support
bond pads
PCB
cooling
connector
The long T should cover the part of the chip that has ground. On the edge of the grid one has metal (above dike) and a resistive layer (in blue). The T should extend to the edge of the metal layer (+100μm overlap) .

## Slide 5
Design with a long T structure
.
chip
grid
support
bond pads
PCB
cooling
connector
The long T should cover the part of the chip that has ground. On the edge of the grid one has metal (above dike) and a resistive layer (in blue). The T should extend to the edge of the metal layer (+100μm overlap) .
Side View, looking N
‘canal’ guard electrode

## Slide 6
TPX-3 GridPix
ColdCarrier
CoCa
String
WireBondingBoard
PowerBoard
Data string
CoCa Top View.
Slits breed genoeg om
PowerBoard door te laten.
Of CoCa een samenstelling van
left (Power) deel, center deel,
en right (data) deel.
Optie: Data string
op CoCa laten eindigen
met print+ connector?
Maar wel: we gaan voor
hoogste readout snelheid,
dus ‘brede’ data string?