## Slide 1: Pixel TPC testbeam results
Yevgen Bilevych, Klaus Desch, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
Lepton Collider 17 July 2023
8 Quad Module

## Slide 2
DESY testbeam Module Analysis
Performance of dEdx
Use the B=0 an 1 T runs select the central chips (same runs as for deformation studies).
Remove 2 chips per row (deformations and low performance)
Calibrate the number of electrons to be equal for the different chips. Correct for slight z dependence (in B=1T data).
We have 6 chips on the track
B=0 T number of tracks 14534
mean number of electrons for 848 with rms 245
B=1 number of tracks 19860
mean number of electrons 632 with rms 119

## Slide 3
DESY testbeam Module Analysis
Performance single electrons
B=0 T has a large Landau tail
B=1 T tiny Landau tail and a more gaussian distribution
Very large difference

## Slide 4
DESY testbeam Module Analysis
Time over threshold
Distributions for Time over threshold (total sum) for B=0 T and 1 T
Slightly larger tail and shifted mean for B=0 data

## Slide 5
DESY testbeam Module Analysis
Performance single electrons
Thesis Kees Ligtenberg Single chip
Quad module
More long tail in distribution

## Slide 6
DESY testbeam Module Analysis
Performance single electrons
Quad module
B=0 T
B=1 T
B=0 T has a large Landau tail
B=1 T tiny Landau tail and a more gaussian distribution

## Slide 7
DESY testbeam Module Analysis
Performance of dEdx
220 pixels per chip along track
make 20 pixel intervals for dEdx @ 90%
Build 1 m long track with 79 chips (100% coverage) resolution (electron) 4.1%
Thesis
Kees Ligtenberg
p 77 onwards

## Slide 8
DESY testbeam Module Analysis
Performance of dEdx
Use 220 pixels per chip along track
Build 1 m long track with 51 chips realistic coverage
B=0 T chips 2 6 7 9 16 17 26 27
B=1 T chips 2 3 6 7 9 12 13 16 17 20 21 26 27
Calibrate the dEdx (scale factor)
Method:Truncated mean electrons
  make 120 pixel intervals
  Remove 10% highest counts -> dEdx @ 90%
  NB Single chip publication used 20 pixel interval with 79 chips (maximal coverage) and more tracks
Quad module

## Slide 9
DESY testbeam Module Analysis
Performance of dEdx
Method:Truncated mean electrons
mean dEdx 5083
rms 384
resolution 0.075
Quad module
B=0 T

## Slide 10
DESY testbeam Module Analysis
Performance of dEdx
Method:Truncated mean electrons
mean dEdx 3774
rms 207
resolution 0.055
Quad module
B=1 T

## Slide 11
DESY testbeam Module Analysis
Performance of dEdx
Method 2 “Truncated tail electrons”
Idea is to remove large clusters
First remove clusters with more than 6 hits in 5 consecutive pixels
Secondly calculate truncated mean (as before) for remaining single electrons
  make 120 pixel intervals for
  Remove 10% highest counts dEdx @ 90%
Quad module

## Slide 12
DESY testbeam Module Analysis
Performance of dEdx
Method:Truncated tail electrons
mean dEdx 3772
rms 221
resolution 0.059
Quad module
B=0 T

## Slide 13
DESY testbeam Module Analysis
Performance of dEdx
Method:Truncated tail electrons
mean dEdx 2652
rms 99
resolution 0.037
Quad module
B=1 T

## Slide 14
DESY testbeam Module Analysis
pixel distance
Single chip
Quad module
B=0 T

## Slide 15
DESY testbeam Module Analysis
Performance of dEdx
Method 3 “Fit of the distance distribution”
The idea is to exploit the physics that is in the distance distribution
For large distances the fluctuations are Poissonian and the distribution is exponential: here we “count” clusters
For small distances, more electrons are freed and larger (non- Poissonian and more Landau-like) fluctuations occur
The idea is to down-weight the distribution at low distances to follow an exponential distribution. The fluctuations are then given by sqrt(N), where N is the down-weighted number of events
The exponential fit p0 exp(-p1 x) has two free parameters the total number of “amplitude” electrons p0 and the slope p1.
Both are sensitive to dEdx
  More clusters/mm means larger p0 and p1

## Slide 16
DESY testbeam Module Analysis
Performance of dEdx
Method 3 “Fit of the distance distribution”
Here one can see that from 10 clusters onwards an exponential distribution is followed.
Below 10 the distribution will be down-weighted (by 1/weight).
The weights are:
Weights B=0 = { 35.0467 , 12.1497 , 4.52914 , 2.76311 , 1.99386 , 1.59795 , 1.3656 , 1.21409 , 1.11898 , 1.04385 };
Weights B=1 = { 18.0291 , 5.92609 , 1.82486 , 1.26074 , 1.08588 , 1.014 , 0.986373 , 0.967029 , 0.959339 , 0.9649 };
B=0 T

## Slide 17
DESY testbeam Module Analysis
Method 3 Fit of the distance distribution
B=0 T
fitted amplitude electrons p0
mean 203 rms 15
resolution 0.073
fitted slope p1
mean 0.169 rms 0.009
resolution 0.053
high resolution for slope

## Slide 18
DESY testbeam Module Analysis
Method 3 “Fit of the distance distribution
B=1 T
fitted amplitude electrons
mean 265 rms 13
resolution 0.048
fitted slope
mean 0.162 rms 0.004
resolution 0.027
high resolution for slope

## Slide 19
DESY testbeam Module Analysis
Started simulation of MIPs extracted from the data:
depositing 70% of the electrons, by stretching the track in one single chip (by 1/0.7). Same technique as was used by Kees.
Check that the dEdx methods scale linearly and the fit values for the amplitude and slope too.
First results look fine
Simulate the performance for a MIP

## Slide 20
DESY testbeam Module Analysis
Summary of results
Method | B=0 Resolution (%) | B= 1 Resolution (%)
dEdx 90 | 7.5 | 5.5
dEdx 90 tail | 5.9 | 3.7
Fit amplitude | 7.3 | 4.8
Fit slope | 5.3 | 2.7
Resolutions for electron track of 1 m with 51 chips (so realistic ~60% coverage).