## Slide 1: Pixel TPC testbeam results
Yevgen Bilevych, Klaus Desch, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
Lepton Collider 4 September 2023
8 Quad Module

## Slide 2
DESY testbeam Module Analysis
Towards a paper
Results on diffusion for B=0 and 1T data
Results on deformations and tracking precision for B=0 and 1 T data
- Results for dE/dx with different methods for B=0 and B=1 T data

## Slide 3
DESY testbeam Module Analysis
287 mm/
268 mm/
ToT > 50 ms
B=0 T
T2K*
Fit quality c2/ndf = 124/137 c2/ndf = 96/121
Study of the B = 0 T field data set
runs 6916 6917 6918 p=6 GeV
T2K* = T2K gas with O2 and H2O
Ed=280 V/cm
Preliminary

## Slide 4
DESY testbeam Module Analysis
Fitted drift velocity per run in mm/ns
run 6916 vdrift 0.0630034
run 6917 vdrift 0.0630206
run 6918 vdrift 0.0616319
Some numbers: 6854 TPX3 Telescope tracks mean nr TPX3 hits 964.3
Study of the B = 0 T field data set
runs 6916 6917 6918 p=6 GeV

## Slide 5
DESY testbeam Module Analysis
120 mm/
251 mm/
ToT > 50 ms
B=1 T
T2K*
Fit quality c2/ndf = 19/35 c2/ndf = 21/34
Study of the B = 1 T field data set
runs 6983 6986 6989 6990 p=5 GeV
T2K* = T2K gas with O2 and H2O
Ed=280 V/cm
Preliminary

## Slide 6
DESY testbeam Module Analysis
Fitted drift velocity per run in mm/ns
run 6983 vdrift 0.0587502
run 6986 vdrift 0.0582876
run 6989 vdrift 0.0590797
run 6990 vdrift 0.0571644
Some numbers: 7605 TPX3 Telescope tracks mean nr TPX3 hits 714.6
Study of the B = 1 T field data set
runs 6983 6986 6989 6990 p=5 GeV

## Slide 7
DESY testbeam Module Analysis
Runs 6909,16-18,34,35 B=0 T p = 5,6 GeV
Remove/exclude
- 4 corner chips
- chips around 11
- chip 16
B=0 T
situation
Preliminary

## Slide 8
DESY testbeam Module Analysis
Here the Telescope tracks are used and residuals in xy calculated wrt to the Telescope track. In z the Telescope track is shifted (1 free parameter refit of T track wrt TPX3 hits) to account for the trigger jitter; and the z residuals are calculated.
Telescope track 5 out of 6 planes and c2z,xy < 100 TPX3 hits > 200
A selection is applied on the difference between the Telescope track and the TPX3 track parameters (in xy, z and angles dxdy and dzdy).
Some numbers: 21789 Telescope tracks mean nr TPX3 hits 860.3
Study of the B = 0 T field data set
Runs 6909,16-18,34,35 B=0 T p = 5,6 GeV

## Slide 9
DESY testbeam Module Analysis
Runs 6981-6988 B=1 T p=5 GeV
Remove/exclude
- 4 corner chips
- chips around 11
- chip 16
Deformations in xy for excluded chips are smaller than for B=0 and have often a different shape.
This is due to the fact that electrons follow the B field lines @ 1T
xy
z
B=1 T
situation
Mean residuals
Preliminary

## Slide 10
DESY testbeam Module Analysis
Study of the B = 1 T field data set
runs 6981-6988 p=5,6 GeV
Here the TPX3 tracks are used and residuals in xy and z calculated wrt to the TPX3 track. The curvature is fitted. TPX3 tracks are selected with more than 200 hits and within the acceptance (position xy, z and angles dxdy, dzdy and curvature).
In the final fit the momentum is fixed and residuals in xy are calculated.
Some numbers: 74447 TPX3 tracks mean nr TPX3 hits 663.5

## Slide 11
DESY testbeam Module Analysis
Runs 6909,16-18,34,35 B=0 T p = 5,6 GeV
B=0 T
situation
xy
z
Preliminary
Mean residuals regrouped the row and column planes

## Slide 12
DESY testbeam Module Analysis
Runs 6981-6988 B=1T p=5 GeV
B=1 T
situation
xy
z
Mean residuals regrouped the row and column planes
xy
z
Preliminary

## Slide 13
DESY testbeam Module Analysis
Runs 6909,16-18,34,35 B=0 T p = 5,6 GeV
method | rms (stat) xy | bins xy | rms (stat) z | bins z
row | 10 (5) mm | 1280 | 12 (5) mm | 638
column | 11 (5) mm | 1280 | 11 (5) mm | 636
B=0 T situation
Preliminary
The 4 corner chips, the chips around chip 11 and chip 16 were excluded.

## Slide 14
DESY testbeam Module Analysis
Runs 6983-6988 B=1T p=5 GeV
method | rms (stat) xy | bins xy | rms (stat) z | bins z
row | 14 (2) mm | 3322 | 22 (5) mm | 640
column | 12 (2) mm | 3266 | 19 (5) mm | 639
The rms for z is larger than the value of 12 mm obtained for the B=0 run for the module and quad.
The rms in xy is excellent!
Preliminary
The 4 corner chips, the chips around chip 11 and chip 16 were excluded.
B=1 T situation

## Slide 15
DESY testbeam Module Analysis
Performance of dEdx
Use the B=0 an 1 T runs select the central chips (same runs as for deformation studies).
Remove 2 chips per row (deformations and low performance)
Calibrate the number of electrons to be equal for the different chips. Correct for slight z dependence (in B=1T data).
Results for 4 methods to measure the dEdx resolution for electrons and MIPs from data by combining tracks to form a 1 m long track with realistic coverage ~60% coverage.

## Slide 16
DESY testbeam Module Analysis
Performance of dEdx
B=0 T has a large Landau tail
B=1 T tiny Landau tail and a more gaussian distribution
B=0 T
B=1 T
Preliminary

## Slide 17
DESY testbeam Module Analysis
Summary of results dEdx resolution
for MIP corrected for the e-MIP scale
Method | B=0 Resolution (%) | B= 1 Resolution (%)
dEdx 90 | 8.6 | 6.3
dEdx 90 tail | 7.7 | 5.4
Fit amplitude | 9.0 | 6.0
Fit slope | 6.7 | 4.0
The “Fit slope” method gives the best scale corrected MIP resolution of 4.0% for a 1 m track with realistic ~60% coverage in a 1 T B field.

## Slide 18
DESY testbeam Module Analysis
Conclusions
Results for the single electron resolution for xy and z
  B=1 T; =120 mm/ and = 251 mm/
  B=0 T; =287 mm/ and = 268 mm/
Results for study of the residuals in xy in the module plane show that that deformations (systematics on the track position) are less than 14 mm for B=0 and 1 T.
Results for the residuals in z show that systematics on the track position is 22 mm (B=1 T) and 12 mm (B=0 T). The reason for the difference is probably due to limited stats in the calibration procedure for the B=1 T data set.
The “Fit slope” method gives a dEdx MIP resolution of 4.0% for a 1 m track with realistic ~60% coverage in a 1 T B field.