## Slide 1: Pixel TPC analysis topics
Yevgen Bilevych, Klaus Desch, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
Lepton Collider 18 September 2023
8 Quad Module

## Slide 2
Analysis topics and ideas
In the paper
Results on diffusion for B=0 and 1T data
Results on deformations and tracking precision for B=0 and 1 T data
- Results for dE/dx with different methods for B=0 and B=1 T data
Other analysis topics
- Result on single electron efficiency in a high rate environment
- Result for the efficieny angle of incidence

## Slide 3
Analysis topics and ideas
Single electron efficiency in a high rate environment
- Result on single electron efficiency in a high rate environment
Method use DESY testbeam :
measure hits on track near beam centre and further away
could use e.g. the high(est) rate 1 GeV data
However, the rates of the quad test at ELSA were much higher
measure hits on track scanning over the quad detector
Makes in my opinion more sense to use the ELSA quad data
-

## Slide 4
Analysis topics and ideas
Resolution as a function of the incident angle
Method analyse the DESY testbeam
Use the rotated data sets and extract the single electron resolution
We have +- 10 rotated data sets e.g. for the B=0 data
Unfortunately, that is still a rather small rotation angle
Secondly, we don’t expect any dependence.
We could reconstruct in the B=1 T data set curlers and really have large incident angles (up to 180 degrees). These tracks are not triggered and need dedicated pattern recognition to find the circles.