## Slide 1
Regional groundwater modeling for estimating the drained fluxes by the ET works and their impact
Guillemoto Quentin, Orban Philippe, Dassargues Alain, Nguyen Frédéric
Liège University
06/12/2023
Einstein Telescope – Site Preparation Board Workshop 3

## Slide 2
Regional hydrogeological model
  Objectives of the regional groundwater model
  Conceptual model
  Numerical model
  Calibration
Estimation of tunnels groundwater inflow and impacts to regional groundwater
Conclusions & perspectives of the model
Summary

## Slide 3: Objectives of the model
Open cross-border groundwater model for ecosystem services
quantify quantitative impacts of ET tunnels implantations on groundwater
estimate groundwater inflows in tunnels
Regional hydrogeological model extent

## Slide 4: Aquifers
Table of hydrogeological units
Hydrogeological map. RUTHY and DASSARGUES, 2009.
Famennian (limestones-sandstones)
Cretaceous aquifers (sands, chalk)
Houiller (Namurian)
(shales, siltstones, sandstones)
Visean and Tournaisian (limestones)
Lower Famennian aquitard (siltstones)
all the aquifers are simulated until lower Famennian
aquifers considered as connected
with different hydrogeological properties
Notes: Aquiclude Rock formation that contains water but has very low hydraulic conductivity.
Aquitard geological formation that is not sufficiently permeable to extract water

## Slide 5: Geology
Houiller (Namurian)
Cretaceous
Famennian
Visean, Tournaisian
Cretaceous in the North
Older formations to the South
Numerous faults
Wallonia geological map
Notes: Geological section

## Slide 6: Conceptual model
natural boundaries of the model:
based on geology
rivers
North and East : no natural boundary
groundwater measurements set as prescribed heads BCs
Notes: Affleurements : emergences. Famenian émergence south east.

## Slide 7: Numerical model
River network, groundwater level measurements and mesh of the finite elements model
Hydrogeological model according to regional geological model
Feflow® hydrogeological flow model construction:
  finite element mesh
  steady flow model
  based on 2018 data
Regional database used in the model:
  groundwater water level observations, groundwater abstractions (Wallonia, Germany, The Netherlands)
  hydraulic conductivities
  topography
  geology
Mesh sizes about 500 meters length

## Slide 8: Numerical model calibration
 | K m/s |  | K m/d | 
Geology | min | max | min | max
Cretaceous | 1.00E-07 | 1.00E-03 | 0.00864 | 86.4
Houiller | 1.00E-08 | 1.00E-05 | 0.000864 | 0.864
Visean and Tournaisian | 1.00E-07 | 5.00E-03 | 0.00864 | 432
Famennian | 1.00E-07 | 1.00E-05 | 0.000864 | 0.864
Groundwater levels calibration
Plot of groundwater level observations and groundwater level simulations.
Calibration with Pest software
50 pilot points/geological layers, considering prior hydraulic conductivities.
Hydraulic conductivity ranges taken from previous studies in the region

## Slide 9: Numerical model calibration
Calibration of river base flows
Map of natural groundwater recharge calibrated from groundwater contribution to river flow, according to subsurface geology, urbanization and rainfall observations
Measured base-flow are estimated with a classical statistical method applied to river hydrograms
4 watershed with data for now
 | Area (km²) | Rainfall (mm) | Recharge (mm/y) | Observed base flow m3/s | Simulated base flow (m3/s)
Fond de Forêt | 39 | 885 | 123 | 0.17 | 0.19
Berwinne Dalhem | 119 | 885 | 123 | 0.43 | 0.50
Berwinne Valdieu | 49 | 885 | 140 | 0.20 | 0.24
Dalhem Bolland | 31 | 885 | 96 | 0.14 | 0.12
Veul Cottessen | 123 | 929 | 166 | 0.4* | 0.65

## Slide 10: Simulated groundwater levels

## Slide 11: Estimation of tunnels water inflow and impacts to regional groundwater
Method:
    estimate analytically the inflow in the tunnels
    simulate the impacts with the groundwater numerical model
Hydraulic head:
109 – 230 mNAP
Topo: 115 – 280 mNAP
Reference: 0 mNAP
H
ha=100m
Tunnel surrounded by an impermeable lining
Kolymbas and Wagner (2007)
uniform drainage layer decreasing the water pressure at the tunnel to 10 bars = hydraulic head ha = 100 m
Kaq

## Slide 12
for a 380 m3/d tunnel water inflow
Considering 3780 m3/d tunnel water inflow transfer rate Φ = 0.03 s-1
estimated impact
Inflow and impacts of groundwater drained by the tunnel on regional groundwater resources
In the case of Kaq=10-8 m/s conductivity, calculations with analytical solution: 380 m3/d -> 4850 m3/d (depending on H)
for a 4850 m3/d tunnel water inflow
Notes: Depending on the local groundwater level

## Slide 13
Inflow and impacts of groundwater drained by the tunnel on regional groundwater ressources
In the case of Kaq = 10-7 m/s conductivity, calculations with analytical solution: 3800 m3/d -> 48500 m3/d (depending on H)
=> If Kaq >10-7 m/s, large amount of groundwater inflow and huge impact on regional groundwater
for a 4850 m3/d tunnel water inflow
for a 48500 m3/d tunnel water inflow

## Slide 14: Conclusions
Regional numerical model adapted to predict impacts of tunnels on regional groundwater resource
Analytically calculated inflows and first estimation of the effects on the water table and base river flows
  estimation of hydraulic conductivities near tunnels are needed.
  if natural conductivities around tunnel K>10-8 m/s, grouting is needed to reduce inflow rates
Feflow regional 3D groundwater model

## Slide 15
Numerical model improvements
  new geological model data
  additional hydro measurements for the robustness of the model
  sensitivity of model results to hydraulic conductivity values (inflows, regional impacts)
Further sub-models (local models) to be developed using regional model for BCs
  fine discretization of tunnels, complex caverns, local heterogeneities
  transient simulations of the tunnel drainage impacts, during excavations works
The current numerical model can be used, as an ideal tool, for future design simulations of the tunnel
Perspectives

## Slide 16
Thank you for your attention !
q.guillemoto@uliege.be