## Slide 1: Pixelated TPC technology for the future e+e- collider
Yevgen Bilevych, Klaus Desch, Sander van Doesburg, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
CEPC 2023 Nanjing October 2023

## Slide 2: Pixel TPC
(TimePix1) TPX3 chip Quad Module TPC plane
(2007-14) 2017 2018 2019
(Octopuce)
Picture IHEP

## Slide 3: Pixel TPC
Material budget is
  0.01 X0 TPC gas
  0.01 X0 inner cylinder
  0.03 X0 outer cylinder
  < 0.25 X0 endplates (incl readout)
Note the very low budget in the barrel region. Material budget can be respected by different technologies like GEM, MicroMegas and Pixels
TPC is sliced between silicon detectors VTX, SIT and SET
pixel readout is a serious option for the TPC readout plane @ ILC/FFC-ee/CLIC/CEPC colliders
https://www.nikhef.nl/pub/services/biblio/theses_pdf/thesis_C_Ligtenberg.pdf

## Slide 4: GridPix technology
Pixel chip with integrated Grid (Micromegas-like)
InGrid post-processed @ IZM
Grid set at negative voltage (300 – 600 V) to provide gas amplification
Very small pixel size (55 µm)
detecting individual electrons
55 µm
50 µm
dyke
Aluminium grid (1 µm thick)
35 µm wide holes, 55 µm pitch
Supported by SU8 pillars 50 µm high
Grid surrounded by SU8 dyke (150 µm wide solid strip) for mechanical and HV stability

## Slide 5: Pixel chip: TimePix3
256 x 256 pixels
55 x 55 µm pitch
14.1 x 14.1 mm sensitive area
TDC with 640 MHz clock (1.56 ns)
Used in the data driven mode
  Each hit consists of the pixel address and time stamp of arrival time (ToA)
  Time over threshold (ToT) is added to register the signal amplitude
  compensation for time walk
  Trigger (for t0) added to the data stream as an additional time stamp
Power consumption
  ~1 A @ 2 V (2W) depending on hit rate
  good cooling is important
Sensitive area
2+3 mm
14.1 mm

## Slide 6: Single hit resolution in transverse direction
( expected)
B T
Single hit resolution in pixel plane:
Depends on:
pixel size
Diffusion from fit
Note that:
A hit resolution of 250 µm is 25 µm for a 100-hit track ( 1 cm track length)
At 4 T ,
Results from Bonn-Elsa testbeam in 2017
https://doi.org/10.1016/j.nima.2018.08.012
T2K gas

## Slide 7: QUAD design and realization
Guard
TPX3
TPX3
TPX3
TPX3
COld
CArrier
Four-TimePix3 chips
All services (signal IO, LV power) are located under the detection surface
The area for connections was squeezed to the minimum
Very high precision 10 μm mounting of the chips and guard
QUAD has a sensitive area of 68.9%
DAQ by SPIDR
39.6 x 28.38 mm
series of QUADs

## Slide 8: QUAD test beam in Bonn (October 2018)
ELSA: 2.5 GeV electrons
Tracks referenced by Mimosa telescope
QUAD sandwiched between Mimosa planes
  Largely improved track definition
  6 planes with 18.4 μm × 18.4 μm sized pixels
Gas: Ar/CF4/iC4H10 95/3/2 (T2K)
Ed = 400 V/cm, Vgrid = -330 V
Typical beam height above the chip: ~1 cm
Field cage
@Bonn
Published NIMA https://doi.org/10.1016/j.nima.2019.163331

## Slide 9: QUAD single hit resolution
DT = 398 μm/√cm
Transverse
Longitudinal
DL = 212 μm/√cm
The DT value is rather high due to an error in the gas mixing (too low CF4)

## Slide 10: QUAD edge deformations (XY)
Small deformations due to
  Dead zone between chips
  Grounded region between chips
Are corrected by:
  fitted correction function
  adding proper guard wire electrode
Grounded region

## Slide 11: QUAD deformations in transverse plane (XY)
After applying fitted edge corrections
RMS of the mean residuals are 13 μm over the whole QUAD
XY

## Slide 12: QUAD as a building block
in red guard wires
8-QUAD module (2x4 quads) with field cage

## Slide 13
DESY testbeam June 2021
Mounting the 8 quad module between the silicon planes
sliding it into the 1 T PCMAG solenoid

## Slide 14
DESY testbeam June 2021

## Slide 15
DESY testbeam Module Analysis
z global
x global
z global
y global
y local
y local
x local
z local drift
Event display with module and telescope
TPX3 track 1130 hits
c2xy = 677.5/1128
c2z = 775.9/1069
Asymmetric tail outlier removal applied 1071 hits in z kept.
TPX3 track hits
Telescope track hits (off track green)
Preliminary

## Slide 16
DESY testbeam Module Analysis
964 selected tracks
Impressive 1009 hits / track
Run 6916 B=0 T p =6 GeV
Preliminary
8-quad module Tracking precision:
position 9 mm (xy) 13 mm (z)
angle 0.19 mrad (dx/dy) 0.25 (dz/dy) mrad
module tracklength = 157.96 mm
Note that in a B field because of the reduced diffusion the tracking precision will improve substantially

## Slide 17
DESY testbeam Module Analysis
Run 6916-6918 B=0 T p=6 GeV
Three runs at different drift distances
Preliminary

## Slide 18
DESY testbeam Module Analysis
Preliminary
Run 6916-6918 B=0 T p=6 GeV
T2K*
B=0 T
Fitted resolution
287 mm/
273 mm/
ToT > 50 ms
Ed=280 V/cm
s2 xy0= s2pixel + s2xy tele s2pixel= 552/12 mm2
sxy tele=35 mm
Magboltz gives DT 287 mm/
T2K* = T2K gas with O2 and H2O

## Slide 19
DESY testbeam Module Analysis
Preliminary
Run 6983-6990 B=1 T p=5 and 6 GeV
T2K*
B=1 T
Fitted resolution
120 mm/
251 mm/
ToT > 50 ms
Ed=280 V/cm
s2 xy0= s2pixel + s2xy tele s2pixel= 552/12 mm2
sxy tele=42 mm
Magboltz gives for DT =121 mm/
T2K* = T2K gas with O2 and H2O

## Slide 20
DESY testbeam Module Analysis
Runs 6909, 6916-17, 6934-35 B=0 T p =6,5 GeV
There are clear deformations in xy for the chips in the 4 corners.
The field around chip 11 (no grid HV) is affected.
The Efield defined by the field cage is in these areas not homogenous enough
Preliminary
Mean residuals in the module plane with acceptance cuts
xy
z
Vertical white bands guards
B=0 T
situation

## Slide 21
DESY testbeam Module Analysis
Runs 6981-6988 B=1 T p=5 GeV
There are clear deformations in xy for the chips in the 4 corners.
The field around chip 11 (no grid HV) is affected.
The Efield defined by the field cage is in these areas not homogenous enough
Preliminary
Mean residuals in the module plane with acceptance cuts
xy
z
Vertical white bands guards
B=1 T
situation

## Slide 22
We did not include the 4 corner chips and (11), 14, 8, 13 and 19.
These are affected by the field cage and the short in chip 11.
DESY testbeam Module Analysis
Runs 6909, 6916-17, 6934-35 B=0 T p =6,5 GeV
Distribution of mean residuals in the plane
xy
z
Method row
Method column
Preliminary
See back up slide for the two methods that group the module plane
method | rms (stat) xy | bins xy | rms (stat) z | bins z
row | 10 (5) mm | 1280 | 12 (5) mm | 638
column | 11 (5) mm | 1280 | 11 (5) mm | 636

## Slide 23
We did not include the 4 corner chips and (11), 14, 8, 13 and 19.
These are affected by the field cage and the short in chip 11.
DESY testbeam Module Analysis
Runs 6983-6988 B=1T p=5 GeV
Distribution of mean residuals in the plane
xy
z
Method row
Method column
Preliminary
B=1 T situation
method | rms (stat) xy | bins xy | rms (stat) z | bins z
row | 14 (2) mm | 3322 | 22 (5) mm | 640
column | 12 (2) mm | 3266 | 19 (5) mm | 639

## Slide 24
DESY testbeam Module Analysis
Performance of dEdx
B=0 T has a large Landau tail
B=1 T smaller Landau tail and a more gaussian distribution
An electron crossing 8 chips in the module has about 1000 TX3 hits
B=0 T
B=1 T
Preliminary

## Slide 25
DESY testbeam Module Analysis
Method | B=0 Resolution (%) | B= 1 T Resolution (%)
(1) dEdx 90 | 8.6 | 6.3
(2) dEdx 90 tail | 7.7 | 5.4
(3) Fit amplitude | 9.0 | 6.0
(3) Fit slope | 6.7 | 4.0
Method (1) dEdx 90 is truncation at 90%; in (2) large clusters are scanned and removed; The “Fit slope/amplitude” method (3); where the exponential slope and amplitude of the distance between the hits is fitted. The slope gives the best resolution of 4.0%.
The dEdx resolution for MIPs (70% of the electron dE/dx) from data by combining tracks to form a 1 m long track with realistic coverage ~60% coverage (corrected for the e-MIP scale).

## Slide 26
Preliminary Conclusions on module
Preliminary results of the 8 Quad Module in the DESY test beam in June 2021 have been presented
One chip (nr 11) out of 32 was disconnected due to a short*
In run 6916 e.g. 964 tracks were selected with 1009 hits on track
The tracking precision: position 9 (xy) 13 mm (z) in angle 0.19 (dx/dy) 0.25 (dzdy) mrad for a module or tracklength is 157.96 mm
The diffusion coefficients at B=0 T = 287 mm/ = 273 mm/
The diffusion coefficients at B=1 T is = 120 mm/ = 251 mm/
  In agreement with Magboltz = 121 mm/
*the chip was successfully repaired in 2023 Bonn see backup slide

## Slide 27
Preliminary Conclusions on module
Results for the module showed that:
  the HV of the guard wires was well tuned
  B=0 T rms residuals in the module plane xy 12 mm and z 14 mm
  The results are compatible with (very) high stats quad measurement
  B= 1T rms residuals in the plane xy 14 mm and z 22 mm;
High tracking precision demonstrated with small systematics
  deformations xy stay below 12(14) mm
Particle identification based on the numbers of hits and their distance.
  the “Fit slope” method gives a dEdx MIP resolution of 4.0% for a 1 m track with realistic ~60% coverage of the readout plane in a 1 T B field
  NB this is much better than our single chip dEdx result at B=0 T.

## Slide 28: Simulation of ILD TPC with pixel readout
To study the performance of a large pixelized TPC, the pixel readout was implemented in the full ILD DD4HEP (Geant4) simulation
Changed the existing TPC pad readout to a pixel readout
Adapted Kalman filter track reconstruction to pixels
50 GeV muon track with
pixel readout
pads
pixels
details: PhD thesis Kees Ligtenberg

## Slide 29: Performance of a GridPix TPC at ILC
From full simulation the momentum resolution can be determined
Momentum resolution is about 15% better for the pixels with realistic coverage (with the quads arranged in modules coverage 59%) and deltas.

## Slide 30: Summary of the Pixel TPC performance
A single chip GridPix detector was reliably operated in a test beam in 2017
  Single electron detection => the resolution is primarily limited by diffusion
  Systematic uncertainties are low: < 10 µm in the pixel xy plane
  A Quad detector was designed and the results from the 2018 test beam shown
  Small edge deformations at the boundary between two chips are observed
    added guard wires to the module to obtain a homogeneous field
    After correcting the edges, deformations in the transverse plane shown to be < 15 µm
An 8-Quad module has been designed with guard wires
Preliminary test beam results are excellent
  High precision at B=1 T: = 120 mm/ and deformations in xy < 15 µm
  dE/dx resolution for a MIP 1 m track with 60% coverage is 4.1% (at 1 Tesla)
A test beam @ FermiLab with the module in a TPC is planned (US Grant EIC)
A pixel TPC has become a realistic viable option for experiments
  High precision tracking like ILD@ILC in the transverse and longitudinal planes, dE/dx by electron and cluster counting, excellent two track resolution, digital readout that can deal with high rates

## Slide 31: A Pixel TPC at CEPC or FCC-ee
The most difficult situation for a TPC is running at the Z.
At the Z pole with L = 200 1034 cm-2 s-1 Z bosons will be produced at 60 kHz
Can a pixel TPC reconstruct the events?
  The TPC total drift time is about 30 μs
  This means that there is on average 2 event / TPC readout cycle
  YES: The excellent time resolution: time stamping of tracks < 1.2 ns allows to resolve and reconstruct the events
Can the current readout deal with the rate?
  Link speed of Timepix3 (in Quad) is 80 Mbps: 2.6 MHits/s per 1.41 × 1.41 cm2
  YES: This is largely sufficient to deal with high luminosity Z running
  NB: Data size is not a show stopper as e.g. LHCb experiment shows using the VeloPix chip
Picture IHEP

## Slide 32: A Pixel TPC at CEPC or FCC-ee
What is the current power consumption?
  No power pulsing possible at these colliders (at ILC power pulsing was possible)
  Current power consumption TPX3 chip 2W/chip per 1.41 × 1.41 cm2
  So: good cooling is important but in my opinion no show stopper
  For Silicon detectors lower consumption for the chips and cooling is an important point that needs R&D (e.g. microchannel cooling).
  Note that the TPX3/4 chips can be run in LowPowerMode
Can one limit the track distortions?
  There are two important sources of track distortions:
    the distortions of the TPC drift field due to the primary ions
    the distortions of the TPC drift field due to the ion back flow (IBF)
  At the ILC gating is possible; for CEPC or FCC-ee this is more involved

## Slide 33: A Pixel TPC at CEPC or FCC-ee
Is it possible to reduce the IBF for a pixel TPC?
  IDEA: by making chip with a double grid structure (see next slide)
  This idea was already realized as a TWINGRID NIMA 610 (2009) 644-648
  For GEMs for the ALICE TPC this was also the way – several GEMs on top of each other to reduce IBF
  For the Pixel the IBF can be easily modelled and with a hole size of 25 μm an IBF of 3 10-4 can be achieved and the value for IBF*Gain (2000) would be 0.6.
  YES: the IBF can be reduced to 0.6 but this needs R&D
  In the new detector lab in Bonn it is possible to make and study this device
What would be the size of the TPC distortions?
  Recent Tera-Z studies by Daniel Jeans and Keisuke Fuji show that for FCC-ee or CEPC this means: distortions from Z decays up to < O(100) mm
  Beam strahlung gives (now) a factor 200 more background. Detector optimization and shielding is important for TPC and Silicon detectors to reduce pair background.
  Recently I argued that in an ILD like detector the distortions can be mapped out using the VTX-SIT/SET detectors.

## Slide 34: Reducing the Ion back flow in a Pixel TPC
The Ion back flow can be reduced by adding a second grid to the device.
It is important that the holes of the grids are aligned. The Ion back flow is a function of the geometry and electric fields. Detailed simulations – validated by data - have been presented in LCTPC WP #326.
With a hole size of 25 μm an IBF of 3 10-4 can be achieved and the value for IBF*Gain (2000) would be 0.6.
Ion backflow | Hole 30 μm | Hole 25 μm | Hole 20 μm
Top grid | 2.2% | 1.2% | 0.7%
GridPix | 5.5% | 2.8% | 1.7%
Total | 12 10-4 | 3 10-4 | 1 10-4
transparancy | 100% | 99.4% | 91.7%

## Slide 35: Conclusions: Pixel TPC at CEPC
YES: a pixel TPC can reconstruct the Z events in one readout cycle
YES: the current readout of the Timepix3 chip can deal with the rate
The current power consumption is 1W/cm2. So good cooling is important but in my opinion no show stopper; but needs extensive R&D.
Track distortions in the TPC drift volume are a concern at high lumi Z running:
  Track distortions from Z decays in TPC are O(100) mm
  It is possible to reduce the IBF for a pixel TPC by making a device with a double grid
  This needs dedicated R&D that can be performed in the new lab in Bonn
The Z physics program at FCC-ee or CEPC with an ILD-like detector with a Pixel TPC (with double grid structures) sliced between two silicon trackers (VTX-SIT and SET) can be fully exploited. The reduction of beamstrahlung needs more study.
A pixel TPC can perfectly run at WW, ZH or tt energies where track distortions are several orders of magnitude smaller

## Slide 36: Pictures of repair work in Bonn for the EIC TPC project
The short in chip 11 was succesully repaired by Fred Hartjes
Backup

## Slide 37
DESY testbeam Module Analysis
Runs 6909, 6916-17, 6934-35 B=0 T p =6,5 GeV
Regrouping the module plane to increase stats
Granularity 8x8 pixels
acceptance cut
entries > 1500
column 256 pixels
row 4x256 pixels
row 256 pixel
column 4x256 pixels
xy
xy
z
z
Mean residuals (module) row (module) column
For the row plot the data is projected keeping 4 bins in local y (one follows the track)
For the column plot the 4 chip rows are kept separately (that is why there are white bands)
Preliminary
Backup