## Slide 1: Update: RedHat 9+ and the issue of sha-1 roots
January 2024
David Groep

## Slide 2
We know SHA-1 is no longer secure as a crypto digest
  all EECs and ICAs moved away ages ago
but some projects and distros are uselessly deprecating SHA-1 for self-signed (root) certificates – where the signature is immaterial
This affects at least
  FF103+
  RHEL9+ (and rebuilds)
yet … in the cases we could find it only applies to CA certs that are not in the WebPKI (and distro) public trust list
This impacts both joint-trust and igtf-only trust when installed in a non-system location. But thy system locations are different is not obvious from the doc …
Although it conceptually makes no sense …

## Slide 3
With RHEL9 also deprecating SHA-1, but at the same time
still having self-signed SHA-1 based root certs in the ca-certificates
package,
unknown why that distribution treats SHA-1 certs in the X509_CERT_DIR differently
At least there is a policy override for now
update-crypto-policies --set DEFAULT:SHA1
even if that is a rather course-grained tool (and do not pick LEGACY)
Rocky9+, AlmaLinux9+, RHEL9+ and

## Slide 4
OSG shipped the dual-blob mode for a few days
using something like https://www.nikhef.nl/~davidg/tmp/make-trusted.sh
first a “BEGIN TRUSTED CERTIFICATE”, then in the same file “BEGIN CERTIFICATE”
However, it broke:
CANL-Java, extending BouncyCastle, cannot process this blob and will balk even if it does not recognise it (https://stackoverflow.com/questions/55550299/java-can-not-load-begin-trusted-certificate-format-certificate)
open as a dCache Feature Enhancement on CANL Java by Paul Millar
will not be fixed overnight, of course. And we my find other issues thereafter
The OSG experiment

## Slide 5
On 2023-12-20 13:25, Guido Pineda wrote:
> I am using fetch-crl version 3.0.22.
> We have a total of 89 trust anchors configured on our /etc/grid-security directory.
> I have tested fetch-crl with different versions of OpenSSL and here are the
> outcomes:
> For versions 1.1.1k and versions 3.2.0, the amount of errors when trying to verify > the CRL's is only one [which was explainable]
> However, when using OpenSSL version 3.0.7, we get 10 errors
Due to self-compiling OpenSSL and does that ignore the RH crypt-policies?
But …

## Slide 6
Still,
if you still have a SHA-1 root
and you are able to re-issue with the same key (and new serial)
and your EECs do not have dirname+serial in their AKI
your CAs should probably re-issuing its root because that is easier.
But for the large ones, esp. the DigiCert Assured ID Root from 2006 for instance, that will be hard.
And migrating to another (SHA-2 rooted) signing hierarchy will take at least 395 days ... and a lot of engineering on the RP and CA side
The root cause is with RH not understanding what a self-signed trust
anchor is, but that will not help us in the short term.
Mitigations?

## Slide 7
ASGCCA-2007 ArmeSFo
BYGCA CESNET-CA-Root
CNIC DFN-GridGermany-Root
DZeScience DigiCertAssuredIDRootCA-Root
DigiCertGridRootCA-Root IHEP-2013
KEK LIPCA
MARGI
RDIG RomanianGRID
SRCE SiGNET-CA
TRGrid seegrid-ca-2013
Reissuance of roots?
Fixed by now: GridCanada, CILogon basic/silver/OpenID, UKeScienceRoot-2007
Removed: DigiCertGridCA-1-Classic, DigiCertGridTrustCA-Classic
Will be discontinued soon: GermanGrid (GridKA)

## Slide 8: what can you do?
Discussion