## Slide 1: Pixel TPC testbeam results
Yevgen Bilevych, Klaus Desch, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
Lepton Collider 29 January 2024
8 Quad Module
dEdx performance

## Slide 2
DESY testbeam Module Analysis
dEdx performance
Contacted Ullrich Einhaus for dEdx studies in ILD
Extracted the ILC soft parametrisations for enerlgy loss based on G4 and ful simulation of the ILC TPC with T2K gas
Link generated in 2020 with ILC soft v02-02 and v02-02-01

## Slide 3
DESY testbeam Module Analysis
dEdx performance
zoom on Low momenta

## Slide 4
DESY testbeam Module Analysis
Performance of dEdx fit slope method for B=1T
MIP scale corrected resolution 4.2%
[electron has 2.9%]
1 m track 60% and coverage
Preliminary
ILD detector with
rInner = 329 rOuter = 1770 mm
MIP resolution = 3.6% at q=p/2
electron resolution = 2.5%

## Slide 5
DESY testbeam Module Analysis
Pixel TCP dEdx performance
ILD Performance is extrapolated TPC dimensions:
rInner = 329 rOuter = 1770
zMax = 2350 mm // half length
Pixel TPC resolution from electron p = 5 (6) GeV test beam (for B = 1 T) of 2.5% at cos q = 0
Resolution scales as:
1/
Separation electron pion
|<Eloss e> - <Eloss p>| / s p
Separation pion kaon
|<Eloss p > - <Eloss K>| / s p
ILD Pixel TPC

## Slide 6
DESY testbeam Module Analysis
Pixel TCP dEdx performance
Separation pion kaon
|<Eloss p > - <Eloss K>| / s p
Separation pion kaon for different cos(theta) values due to the track length dependence
For cos(theta)=0 till 0.95 the separation lies between the black and red curves. Only above 0.95-0.975 the separation drops till the blue curve.
Excellent performance
ILD Pixel TPC