## Slide 1: Pixel TPC testbeam results
Yevgen Bilevych, Klaus Desch, Harry van der Graaf, Fred Hartjes, Jochen Kaminski, Peter Kluit, Naomi van der Kolk,
Cornelis Ligtenberg,
Gerhard Raven, and
Jan Timmermans
Lepton Collider 12 February 2024
8 Quad Module

## Slide 2
DESY testbeam Module Analysis
dEdx performance for the paper
Make plots for two dEdx methods for the 1T data
Combine chips to form 1 m long track with 60 % coverage for electrons
Method 1) reject large clusters and then runs dEdx @ 90% (gives nr of selected hits)
Method 2) fit the slope of the scaled minimum distance (d) distribution with an exponential function (after scaling down the N(d) distribution):
N(d) scaled = N scale (d) N observed (d)
N(d) scaled is then fitted fr each track with N0 exp(-slope d)
Calculate the “dEdx” variable (method 1 = nr of selected hits; method 2 = slope) for electrons and MIP (== 70% of hits)
Resolution is s (dEdx) / dEdx (for s we use the rms)
Scale corrected MIP resolution: scales up the resolution by
factor = dEdx(MIP))/dEdx(e)/0.7 = method 1(2) 1.10 (1.18)

## Slide 3
DESY testbeam Module Analysis
dEdx performance for the paper method 1
MIP scale corrected resolution
5.3%
[electron has 3.6%]
1 m track 60% and coverage

## Slide 4
DESY testbeam Module Analysis
dEdx performance for the paper method 2
MIP scale corrected resolution
4.2%
[electron has 2.9%]
1 m track 60% and coverage

## Slide 5
DESY testbeam Module Analysis
Efficiency at high hit rates
The efficiency of the device to detect a hit in a high (low) rate environment is measured comparing the mean time over threshold for low and high rate runs at B fields of 0 and 1T.
It was first tested whether this study (measurement) could be done using inclusively “raw” hits without applying a track selection. It turned out that this is rather difficult because the mean ToT varies with the beam location inside the detector. It turned out that the higher the rate the higher mean ToT was (relative changes of 20%). This would lead to large systematic uncertainties for a method based on raw hits.
A more succesfull approach – see next slides - is based on hits associated to TPX3 tracks using the 2 central rows of 6 chips. NB same selection as was used for the dEdx and number of hit results. The mean ToT was calculated for ToT values between 0.15 and 1.4 ms to remove the tail.
.

## Slide 6
DESY testbeam Module Analysis
Efficiency at high hit rates for B=0T
Tot 1 (2) = mean ToT for mcol =1 (2) (each 6 chips) stat errors are neglible
Hits 1 (2) are raw hits with ToT> 0.15 ms
Runs 6916 and 6909 are consistent within 1%
Relative change wrt 6916 in mean ToT -1.2% (mcol=1) -0.3% (mcol=2)
up to 8.5 kHz for 6 chips or 1.4 kHz per chip.
The black numbers could go in the paper
run | ToT 1 | ToT 2 | triggers | time | Hits 1 | Hits 2 | trigger | Rate 1 | Rate 2
 | ms | ms | nr | (s) |  |  | Hz | Hits/s | Hits/s
6916 | 0.6280 | 0.6527 | 16837 | 23221 | 6.252e+06 | 1.312e+07 | 0.72 | 269 | 565
6909 | 0.6220 | 0.6482 | 89250 | 134254 | 2.226e+07 | 5.040e+07 | 0.66 |  | 
6934 |  | 0.6510 | 73414 | 2413 |  | 2.046e+07 | 30.4 |  | 8479
6935 | 0.6204 |  | 73902 | 2414 | 6.948e+06 |  | 30.6 | 2878 | 

## Slide 7
DESY testbeam Module Analysis
Efficiency at high hit rates for B=1T
Runs 6985 and 6988 are consistent with 6983 within 0.5%
Relative change wrt 6983 in mean ToT +1% (mcol=1) +1.7% (mcol=2)
up to 5 kHz for 6 chips or 1.2 kHz per chip.
The black numbers could go in the paper
run | ToT 1 | ToT 2 | triggers | time | Hits 1 | Hits 2 | trigger | Rate 1 | Rate 2
 | ms | ms | nr | (s) |  |  | Hz | Hits/s | Hits/s
6969 | 0.6499 | 0.6658 | 7947 | 13816 | 1.929e+06 | 2.164e+06 | 0.57 | 139 | 156
6983 | 0.6568 | 0.6775 | 67968 | 2825 | 1.162e+07 | 1.409e+07 | 24.1 | 4110 | 4986
6985 |  | 0.6783 | 102488 | 4373 |  | 2.925e+07 |  |  | 
6988 | 0.6653 |  | 95785 | 4251 | 6.148e+06 |  |  |  | 

## Slide 8
DESY testbeam Module Analysis
Efficiency at a high hit rates
The relative change in mean ToT is related to the relative change in the efficiency e - at the working point around 0.6 ms - as:
  See the efficiency vs ToT curve on slide 3
  de/e ~ 0.5 dToT/ToT
This means that the efficiency de/e is stable at the level of +1.7% (B=1T) and -1.2% (B=0T) for hit rates up to 1.2 kHz per chip.
It is demonstrated that running at hit rates up 1.2 kHz gives at most a reduction of 0.6% in the relative efficiency.

## Slide 9
DESY testbeam Module Analysis
To be discussed: further results for the paper
Should we include the ILD pixel TPC dEdx performance? (Presented in LCTPC , dEdxPerformance_ILD.pptx)
Should we include the burst analysis? (last meeting Analysis_burst_jan.pptx)
Should we include the result for the resolution versus incident track angle? See Analysis_circle_feb.pptx , this meeting