## Slide 1
Jay Lyu
Particle Detection Presentation
20th March 2024
for ATLAS Phase-II Upgrade
The ATLAS High-Granularity Timing Detector

## Slide 2
ATLAS: General-purpose detector in LHC
High-Luminosity LHC (HL-LHC):
  Will start operation in 2026
  More collisions to study new phenomena
  Greater precision
  Integrated luminosity increases by a factor of 10
  But: Large increase of pileup interaction!
  To mitigate pileup effects: High-Granularity Timing Detector (HGTD) —> distinguish collisions occurring close in space but well-separated in time.
    Motivation
Notes: The most difficult challenge of this program is the the large increase of the pileup interaction.

## Slide 3
In the forward region, between the Inner Tracker and the End Cap of Calorimeter
Covers from |η| = 2.4 to |η| = 4
    Complement the capabilities of ITk
    Improve the performances in forward region of ATLAS, e.g. jets and leptons reconstruction
    Region very important for the study of the vector boson fusion
Aim at average ~ 30ps per track at the start, 50ps per track at the end
As counting detector for luminosity measurements
    Overview
Notes: It provides an average target time resolution of 30 ps per minimum-ionising particle in the forward region, although at the end of HL-LHC operation, increase to 50ps.

## Slide 4
Small Elements
Detector Design

## Slide 5
Key components: Hybrid module!
Two main parts:
the sensor - Low-Gain Avalanche Detector (LGAD)
the electronics - Application-Specific Integrated Circuit (ASIC)
    Detector Design
Notes:     2 dedicated read-out chips called ASIC

## Slide 6
Pixel (pad) size of 1.3 × 1.3 mm2
Key ingredient to get excellent time resolution: larger current further created by holes
n-on-p silicon hybrid pixel detectors with an internal gain ~10 to 50
An extra highly-doped p-layer (Boron B)!
Low noise amplification to improve the S/N
    Detector Design - LGAD
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Notes:     These LGAD sensors, or say the active detector elements, are made of silicon pixels in order to cope with the thickness constraints and the high radiation level. Needs to be replaced.
    The detection is based on electro-hole pair production.
    When electrons reach the amplification region, new e+e- pairs are created. The new holes drift towards the p+ region and generate a large current. This charge amplification is referred as the internal gain of the LGAD (about 10 to 50).
    After amplification the height of the signal is proportional to the gain. And this current is larger than in a standard diode. So this is the key for the time resolution of energy deposited by Minimum Ionised Particles.

## Slide 7
LGAD signal
Key aspect: rise time :
convolution of signal duration and amplifier rise time
Large gain: ~50ps, signal duration ~1ns
Smaller rise time if thinner & larger gain
If irradiation neutron fluence increases —> smaller charge and current, shorter signal duration
    Detector Design - LGAD
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Notes: A key aspect is rise time. The LGAD rise time is the convolution of signal duration and amplifier rise time. For large gain, the rise time is about 500 ps and the signal duration is approximately 1 ns. It’s smaller for thinner pads and larger gain. When the irradiation neutron fluence increases, the charge is smaller and the rise time and the signal duration are shorter.

## Slide 8
Dedicated front-end electronics
The LGAD sensors will be read out by the ALTIROC
Excellent time resolution and radiation hard
In each module:
  two ASICs Bump-bonded to sensor
  —> 450 pads, 225 channels + common digital electronics in each ASIC
    Detector Design - ALTIROC
Customised read-out ASIC chip: ALTIROC
Notes:     Customised for this experiment it is called ALTIROC, to meet the requirements of time resolution and radiation hardness. It’s a dedicated front-end electronics. In each module, one LGAD sensor is bump-bonded to two dedicated read-out ASICs.

## Slide 9
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
The two TDC provide digital hit data: time of arrival (TOA) and time over threshold (TOT)
Significantly reduced number of channel + an optimised front-end block
Notes:     Compared to other ASICs for pixel detectors, the ALTIROC had significantly reduced number of channel, and a quite different Front End block optimised for time measurement

## Slide 10
~ 25ps
  Landau fluctuations in the deposit energy of the traverse particles
  Non-uniform
  Caused by rare knock-on electrons
  Greater for thinner sensor
    Detector Design - ALTIROC - Time resolution
  where
Notes:     Causedby the rare occurrence of knock-on electrons which have enough energy to become ionising particles.
    The fluctuation around the maximum of energy distribution becomes greater as the sensor becomes thinner.

## Slide 11
  Time-walk < 10ps
  Can be addressed by applying a correction based on the fact that the variations in TOA are related to the TOT
    Detector Design - ALTIROC - Time resolution
  where
Notes:     Time-walk variation is due to the differences in the amplitude of the signals. So the time of preamplifier signal crosses the threshold depends on the pulse height. The lower the height, the later the signal crosses the threshold, consequently the later the pixel detects the hit. If two simultaneous hits have large difference in the pulse height, they will be assigned to different clock cycles and not the same trigger signal.

## Slide 12
  Jitter from 25ps to 85ps after irradiation
  due to the noise in signal, decreases with gain
    Detector Design - ALTIROC - Time resolution
  where
Notes: Jitter variation is due to the noise in the signal, from 25ps to 85ps after irradiation. It’sthe most critical aspect is the design of the analog front-end electronics

## Slide 13
  Time to Digital converter < 10ps
    Detector Design - ALTIROC - Time resolution
  where

## Slide 14
< 15ps after calibration
  non-deterministic jitter contribution
Goal: total time resolution per track = < 30 ps
    Detector Design - ALTIROC - Time resolution
  where
Notes: total time resolution per track combined with number of hits per track

## Slide 15
Assembly
Detector Design

## Slide 16
    Detector Design - Module Assembly
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Notes:     All connections between the ASICs and peripheral electronics are routed through flex cable

## Slide 17
    Detector Design - Module Assembly
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Glue on each sides
Notes:     Modules overlap of 80% at radius <320mm and and 20% for larger radius region.

## Slide 18
    Detector Design - Module Assembly
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Mounted on the CO2 cooling disks
Inserted in the pre-define window
Modules align along x or y direction
Each active double-layer plate: three rings, radius from 120mm to 640mm
Average 2.6, 2.4 and 2.0 hits per track (in to out)
Beyond r > 640 mm are the peripheral electronics
Notes:     Average 2.6, 2.4 and 2.0 hits per track respectively, from small to large

## Slide 19
    Detector Design - Layout
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Notes:     Hermetic vessel (front and rear covers, inner and outer rings)
    Total thickness of 125mm including two moderators.

## Slide 20
    Basic Conditions
Each module requires operating bias voltage in a range up to 750 V
Power consumption constrained by CO2 cooling power
  —> operating temperate -35°C
Outside the HGTD vessel: >14°C
Grounding and shielding similar to ITk requirements
Notes: Operation conditions
  But the external face outside of the HGTD vessel is kept to be at least 14°C to avoid condensation.
  The grounding and shielding of HGTD follows similar requirements as for ITk.

## Slide 21
    Detector Design - Layout
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Notes: 3.5m from interaction point.

## Slide 22
    Summary
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Notes: The timing information provided by LGAD will be used to mitigate the effects of the pile-up interactions in the forward region, and more complex studies could show further impact of this detector.

## Slide 23
    References
CERN, “High-Luminosity LHC | CERN,” Home.cern, Nov. 28, 2019. https://home.cern/science/accelerators/high-luminosity-lhc
“About,” ATLAS Experiment at CERN. https://atlas.cern/about
ATLAS Collaboration, Technical Design Report: A High-Granularity Timing De- tector for the ATLAS Phase-II Upgrade, CERN-LHCC-2020-007 ; ATLAS-TDR-031, Geneva, 2020, https://cds.cern.ch/record/2719855/files/ATLAS- TDR- 031.pdf.
“HGTD | ATLAS IJCLab.” https://atlas.ijclab.in2p3.fr/detector/high-granularity-timing-device/.
M. P. Casado, “A High-Granularity Timing Detector for the ATLAS Phase-II upgrade,” Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, vol. 1032, pp. 166628–166628, Jun. 2022, doi: https://doi.org/10.1016/j.nima.2022.166628.
C. Allaire, “A High-Granularity Timing Detector in ATLAS: Performance at the HL-LHC,” Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, vol. 924, pp. 355–359, Apr. 2019, doi: https://doi.org/10.1016/j.nima.2018.05.028.
N. Seguin-Moreau et al., “ALTIROC1, a 25 pico-second time resolution ASIC for the ATLAS High Granularity Timing Detector (HGTD),” HAL (Le Centre pour la Communication Scientifique Directe), Mar. 2020, doi: https://doi.org/10.22323/1.370.0042.
S. Sacerdoti, “The ATLAS High-Granularity Timing Detector,” CERN Document Server, 2018. https://cds.cern.ch/record/231853. ‌

## Slide 24
Get some real tastes!

## Slide 25
    Performance
Electron beams at DESY
Bias voltage 230V —> MIP charge deposit of 20fC
Achieved
CERN-LHCC-2020-007; ATLAS-TDR-031, Geneva, 2020
Time difference between the sensor and a timing reference (Quartz+SiPM)
Subtracting Landau contribution —> 39ps of the remaining time resolution
Notes:   test results of the time resolution.
  A version of ALTIROC was exposed to electron beams at DESY in 2019. The LGAD were operated with a bias voltage of 230V, resulting in a minimum ionising particle (MIP) charge deposit of 20fC. The time resolution of this device was measured to be 37.6±0.7 ps.
  distribution of TOA as a function of the TOT. The black dots are mean value of the TOA distribution for a given TOT bin extracted from a Gaussian. The red line is a fit of average TOA as a function of TOT.
  Another picture shows the time difference between our sensor and a timing reference (Quartz+SiPM) before and after the time walk correction together with Gaussian fit in the left figure.
  Subtracting Landau contribution we have 39ps of the remaining time resolution.