## Slide 1: Faster, smaller, more and better. Future pixel detectors for particle tracking
Martin Fransen
Detector R&D group, Nikhef

## Slide 2: The LHC at CERN
Swiss/French border near Geneva.
Accelerating and colliding atomic nuclei (protons, lead ions).
Testing theories by detecting ‘debris’ from particle collisions.
Do ‘things’ happen
  with the energies we expect,
  with the particles we expect,
  as often as we expect,
  in the ratios we expect, and
  do we observe things that we don’t expect?
LHC 27 km circumference

## Slide 3: Detectors at the LHC
CMS
LHCb
ATLAS
ALICE

## Slide 4
CMS
LHCb
ATLAS
ALICE
Detectors at the LHC

## Slide 5: Detectors at the LHC
Enclosing a collision point, 10 to 20 m wide, 20 to 45 m long.
Mostly cylinder like, in layers that each perform a specific measurement.
Every 25 ns two bunches of particles collide.  40 million ‘frames’ per second.

## Slide 6: Detectors at the LHC
Particle tracking:
Find the origin of particles.
Minimise scattering and ‘Showering’.
Energy/momentum:
Calorimeter (absorbing all energy)
Muon spectrometer (deflection)
Identify particles by:
Direction of deflection (polarity)
Momentum, velocity, energy

## Slide 7: Particle tracking
Inner layers of detectors at the LHC
Silicon sensors register the spot where a charged particle went through.
Track reconstruction: connecting the dots…

## Slide 8
New 13 billion pixel tracker ALICE
(Yes, that is sort of a 13000 Mpix camera doing 40 million fps)
https://home.cern/news/news/experiments/ls2-report-upgraded-inner-tracking-system-joins-alice-detector

## Slide 9: LHC timeline: Higher event rates
https://hilumilhc.web.cern.ch/sites/default/files/HL-LHC_Janvier2022.pdf
Need more data for better precision and to improve sensitivity for rare phenomena

## Slide 10: Timing for track reconstruction
Current developments put a lot of effort in time measurement.
Need to know down to about 20 ps when something happened

## Slide 11: Pixel chips for particle tracking
Chip with (smart) pixels to read out sensor.
  Hybrid
    Flexible: ‘independent’ development of readout ASIC and sensor
    Bulky and expensive
  Monolithic
    Light/thin, cheap (or least expensive)
    Less flexible in sensor and readout ASIC development
Sketch of cross section
hybrid
monolithic

## Slide 12: The signal starts in the sensor
Charge liberation by ionising particle.
Particle energy loss statistical process.
 Variations in liberated charge.
Animations courtesy of Robbert Geertsema

## Slide 13: Improving signals from a sensor
Conventional planar.
3D sensor.
Short drift distance for fast readout
Signal strength proportional to sensor thickness
Low gain avalanche.
Thin sensor for fast readout
Gain to amplify signal
Animations courtesy of Robbert Geertsema

## Slide 14: Set-ups @ R&D group for timing and efficiency
Faraday cage and 90Sr β source
Electronic pulse generators, powering, ‘chip tuning’
55Fe γ source

## Slide 15: Set-ups @ R&D group for timing and efficiency
Generic pulsed lasers
fs two photon absorption laser
Ps pulsed laser
X-ray set-up

## Slide 16: Testing with laser pulses at Nikhef I
Creating a signal in the sensor using a laser
Allows for sub pixel precision sensitivity scans
Infrared 1060nm = 1.17 eV Penetrates deep into sensor
1 photon = 1 eh pair

## Slide 17: Testing with laser pulses at Nikhef II
3D scanning. Resolution: about 1 µm X,Y, few µm in Z.
1550 nm = 0.8 eV: smaller than silicon band gap!
→ 2 photons = 1 electron-hole pair
380 fs – 5.5 nJ – 1 µm wide spot fast – powerful – precise
Picture by Marco Kraan