## Slide 1
Multispectral imaging of plasma edge emission distributions
Wouter Vijvers
Dutch Institute For Fundamental Energy Research
Notes: Contribute to DIFFER’s mission of developing sustainable energy sources
by taking a big step towards solving the main challenge in fusion research.
This step consists of understanding and stabilizing new shapes of the plasma in the fusion reactor, making use of novel measurement and control system.

## Slide 2: Roadmap to fusion energy
Current-day
machines
ITER
DEMO
1-50 MW
500 MW
2 GW
Goal: contribute to development of an exhaust solution for DEMO

## Slide 3: What is power exhaust and why is it important?
Heat confined to closed magnetic field lines in core
Part of heat flows into scrape-off layer (SOL)
SOL has open magnetic field lines that intersect divertor walls
Have to keep heat loads below material limits (q < qmax)
Biggest challenge in fusion research
Core
SOL

## Slide 4: Why use imaging on fusion plasmas?
Log(length scale) [m]
Log(time scale) [s]
Imaging is “information dense” and enables us to cover a large range of length and time scales, potentially providing insight in a multitude of physics processes
Example movie of plasma in MAST tokamak (CCFE, UK)
Chart: 
| 1.0 | 2.0 | 3.0
Y-Value 1 | 2 | 5 | 3
Practical: passive, single access port, low infrastructure demands
ELMs
Discharge evolution
Detachment front dynamics
MARFE
SOL turbulence
Core MHD (impurities)
Observable by imaging systems
Core turbulence (impurity transport)

## Slide 5: DIFFER aims to advance to quantitative multi-spectral imaging
Hydrogen spectrum
Helium spectrum
Spectral Information
Spectral Model
Plasma State
temperature
density
composition
recombination
…
We need at least 10 spectral channels for quantitative analysis (more is better)

## Slide 6: First results of 4-channel multi-spectral imaging system on TCV
C2+ (465 nm)
Dα (656 nm)
Dg (434 nm)
C1+ (428 nm)
Inverted D-alpha emissivity
~3 eV
~1 eV
MultiCam system:
4 cameras
3 beam splitters
4 interference filters
Tangential view

## Slide 7: Multi-spectral Advanced Narrowband Tokamak Imaging System (MANTIS)
>1 kHz time resolution
1 mm spatial resolution
develop real-time control strategies
generate extensive dataset for modellers
First light (2016)
Relay optic
TCV
Spherical relay mirrors
Relay lenses + narrow bandpass filters/mirrors
80 cm
Cameras + lenses
Goals:
Main lens
…….

## Slide 8: DIFFER aims for future work
Develop real-time acquisition and analysis system
Develop feedback controllers
  Plasma shape (OFIT)
  State of ”detached” plasma
Efficient processing and interpretation of large data volumes via modelling
Application of smarter image processing algorithms (e.g. EVM)
Expansion to other (industrial) applications
Expansion to other parts of the electromagnetic spectrum
FPGA framegrabber
(ECE-I)
Core and edge instabilities
Heat fluxes walls
Molecular spectra
Some examples
Heavy impurities in core
Lighter impurities in edge

## Slide 9
Extra slides

## Slide 10: Summary
Developing a detailed understanding of detachment physics is essential for design of a fusion power plant
Multi-spectral imaging employed to deliver detailed qualitative information on detachment in TCV
MANTIS under development to make step to quantitative imaging, enabling new physics studies and control strategies
Mantis shrimp have eyes with up to 16 types of photoreceptors
Notes: Investigate detachment in the SF- configuration

## Slide 11: First assessment of image quality proves 10+ channels is feasible
Channel 1
Channel 2
Channel 3
Channel 4
Channel 5
Channel 6
Channel 7
Channel 8
Channel 9
Channel 10
Image quality does not degrade rapidly
Some optical aberrations cancel at even channels

## Slide 12: Interpretative modelling required to obtain 2D distributions
Onion-Skin Model solves plasma fluid equations for nested, independent, 1D flux tubes (coupled to 2D neutral transport code)
[J. Harrison et al., Nuc. Mat. En. 000 (2016) 1–6]
Constrained by experimental data
Model “fills gaps” between measured 1D profiles
Time-independent

## Slide 13: Multi-spectral Advanced Narrowband Tokamak Imaging System (MANTIS)
Mantis shrimp have eyes with up to 16 types of photoreceptors

## Slide 14: Development of spectral model
Spectral Model
Spectroscopy in known conditions (Magnum-PSI)
Theory
Collisional-radiative modelling (Yacora)
Full plasma + neutral transport model (Eunomia)