## Slide 1
B.A. Boom, Nikhef Amsterdam
Detector R&D Group Meeting
MEMS Seismometer Development
Detector R&D 7 December 2016 borisb@nikhef.nl

## Slide 2: Backup Slide: MEMS Seismometer
  Seismometer response in m/g
  MEMS Seismometers
    Mass limited to few tens of milligrams
    Lower by miniaturized anti-spring technology
Seismometer sensitivity grows inversely proportional to the system natural frequency squared. A low natural frequency is desirable.
Spring suspension
Proofmass
Capacitors
Thermal actuator
3mm
150µm

## Slide 3: Importance of Quality Factor
Q determines the mechanical noise floor of the sensor
  Q as function gap size
    Strong dependence on gap for viscous regime (-55% @ dx=4.5)
    Moderate dependence on gap for molecular gas damping regime (-25% @ dx=4.5)
    Strong dependence on gap for non-gaseous damping (-55% @dx=4.5)

## Slide 4: Normalized Q factors vs pressure
Q decreases with gap size for all pressures. The minimum observed change occurs around pressure aimed at for packaging
  Q vs gap
    Q factor is maximum in center of gap
    Q factor depends on gap for all pressure ranges:
      Also for non gaseous damping, why?  open question
    At vacuum packaging pressures, gap dependence is minimum.
  Conclusion for ~10-2 mbar
    Reducing the gap by 50% will change the Q by ~50%
    This will double C0
    Throwing away half the sensing fingers halves the damping
     Q is almost independent on the gap size in this pressure range

## Slide 5: MEMS 2017 Conference
My submission got accepted for an oral presentation! 
Relations
Content
Operations