## Slide 1: Clustering methods for high-luminosity
ANDREJ Sarnatskiy
FASTER meeting

## Slide 2: Motivation
Challenges to get data from chips to trigger farm
  Decrease data rate (compression)
  Distinguish PV events during high pile-up (timing)
  Apply corrections as soon as possible for improved reconstruction
What corrections can be applied and where ? e.g. timewalk correction or hit interpolation
Being part of both R&D and LHCb, analysis is done both on LHCb simulation of run5 and the current hardware.
Courtesy: R. E. Geertsema
~ 1.6 Tbps
~ 5 – 40 collisions

## Slide 3: Data processing
Attempt to reduce data rate by rejection in the ASICs
  Uncertainty of hits, e.g. multiple particles mimicking a cluster
  No possibility of correcting data afterwards
  Is the system reliable for the lifetime of U2?
  Current bit structure of TimePix4 still available
The alternative is to apply corrections down the road @ FPGA
  Possibility of combining and correcting pixel hit to clusters
  Firmware is adjustable
Reference to Xavi Llopart’s presentation: https://indico.cern.ch/event/1381444/
Interesting methodology exists already: https://doi.org/10.1016/j.nima.2016.05.077

## Slide 4: LHCb Upgrade 2 simulation
Using LHCb simulation to analyse impact of algorithms
Local (chip) coordinates needed
Failed to use existing functions within LHCb software
No geometry information found

## Slide 5: Struggle of duality
Either run the LHCb simulation ones, then do analysis/transformations later
Or implement additional code in the simulation
Online C++
algorithm
in Gaudi
Offline Python
analysis code
in Jupyter

## Slide 6: OFFLine analysis
Global to local mapping
Columns and rows aligned, reflected if needed
Additional micro alignment applied
Source for systematic uncertainty

## Slide 7: Microalignment
The error is plotted between the centre of the column/row , and the average of hits in that column/row ,

## Slide 8: Clustering interpolation
Three methods tested:
  Charge weighted center of gravity (CoG)
  Binary Every pixel in cluster has equal weight
  Semi-binary Pixel with highest collected charge is Main pixel (M), others are Spectators (S). Different ratio’s (M/S) tested.

## Slide 9: Clustering interpolation
Low statistic: 10 PV events, (200,000) hits
First pixels are clustered by neighbourhood approximation
Later simulation truth information used

## Slide 10: Results
All results are work in progress. Additional checks are still being made.

## Slide 11: Results
Different (M/S) ratio’s tested:
  For different cluster size’s
Some residuals are of order ~ 2000um
Caused either by the alignment or huge clusters

## Slide 12: Results
Filtering out unphysical results shows better resolution
If |residuals| > 300 um filtered out:

## Slide 13: Results
Sanity check
Local residuals, single pixel clusters unfiltered
|res|>200um filtered

## Slide 14: Results
Local residuals, double pixel clusters |res|>200um filtered

## Slide 15: Results
Local residuals, two pixel clusters

## Slide 16: Results
Local residuals, 3 pixel hits, within 2x2
3 pixel hits, within 1x3

## Slide 17: Results
Local residuals, all clusters
|residual| > 200 um filtered out

## Slide 18: Results
Also angular residuals are considered:
  Residuals calculated as projections on the chip:
    is approximated as
    is approximated as
    where is the global radius and is the radius in XY-plane
However the global coordinates are used for these residuals, see slide 9.

## Slide 19: Caveats
Chip 0 (mod24): [dx,dy] = [+0.1, 0]
Chip 1 (mod24): [dx,dy] = [+0.25, 0]
Chip 2 (mod24): [dx,dy] = [+0.40, 0]
Chip 11 (mod24): [dx,dy] = [0, -0.27]
Chip 12 (mod24): [dx,dy] = [-0.1, 0]
Chip 13 (mod24): [dx,dy] = [-0.25, 0]
Chip 14 (mod24): [dx,dy] = [-0.40, 0]
Chip 23 (mod24): [dx,dy] = [0, +0.27]
Apart from the micro alignment, additional systematic deviation found in simulation. Cause unknown.

## Slide 20: Caveats
Apart from the micro alignment, additional systematic deviation found in simulation. Cause unknown.
These results depend on the way pixel hits are and charge sharing is simulated.

## Slide 21: Caveats
Apart from the micro alignment, additional systematic deviation found in simulation. Cause unknown.
These results depend on the way pixel hits and charge sharing are/is simulated.
Clear indication that some code needs to run online
Online C++
algorithm
in Gaudi
Offline Python
analysis code
in Jupyter

## Slide 22: Outlook
Implement detailed timing in simulation → time-weighted clustering
Investigating impact of digitization (bit allocation), e.g. in LHCb simulation and/or Allpix2
Can timing information improve spatial resolution, or vice versa?

## Slide 23: Outlook
Track reconstruction information can be fed back to cluster calculation to improve resolution
Develop firmware to test algorithms during test beam
Hit
Cluster
Track

## Slide 24: Thank you for your time and attention

## Slide 25: BACK UP

## Slide 26: Timing and Timepix
Courtesy: E. Rodríguez2

## Slide 27: Global Coordinates

## Slide 28: Micro alignment
Before
After
every 5th row/column plotted

## Slide 29: Micro alignment
Before After
Before After

## Slide 30: Micro alignment
0th column
255th row