## Slide 1: GridPix Detector for EIC
In spetmber 2024 we found out that the wrong “offline” decoding software was put un arawana.
The decoding software reads the byte streams and decodes the information in the stream.
In particular: the trigger and TPX packets
We know preciser what went wrong: the decoding sw of the Module (with 8 quads and two concentrators) was put on the computer.
This Quad decoding software is different in a few important aspects from the Module software.

## Slide 2: Difference between Quad and module
The difference between the quad and module is that the the module needed more information: namely 4 bits for the concentrator and 4 bits for the chips.
For the quad this is not needed; the four chips get different streams (so no number needed) and no concentrator is present.
The solution chosen was the 8 (most significant) bits of the Spidr time were used for the 4 chip and 4 concentrator bits.
The decoding for quad and module is therefore different.

## Slide 3: The decoding for the quad
The software of the decoding is used in make_tree.
See the commands in the back up slide.
Underlying it uses from /localstore/TPX3/laser_setup_software/SpidrTpx3DataTools
Packet.h Packet.cpp
PacketStream.h PacketStream.cpp
In the module Packetstream the heartbeat was searched for in requiring that concentrator 13 or 14 is found.
For the quad one can only find by chance a nr 13 or 14 in the wrongly decoded bytestream.

## Slide 4: The decoding for the quad
The quad software for the PacketStream.h PacketStream.cpp
was found and this now works.
The question now is do we have the right decoding of the packets?
Here I mean that the column, row, ToT, ToA and trigger time are correctly decoded from the bytestream.
As said the Packet.h Packet.cpp are different for the quad and the module. We tried to re-install an older version, but that may be not the right one.

## Slide 5: Decoding for the quad/module:Packet.h
// For pixel packets
uint64_t Col() const { return EoC() << 1 | Pixel() >> 2; }
uint64_t Row() const { return SuperPixel() << 2 | (Pixel() & 0x3); }
uint64_t EoC() const { return value >> 53 & 0x007F; }
uint64_t SuperPixel() const { return value >> 47 & 0x003F; }
uint64_t Pixel() const { return value >> 44 & 0x0007; }
uint64_t ToA() const { return value >> 30 & 0x3FFF; }
uint64_t ToT() const { return value >> 20 & 0x03FF; }
uint64_t fToA() const { return value >> 16 & 0x000F; }
// standard data stream
uint64_t SpidrTime() const { return value >> 0 & 0xFFFF; } //16 bits?
// data stream with lepcol concentrator 2020
uint64_t Conc() const { return value >> 12 & 0x000F; }
uint64_t Chip() const { return value >> 8 & 0x000F; }
uint64_t SpidrTimeC() const { return value >> 0 & 0x00FF; }
// For the trigger packets
uint64_t Count() const { return value >> 44 & 0x00000FFF; }
uint64_t Coarse() const { return value >> 12 & 0xFFFFFFFF; }
uint64_t Fine1() const { return value >> 9 & 0x00000007; }
uint64_t Fine2() const { return value >> 5 & 0x0000000F; }

## Slide 6: The decoding for the quad
In the Packet.h file one can see that features for the module are added.
As explained for pixel packets the SpidrTime of the Quad is different from the SpidrTimeC of the Concentrator.
Note that the Packet.Conc() will for the Quad just give return a value that corresponds to bits in the SpirTime measurement…
So it is pure chance if they are 13 or 14.
The decoding of trigger packets is unchanged for quad/module.
The Packet.h file looks fine, however we need to have a look at the Packet.cpp. For the quad one cannot use Conc(), Chip() and SpidrTimeC() …

## Slide 7: How the time is coded and decoded
In order to avoid sending 64 bit long words for the precise time measurement, only the least significant bits are sent. To get the full precise time one has to add the (more significant) bits from the SpidrTime and from the Hearbeat.
A Heartbeat is a full precision time stamp that is injected with a frequency of about 1 Hz.
Running at 40 MHz one count is 25 nsec and subdivided in 8 fine bins.
uint64_t Timestamp() const; // Calculates a global timestamp in units of 25ns/4096;
The precise time of arrival “Timestamp” needs to be calculated from components fToA ToA SpidrTime Hearbeat.

## Slide 8: How the time is coded and decoded
In order to avoid sending 64 bit long words for the precise time measurement, only the least significant bits are sent. To get the full precise time one has to add the (more significant) bits from the SpidrTime and from the Hearbeat.
A Heartbeat is a full precision time stamp that is injected with a frequency of about 1 Hz.
Running at 40 MHz one count is 25 nsec and subdivided in 8 fine bins.
uint64_t Timestamp() const; // Calculates a global timestamp in units of 25ns/4096;
The precise time of arrival “Timestamp” needs to be calculated from components fToA ToA SpidrTime Hearbeat.

## Slide 9: How the time is coded and decoded
In order to avoid sending 64 bit long words for the precise time measurement, only the least significant bits are sent. To get the full precise time one has to add the (more significant) bits from the SpidrTime and from the Hearbeat.
A Heartbeat is a full precision time stamp that is injected with a frequency of about 1 Hz.
Running at 40 MHz one count is 25 nsec and subdivided in 8 fine bins.
uint64_t Timestamp() const; // Calculates a global timestamp in units of 25ns/4096;
The precise time of arrival “Timestamp” needs to be calculated from components fToA ToA SpidrTime Hearbeat.
The timestamp calculation for the quad (comment for old setup) was commented out and a new for data concentrator was used.

## Slide 10: Packet.h for quad and validation
I will send the Packet.h for the quad by email (simply comment out the lines and commenting out the concentrator time stamp).
Whether the make_tree plus decoding is really right one can check by the following procedure.
- Take the root file of run 650 as it was produced at Nikhef
- Produce on arawana a root file ./make_tree -r 650 -c 0 -c 1 -c 2 -c 3
Then open the two rootfiles in two browsers
triggers->Scan(“timestamp”)
hits_chip0-> Scan(“toa:tot:col:row”)
hits_chip1-> Scan(“toa:tot:col:row”)
The numbers for timestamp and toa etc should be the same.

## Slide 11: Example of decoding run
Ntuple production start a new terminal (cannot mix the setups for ntuple production and A run/ B analysis):
cd /home/gastpx
source init_laser_setup_software.sh
you are in /localstore/TPX3/laser_setup_software
// Testbeam 2018 // under /localstore2/TPX3/LOGFILES are instructions and Logbook
// Also the data of Run650 is copied /localstore2/TPX3/DATA/CHIP0/Run650 etc up to CHIP3
//
// Note in make_tree that nMaxPackets = 100000000
// one can edit make_tree.cpp end do make make_tree
//
./make_tree -r 650 -c 0 -c 1 -c 2 -c 3
// output with triggers and TPX3 chip data
root -l run650.root