## Slide 1: LEPCol readout scheme proposal
SPIDR
(KU040 FPGA Development Kit)
10Gb Ethernet
3.125Gb 8b10b
DAQ PC
1x
8x
Quad
TPX3 Module
Quad
TPX3 Module
Quad
TPX3 Module
Quad
TPX3 Module
Link
Concentrator
(rad hard+ magnetic field tolerant)
TPX3 @ 160Mb readout speed ≈ 2Mhit/s
8x4x4=128 TPX3 chips per readout syste
KU040 devkit = 1K€
Link concentrator uses cheap (25€) Microsemi FPGA
Option for magnetic field tolerant DC/DC converter
2x
8x
SFP

## Slide 2: Planning first half of 2017
TODO PCB
  Finish layout WireBond board
  Schematic + layout of simple SPIDR adapter
  Schematic + layout of Data Concentrator
  Schematic + layout of SFP board
TODO FPGA Firmware
  Firmware for Data Concentrator
  SPIDR modification

## Slide 3: Planning first half of 2017
 | Jan | Feb | Mar | Apr | May | Jun
PCB |  |  |  |  |  | 
Layout WB Board |  |  |  |  |  | 
Schematic adapter board |  |  |  |  |  | 
Layout adapter board |  |  |  |  |  | 
Schematic DC board |  |  |  |  |  | 
Layout DC board |  |  |  |  |  | 
Schematic SFP board |  |  |  |  |  | 
Layout SFP board |  |  |  |  |  | 
Firmware |  |  |  |  |  | 
DC firmware |  |  |  |  |  | 
SPIDR modification |  |  |  |  |  | 
Bas
Production
Hans
Charles
Intern
Start assembly testing

## Slide 4
HV guard
HV power
WireBond board
Quad assembly

## Slide 5: Data concentrator
FPGA
SFP cage
Q1 data
Q1 power
Q2 data
Q2 power
Q3 data
Q3 power
Q4 data
Q4 power
Power mezzanine
Power mezzanine

## Slide 6: DC/DC converter for data concentrator
Magnetic field tolerant
50W power
12V input?
Mezzanine board