## Slide 1: Particle Detection using the XENONnT Detector
Bart Sarlemijn March 2025
The XENON Experiment. Photo gallery. Available at:
https://xenonexperiment.org/photos/ (Accessed: 13 March 2025)

## Slide 2: XENONnT
XENON Collaboration
  LNGS in Gran Sasso Italy
  1400m underground
  29 institutes, 200 scientists
Detecting dark matter
  Weakly interacting massive particles (WIMPs)
History
  XENON10 15kg Xe (2006)
  XENON100 160 kg Xe (2008)
  XENON1T 3200 kg Xe (2015)
  XENONnT 8600 kg Xe (2020)
The XENON Experiment. The XENONnT experiment underground at LNGS. Available at:
https://xenonexperiment.org/photos/ (Accessed: 13 March 2025)

## Slide 3: Dual-PhaseTime Projection Chamber
Liquid xenon (LXe) & gaseous xenon (Gxe)
Incoming particle
  Excites LXe → emits light (S1)
  Ionizes LXe → frees electrons
Electrons
  Drift upwards
    By electric drift field
    To liquid gas interface
  Accelerated in GXe
    Stronger electric extraction field
    Excites GXe → emits light (S2)
Althüser, L. (2017). Light collection efficiency simulations of the xenon1t experiment and comparison to data.

## Slide 4: Particle Identification
Electronic recoil (ER)
  Scatter of Xe electronic shell
  Background
    Gamma & Beta
Nuclear recoil (NR)
  Scatter of Xe nucleus
  Heavier particles
    WIMPs
    Muons & Neutrons
The XENON Experiment. Time projection chamber. Available at:
https://xenonexperiment.org/time-projection-chamber/ (Accessed: 13 March 2025)
Baudis, L., et al. Dark Matter Detection with XENON [Conference poster]. University of Zurich.

## Slide 5: Xenon
Properties:
  Excellent scintillator:
    Emits UV light( = 175nm)
    Transparent to its own scintillation
  High atomic number (A=131) → enhances WIMP detection ()
  High charge (Z=54) → stops low-energy gamma rays → Self-shielding
  Dense (3 g/cm3 ), low boiling point (178K at 2 bar), which allows for the construction of a compact detector
Moriyama, S. (2016) ‘Direct dark matter searches with XMASS’, Proceedings of the 11th International Workshop Dark Side of the Universe 2015.

## Slide 6: The detector
Outer layers
  Muon Veto
    Pure water
    Tags cosmic-ray muons
      Water Cherenkov Detectors
      Why? NRs
  Neutron Veto
    Gadolinium-doped water
    Capture neutrons → reduce material neutrons
Time projection chamber
  Diameter 1.34m (d) x 1.48m (h)
  494 photomultiplier tubes (PMTs)
    Hamamatsu R11410-22 3-inch
The XENON Experiment. XENONnT infrastructure. Available at:
https://xenonexperiment.org/infrastructure/ (Accessed: 13 March 2025)

## Slide 7: The detector
Aprile, E. et al. (2024). ‘The XENONnT dark matter experiment’, The European Physical Journal C, 84(8), p.784.

## Slide 8: Data acquisition
Gaemers, P.W. (2024) Electronic recoils in XENONnT. PhD Thesis, University of Amsterdam.

## Slide 9: Challenges
Noise reduction
  Deep underground
  Detector housed in water
  Nonradioactive detector materials
Cooling Xe
  Essentially a bomb when cooling stops
  Emergency cooling systems
    LN2 (Liquid Nitrogen)
Cleaning Xe
  Remove impurities
  Steady liquid gas interface
The XENON Experiment. Gaseous Purification System. Available at:
https://xenonexperiment.org/photos/ (Accessed: 13 March 2025)

## Slide 10: XAMS (Xenon Amsterdam)
At Nikhef
  First lab left of the entrance
  Dark matter group
R&D for future generation xenon detectors

## Slide 12: TPCs

## Slide 13: P&ID XAMS