## Slide 1
KATRIN
Karlsruhe
Tritium
Neutrino Experiment
Mathilda Lopuszanski
1

## Slide 2
KATRIN Experiment
  What are the masses of neutrinos?
  Are neutrinos Dirac of Majorana particles?
  New Physics? Sterile Neutrinos?
2
β-decay of molecular Tritium:
[1]

## Slide 3
3
Tritium Source
[2]
95% purity of T2
Continuous injection of T2

## Slide 4
4
Spectrometer
[2]
Electrons only pass with sufficient kinetic energy
Energy resolution of 2.7 eV

## Slide 5
5
[3]
[4]

## Slide 6
6
Focal Plane Detector
[5]
  Detection of electrons in 10 - 100 keV range after the spectrometer

## Slide 7
FPD Wafer
  Monolithic 148 p-i-n diode array
  Single silicon wafer
  Thickness: 503 µm
  Diameter: 125 mm
  Pixel area: 44 mm2
  Bias voltage: 120 V
7
[5]

## Slide 8
Focal Plane Detector System
  Ultra High (10-9 mbar) and High Vacuum (10-6 mbar)
  Cooling system
  Veto to detect incoming muons using scintillators
  Shielding of lead and copper to reduce 𝛾-background
8
[5]

## Slide 9
Data Processing
9
  Pixel connected to preamplifier with a pogo pin
  24 preamplifier modules in radial pattern connected to 6 or 7 pixels
  Optical fibers transport the signal to DAQ system
  DAQ system is at 2.5 m distance from the front end electronic and consists of triggers system and ADC
[5]

## Slide 10
Perfomance of the FPD
  Dead layer thickness
    155.4 ± 0.5 (stat.) ± 0.2 (sys) nm
    46% charge collection
  Detection efficiency
    95.0 ± 1.8 (stat.) ± 2.2 (syst.) %
    mainly due to dead layer losses
  Energy resolution
    Global 1.86 ± 0.13 keV
  Timing resolution
    between 96 ns and 246 ns for 18 keV electrons
  Charge splitting over pixels
10
[6]

## Slide 11
11
References
[1] M. Steidl, KIT Katrin. KIT Available at: https://www.katrin.kit.edu/1033.php.
[2] M. Aker et al 2022 J. Phys. G: Nucl. Part. Phys. 49 100501
[3] Katrin Experiment investigates Neutrino Mass Available at: https://phys.org/news/2018-06-katrin-neutrino-mass.html.
[4] Katrin. Wikipedia (2025). Available at: https://de.wikipedia.org/wiki/KATRIN.
[5] J. F. Amsbaugh et al 2015 Nucl. Inst. Meth. A 778 arXiv:1404.2925v3
[6] The KATRIN collaboration et al 2021 JINST 16 T08015 DOI 10.1088/1748-0221/16/08/T08015

## Slide 12
12