## Slide 1
photo: J. Wenninger
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; iFAST, grant agreement 101004730, FCCIS, grant agreement 951754; E-JADE, contract no. 645479; EAJADE, contract number 101086276; and by the Swiss CHART program
http://cern.ch/fcc
Highlights from Future Circular Collider Feasibility Study and Path to Construction
NIKHEF, 16 May 2025
Frank Zimmermann
on behalf of the FCC collaboration

## Slide 2: FCC integrated program
FCC-ee
FCC-hh
stage 1: FCC-ee (Z, W, H, ) as Higgs factory, electroweak & top factory at highest luminosities
stage 2: FCC-hh (~100 TeV) as natural continuation at energy frontier, pp & AA collisions; e-h option
highly synergetic and complementary programme maximising the physics opportunities
common civil engineering and technical infrastructures, building on and reusing CERN’s existing infrastructure
FCC integrated project allows the start of a new, major facility at CERN within a few years of the end of HL-LHC
2020 - 2045
2045 - 2065
2070 -

## Slide 3: Feasibility Study Report published on 31 March 2025
Structure:Three Volumes
Vol. 1: Physics, Experiments and Detectors
Vol. 2: Accelerators, Technical Infrastructures, Safety Concepts
Vol. 3: Civil Engineering, Implementation & Sustainability
Three FSR volumes & other FCC-related input to 2025/26 European Strategy Update posted at https://indico.cern.ch/event/1534205/
to be prepared with Overleaf & published by EPJ (Springer-Nature) – FCCIS members
Input for Update of European Strategy for Particle Physics

## Slide 4
Expressions of Interest for the Development of Detector Concepts and Sub-detector Systems for the Future Circular Collider FCC
https://repository.cern/records/azb81-6ee21
FCC-ee baseline layout with four collision points allows for
four multi-purpose detectors, with different scientific and cost optimisations,
e.g., for
Higgs physics, ultraprecise electroweak and QCD measurements, heavy flavour physics, and searches for feebly coupled particles, respectively.

## Slide 5: Reference layout and implementation:PA31 - 90.7 km
Layout chosen out of ~ 100 initial variants, based on geology and surface constraints (land availability, access to roads, etc.), environment, (protected zones), infrastructure (water, electricity, transport), machine performance etc.
“Avoid-reduce-compensate” principle of EU and French regulations
Overall lowest-risk baseline:
90.7 km ring, 8 surface points,
4-fold superperiodicity
(Reduction from the 97.8 km and the 12 surface sites in 2019)

## Slide 6
-9%
-7%
-60%
-180M
TUNNEL DE
90.7 km
8 SITES DE SURFACE
40 ha
PROFONDEUR DES PUITS
150 À 400 m
16.4 Mt
DE MATÉRIAUX EXCAVÉS
TUNNEL DE
97.8 km
12 SITES DE SURFACE
110 ha
PROFONDEUR DES PUITS
150 À 580 m
18 Mt
DE MATÉRIAUX EXCAVÉS
-60%
1.9 MILLION m3 /AN
DE CONSOMMATION MOYENNE D’EAU
4.9 MILLION m3/AN
DE CONSOMMATION MOYENNE D’EAU
ÉVOLUTION DES CHIFFRES CLÉS
ÉVITER
RÉDUIRE
COMPENSER
APPLICATION DU MODÈLE D’OPTIMISATION E.R.C
AVANT 2020
EN 2025
-18%
1.3 TWh
DE CONSOMMATION MOYENNE D’ÉLECTRICITÉ
1.6 TWh
DE CONSOMMATION MOYENNE D’ÉLECTRICITÉ

## Slide 7: Resource needs & connections to regional infrastructure
Road access
Road accesses developed for all 8 surface sites
Four possible highway connections defined
Less than 4 km of new roads required
Electricity 1.1 – 1.8 TWh/year
(Current CERN consumption: 1.3 TWh/year)
Feasibility of electrical grid connections confirmed with RTE
The loads could be distributed on three main sub-stations :
Point D with a new sub-station covering PB – PD – PF – PG
Point H with a new dedicated sub-station for collider RF
Point A with existing CERN station covering PB – PL – PJ
Raw water 1 – 3 million m3/year
CERN 2022: 3.2 million m3
No new intake required
Waste heat recovery & supply
Demand for >300 GWh/year identified
Requires development with stakeholders

## Slide 8: Environmental initial state analysis
  The environmental initial state analysis at the eight surface site locations (~600 ha covered) did not reveal principal showstoppers for the project.
  Documentation provides basis for the environmental impact assessment.
  All data will be made publicly available in particular for host states administrative and technical services.
Environmental information system

## Slide 9: Environmental analysis coverage
Soil
Landscape
Forest and agriculture
Background noise
Air quality
Traffic
Topography and relief
Wetlands
Biodiversity, habitats, fauna and flora
Aerial imaging
Technical risks
Urbanisation
Economy and social topics

## Slide 10: simplified longitudinal profile of FCC tunnel and geology
FCC passes below Lake Geneva moraines
FCC above limestone
FCC inclined at 0.5% gradient to minimise depth of point F
Limestone unavoidable between G-H
  Tunneling mainly in moraine layer (soft rock), well suited for fast, low-risk TBM construction.
  6 million m3 excavated volume  8.5 million m3 excavation material on surface
  CE Designs of all underground structures developed
  Average shaft depths ~240 m
  To fix the vertical position of the tunnel, interfaces between geological layers have to be known

## Slide 11: FCC – Initial Sub-Surface Investigations
ARVE
BORNES
MANDALLAZ
USSES
VUACHE
JURA1
JURA2
LAKE
RHONE
Complete
Ongoing
Starting shortly
  Site investigation results provide:
  Locations of geologic interfaces, permitting to fix vertical position and inclination of tunnel
  All data will be made publicly available in particular for host states administrative and technical services.
  Southern work package status end March 2025
  All geophysics acquisition and interpretation in sections Arve, Mandallaz, Usses, Vuache is completed (40 km)
  6 boreholes completed (including logging and testing), 4 remaining bore holes complete in May 2025.
  Preliminary results positive, confirming 3D geol. model
  Northern work package completed by end 2025
  1st drilling ongoing, further from April 25 (pending permits)
  28 boreholes and 80 km of geophysics in total between October 2024 and December 2025

## Slide 12
Transformation of Molasse (FCC ~8 Mm3 volume) into fertile soil for agricultural and other uses
Materials: Molasse from HL-LHC construction
Duration: 4+ years (2024 - )
Trials with 5 000 t molasse
Estimate of reuse quantities:
40% refill of quarries (∼ 7.5 Mt)
25% reconstituted soil (∼ 4 Mt)
30% deposit (∼ 5 Mt)
5% other reuse

## Slide 13: territorial dialogue and public participation
So far, 11 sessions incl. public meeting at CERN on April 24, 2024. brought together over 1,500 people in France & Switzerland
In France, dialogue and public participation is mandatory for significant projects to hold a public debate before a decision is made to proceed with the project. Similarly, in Switzerland, it is customary.
Dialogue Website
In 2026 ?
Formal public participation is planned for 2026 in France and Switzerland.
In 2025
Second cycle of information meetings on the FCC study in the territory.
First cycle of workshops with residents in municipalities potentially affected by surface sites.
Privileged meetings with citizen stakeholders of the territory.

## Slide 14: Architectural language and integration development
Architecture Using materials, facades expressions, and design to integrate facilities into the local context, softening industrial architecture and minimizing building’s presence.
Landscape Utilizing the site’s natural terrain and potential to minimize visual impact on the landscape while creating spaces that foster biodiversity.
Community Creating spaces for the local community to gather for leisure and recreation and providing opportunities to showcase science and share project insights.
Nature restoration
Recreational use of energy
Leisure
Green roofs
Utilising the terrain
Facade expression
Green buffer
Education
Innovative construction
Uninterupted landscape
Community gardens & pastures

## Slide 15
Légende :
Guérite d’accès
Bâtiment Tête de puits
Systèmes Ventilation
Systèmes Refroidissement
Systèmes Cryogénie
Stockage Helium liquide
Stockage Helium gazeux
Systèmes électriques
Sous-station électrique
Site Boundary
Green buffer - Trees Access road
Code couleur :
Phase 1 : FCC-ee Phase 2 : FCC-hh
building
area
surface site development

## Slide 16
Constructed space | 25’562 m2
Buildings | 14’130 m2
Paved | 11’432 m2
Green space | 11’825 m2
TOTAL | 37’388 m2

## Slide 17: VIEW 1
Existing
EFFEKT / 53 - 184
FCC / Surface sites

## Slide 18
VIEW 1
New Structures
EFFEKT
/ 54 - 184
FCC / Surface sites

## Slide 19
Stage 1: e+e- collider FCC-ee
parameter | Z | WW | H (ZH) | 
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50
beam current [mA] | 1294 | 135 | 26.8 | 5.1
number bunches / beam | 11200 | 1852 | 300 | 64
total RF voltage 400/800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.09 / 0 | 2.1 / 9.2
luminosity / IP [1034 cm-2s-1] | 145 | 20 | 7.5 | 1.4
total integrated luminosity / IP / year [ab-1 / yr] | 17 | 2.4 | 0.9 | 0.17
beam lifetime [min] | 21 | 13 | 9 | 10
parameter | Z | WW | H (ZH) | 
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50
beam current [mA] | 1294 | 135 | 26.8 | 5.1
number bunches / beam | 11200 | 1852 | 300 | 64
total RF voltage 400/800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.09 / 0 | 2.1 / 9.2
luminosity / IP [1034 cm-2s-1] | 145 | 20 | 7.5 | 1.4
total integrated luminosity / IP / year [ab-1 / yr] | 17 | 2.4 | 0.9 | 0.17
beam lifetime [min] | 21 | 13 | 9 | 10
Main parameters
FCC-ee functional layout

## Slide 20
Chart: 
| FCC-ee Z | FCC-ee WW | FCC-ee ZH | FCC-ee tt | KEKB | SuperKEKB | SLC | CLIC | ILC | ILC at CERN
 | 180 | 27 | 8.5 | 1.5 | 40 | 250 | 500 | 9152 | 13120 | 52500
required for top up
routinely
achieved
positron rates [1010e+/s]
required at IP
>1014 e+/s
x100
SLC e+ target failed after 5 years of operation
<SLC rate

## Slide 21
FCC-ee injector complex
coordinated by Paul Scherrer Institute, supported by CHART
novel e+ source
- HTS solenoid (15 T on axis, tested 18 T @ 12 K), factor 3 higher yield
- proof-of-principle beam tests at PSI SwissFEL from 2026

## Slide 22: FCC – Linacs based on PSI design
Electron and Positron Linacs
HV klystron modulator
4 accelerating structures
Bunch repetition rate:
  100 Hz x 4 bunches in Z-mode,
  100 Hz or lower in other modes
RF module layout:
  4 AS per module,
  1 quad per AS
Acc. Structure (AS):
  Active length = 3 m,
  average aperture <a>/λ:
    0.15 <2.86 GeV
    0.12 >2.86 GeV
  RF frequency = 2.8 GHz
  Max gradient 22.5 MV/m
SwissFEL
Courtesy Paolo Craievich and Alexej Grudiev on behalf of the CHART/FCC-ee Injector Study collaboration

## Slide 23
linac
“golden
pulse”
→
minimum
energy
variation
for any
charge in
top-up
bunches

## Slide 24
FCC-ee injector complex with High Energy Linac – CERN Prévessin site
“cut and cover” construction technique

## Slide 25
Transfer Lines Injector to Booster-Collider (possible connection to North Area)

## Slide 26
past (black, green) and present colliders (red),
and the proposed FCC-ee (blue)
arrows symbolise important lessons from other colliders incorporated into the FCC-ee design
luminosity per interaction point vs. centre-of-mass (c.m.) energy
SLC

## Slide 27
FCC-ee collider: key elements for high performance
double ring collider
- many bunches, high current, like LHC and B factories, different from LEP
top-up injection
- standard at modern light sources, like SLS
- used at recent e+e- colliders, PEP-II (USA), KEKB (Japan), BEPCII (China)
crab-waist collision scheme
- successfully demonstrated at DAFNE (Italy) and SuperKEKB (Japan)
superconducting radiofrequency (RF) system
- Nb/Cu 400 MHz SC cavities pioneered at former CERN LEP
- bulk Nb 800 MHz SC cavities similar to ESS (Sweden), EuXFEL (Germany)
- revolutionary highly efficient RF power sources
- new operation scheme for flexible energy switching & reduced complexity
→100,000x luminosity of LEP

## Slide 28
luminosity per electrical energy: a giant step in efficiency
P. Janot,
M. Wolf,
N. Bellegarde,
M. Benedikt,
F.Z.

## Slide 29
FCC-ee booster
full energy booster, ramping from 20 GeV to 46 GeV – 182.5 GeV;
injection ~every minute to keep collider beam currents constant;
booster intensity ~1% of collider; full RF voltage as in collider
Collider
Booster

## Slide 30: superconducting RF system – key technology, R&D
Superconducting elliptical cavity
400 MHz, 2-cell, copper Nb coated
1.5 m. long
400 MHz Cryomodule
Superconducting elliptical cavity
800 MHz, 6-cell, bulk Nb
Nb3Sn if R&D is successful
800 MHz Cryomodule
X 264
X 66
X (408 + 448 booster)
X (102 + 112 booster)
400 MHz Collider
800 MHz Collider + Booster
Move from Nb @2K to Nb3Sn @4.5 K would reduce cryogenic power by factor 3
Nb3Sn on Cu coating
Equivalent to a Q of 9*109 @5 MV/m @4.5 K
Almost 1 order of magnitude better than LHC !
Room for improvement
FCC 1 cell
QPR Nb3Sn
G=216 Ω
4.5 K

## Slide 31: FCC-ee operation sequence and SRF concept
2-cell 400 MHz SRF system for Z, W and ZH, entire system installed at operation start of FCC-ee
Constant cavity coupling thanks to reverse phase operation at Z
Reverse phase operation (RPO) mode allows increasing RF cavity voltage (Y. Morita et al., SRF, 2009)
Experimentally verified with high beam loading in KEKB (Y. Morita et al., IPAC, 2010)
Baseline solution for EIC ESR (e.g., J. Guo et al., IPAC, 2022)
Full installation prior to operation, incl. cryogenic system (vs staging with shutdown requirements)
  Allows flexibility and switching between Z, WW, ZH modes thanks to RPO
  Suppression of the single-cell 400 MHz system (reduced R&D, installation, commissioning, etc…)
800 MHz SRF system real estate gradient increases by ~ 20% by using 6 cells cavities instead of 5 cell.
Z,
WW
ZH

## Slide 32
I. Syratchev
efficient RF power source
Very efficient: >90%, Low Voltage: <50kV
Compact: ~ 1m3, Cost effective (w.r.t. klystron)

## Slide 33: beam vacuum
ultrathin NEG coating (200 nm, 10x thinner than for LHC)
winglets with localized synchrotron radiation absorbers, electron-cloud mitigation by sawtooth, and shielding
electron beam
synchrotron radiation
Radiation Power Density simulated with SynRad+ for sawtooth absorber surface
Peak Power Density: 74.6 W/mm²
Maximum Power per absorber:4.5 kW
Most of the radiation is intercepted perpendicularly by the inner side of sawtooth surface, which diminishes the reflection of the radiation back into the vacuum chamber.
sawtooth surface

## Slide 34: shielding concept: limiting cumulative dose (ttbar)
Synchrotron radiations absorbers and additional shielding aiming factor ~100 dose reduction in arcs

## Slide 35
Key topics:
SC IR magnet system &Cryostat design
3D integration
IR mock-up / INFN
Q1 prototype tested at cold in SM18 (CERN), October ‘23
M. Koratzinos, PSI
M. Boscolo, F. Palla, INFN
J. Seeman, SLAC
P. Tavares , CERN
machine detector interface

## Slide 36: design of arc magnets, girders, prototypes, mock-ups
Vibration studies with girder on PSI jacks
Arc half-cell =
the most repeated region of mechanical hardware in the tunnel:  77 km over 90 km are arc cells
Booster dipole
low-field cycling magnet
Goal: arc half-cell mock-up to test aspects related to:
Transport - Installation
Integration - Alignment
Assembly - Maintenance
Stability inspection - Safety
Fabrication, machining capabilities, etc.
Interaction Region mock-up
under construction in Frascati
central chambers, just back
from e-beam-welding in UK ;
will be used for paraffin test

## Slide 37
R&D on ~40 K HTS arc sextupoles & quadrupoles as alternative
Lower power consumption and lower weight.
More flexibility in optics design.
An improved filling factor.
State-of-the-art technology with increased societal impact
The HTS4 sextupole demonstrator: left: CAD design; right: the magnet after winding, before the assembly of its aluminium sleeve.
Cryogenic power supply: The CPES demonstrator comprises five full-bridge phase modules using Gallium Nitride (GaN)transistors
Left: HTS tape coating station, with the uncoated tape-spool on the left and coated tape spool on the right. Right: CT sextupole coil wound w coated dummy tape.

## Slide 38
developed at CERN since 2021, in close collaboration with code users to enable beam dynamics simulations from low-energy hadron rings to high-energy lepton colliders
greatly extended for FCC design studies and SuperKEKB modelling with contributions from CHART, EPFL, KEK,…
beam physics aspects like synchrotron radiation, tapering, beam-beam, polarisation and spin dynamics (ongoing ) …
Interaction Region (SuperKEKB)
dynamic aperture FCC-ee
beam-beam emittance blow-up
etc.
Xsuite: key package for integrated simulations of FCC-ee and other projects, e.g. EIC and SuperKEKB
complete modelling of beam dynamics
essential tool for choice of preferred FCC-ee lattice variant and further optimisation
full lattice modelling for SuperKEKB
xsuite simulation toolkit

## Slide 39
G. Iadarola
Reproducing from “scratch” construction and matching of FCC-ee LCC lattice, based on
→ tutorial in form of Jupyter notebooks illustrating (1) lattice ”assembly”, (2) linear optics matching, (3) controlling chromatic & detuning properties

## Slide 40
Other FCC-ee science opportunities
Examples:
production of true muonium
creation of a Bose-Einstein condensate of positronium
high(est)-energy photons, Compton imaging, nuclear research etc.
spatially coherent photon beams, possibly down to 0.1 Å wavelengths
higher average and peak brightness than any existing or planned light source
radioactive isotope production
neutron source
large circumference, high energy, abundant positron production, low-emittance beams, high-power beamstrahlung, injector complex → FCC-ee offers unique opportunities for various other fields of physics and science
CERN-FCC-ACC-2025-0005,
doi: 10.17181/CERN.BSP4.H8ED

## Slide 41
FCC-ee cost estimate, FSR 2025
Domain | Cost [MCHF]
Civil engineering | 6,160
Technical infrastructures | 2,840
Injectors and transfer lines | 590
Booster and collider | 4,140
CERN contribution to four experiments | 290
FCC-ee total | 14,020
+ four experiments (non-CERN part) | 1,300
FCC-ee total incl. four experiments | 15,320
Operation of the FCC collider at the working point will require later installation of additional RF cavities and associated cryogenic cooling infrastructure with a corresponding total cost of 1,260 MCHF.
Capital cost for construction of the FCC-ee is summarised below. This cost includes construction of the entire new infrastructure and all equipment for operation at the Z, WW and ZH working points.

## Slide 42
Stage 2: hadron collider FCC-hh
Main parameters FSR 2025
FCC-hh functional layout
parameter | FCC-hh | FCC-hh CDR | HL-LHC
collision energy cms [TeV] | 85 | 100 | 14
dipole field [T] | 14 | 16 | 8.33
circumference [km] | 90.7 | 97.8 | 26.7
beam current [A] | 0.5 | 0.5 | 1.1
synchr. rad. per ring [kW] | 1200 | 2400 | 7.3
peak luminos. [1034 cm-2s-1] | 30 | 30 | 5 (lev.)
events/bunch crossing | 1000 | 1000 | 132
stored energy/beam [GJ] | 6.5 | 8.3 | 0.7
integr. luminosity / IP [fb-1] | 20000 | 20000 | 3000
Parameter optimization towards “acceptable power consumption” (~max. consumption of FCC-ee)
Magnetic field considered realistic with today’s technologies (Nb3Sn, ~14T)

## Slide 43
FCC-hh optimization of power consumption
Technical system choices and areas for further optimisation:
Accelerator optics design to increase arc dipole filling factor and maximize beam energy
Cold mass either at 1.9 K with superfluid He (studied in CDR, cf. LHC) or with 4.5 K with forced flow
Temperature of beam vacuum system (beam screen)
 | FCC-hh 90.7km Nb3Sn 14T | FCC-hh 90.7km Nb3Sn 14T
Magnet temperature | 1.9 K | 4.5 K
Yearly electricity consumption | < 2.5 TWh | < 2.0 TWh
Significant reduction of electrical power consumption (close to factor 2!) compared to CDR version 2019.
Potential for further reduction, to be addressed with design optimisation and R&D in next phase.
Long term R&D towards accelerator magnets based on high-temperature superconductor materials.

## Slide 44
for 2nd stage: FCC-hh High-Field Magnet Nb3Sn Demonstrators
12- and 14-T short Nb3Sn demonstrators;
tests scheduled for 2026 -
in parallel HTS magnet R&D (next slide)
Updated FCC-hh magnet baseline parameters
B. Auchmann
 | Unit | CDR 2019 | 2025-Nb3Sn
Dipole field | T | 16.0 | 14.0
Dipole aperture | mm | 50 | 50
Magnetic length | m | 14.3 | 14.3
Operational temp | K | 1.9 | 1.9
Tunnel length | km | 97.8 | 90.7
Arc length | km | 82.0 | 76.9
Arc filling factor | - | 0.80 | 0.83
Energy c.o.m. | TeV | 50+50 | 42.5+42.5
Loadline fraction | - | 0.86 | 0.80
Jc at 16 T and 4.2 K | A/mm2 | 1500 | 1200
# dipoles | - | 4587 | 4463
# quadrupoles | - | 760 | 520

## Slide 45: HFM HTS Program
REBCO characterization and QC with TAPESTAR® at CERN.
Insulated tape-stack coils for assembly in common-coil config at CERN.
CEA process development for metal-insulated racetrack coils.
Iron-based Superconductor powder synthesis and R&D tape fabrication at CNR SPIN
Fabrication of racetrack from solder-impregnated tape-stack cable at PSI.
REBCO coated-conductor R&D line at KIT.
B. Auchmann

## Slide 46: Timeline till start of FCC construction
Feasibility Study
2024
2025
2026
2027
2028
2029
2030
2031
2032
2033
“Pre-TDR Phase”
TDR Phase
Construction 
FS Report
cost update
Project
Decision
CE Concept Design update
Start construction
Detector EOI submissions
FC3 formation, call for CDRs
Detector CDRs submitted to FC3
ESPPU
2025/26
Construction Design
TDR
cost update
CE Tender Design
engineering design 
Phase 1 Site Investigations
Environmental Impact study & Authorization Process
Phase 2 Site Investigations
accelerator design, technical infrastructure design, R&D, towards TDR
pre TDR
cost update
FC3 = Future Circular Collider Committee

## Slide 47
Start of FCC-ee physics run
FCC-ee Accelerator
Key dates
FCC-ee Detectors
FCC Approval: Start of prototyping work .
European Strategy Update: FCC Recommendation
FC3 formation, call for CDRs, collaboration forming
End of HL-LHC upgrade: more ATS personnel available .
Detector CDRs (>4) submitted to FC3
Detector component production
Four detector TDRs completed
Start detector installation
Start detector commissioning
End of HL-LHC
Start of ground-breaking and CE at IPs
Industrialisation and component production
Technical design & prototyping completed
Start accelerator installation
Start accelerator beam commissioning
End of HL-LHC upgrade: more detector experts available
Detector EoI submission by the community
– 2047
– 2046
– 2045
– 2044
– 2043
– 2042
– 2041
– 2040
– 2039
– 2038
– 2037
– 2036
– 2035
– 2034
– 2033
– 2032
– 2031
– 2030
– 2029
– 2028
– 2027
– 2026
– 2025
FCC Feasibility Study Report
2047 –
2046 –
2045 –
2044 –
2043 –
2042 –
2041 –
2040 –
2039 –
2038 –
2037 –
2036 –
2035 –
2034 –
2033 –
2032 –
2031 –
2030 –
2029 –
2028 –
2027 –
2026 –
2025 –

## Slide 48
Status of the FCC Global Collaboration
161 Institutes
38 Countries
+
CERN
Increasing international collaboration is a prerequisite for success: links with science, research & development and high-tech industry will be essential to further advance and prepare the implementation of the FCC
FCC Feasibility Study:
Aim is to further increase the collaboration,
on all aspects, in particular on
Accelerator and Physics/Experiments/Detectors
38 Participating Countries
Austria – Belgium – Brazil – Canada – Chile – Colombia – Czech Republic – Denmark – Estonia – Finland – France – Georgia – Germany – Greece – Hungary – India – Iran – Italy – Japan – Latvia – Malta – Mexico – Netherlands –
Norway – Pakistan – Poland – Portugal – Republic of Korea – Romania – Serbia – Spain – Sweden – Switzerland – Thailand – Türkiye – Ukraine – United Kingdom – United States of America

## Slide 49
“One of CERN’s most promising current projects, with significant scientific potential, is the construction of the Future Circular Collider (FCC): a 90-km ring designed initially for an electron collider and later for a hadron collider..
Refinancing CERN and ensuring its continued global leadership in frontier research should be regarded as a top EU priority, given the objective of maintaining European prominence in this critical area of fundamental research, which is expected to generate significant business spillovers in the coming years.”
https://commission.europa.eu/topics/strengthening-european-competitiveness/eu-competitiveness-looking-ahead_en
edited by Mario Draghi, and officially handed over to Ursula von der Leyen in September 2024
EU competitiveness report

## Slide 50
Key messages:
FCC-ee: Z bosons, WW pairs, Higgs bosons, and pairs in 15 years of operation. Z and WW running: precise energy calibration. Flexible sequence of beam energies. Four multi-purpose detectors. Preparing the base for future highest-energy hadron collider.
Other pioneering science becomes possible
FCC feasibility study report completed ! – the result of >10 years of intense work, with a focus on local implementation.
No showstopper found and clear path ahead with plenty of opportunities, also for other sciences, and with a significant socio-economic net benefit.
No lack of challenges – community consensus essential.
thank you !