## Slide 1: Timepix 4 Substrate ideas
3 JUN 2025
Yutaro Takahashi

## Slide 2: Wet-etched glass
Micronit
  Received cost estimate for 3, 10 and 10 wafers
Concept Wafer
(status last meeting)
Proposal Nikhef
Suggestion Micronit
(Better use of space, cheaper production)
 | # of wafers |  | 3 | 10 | 20
 | # of substrates |  | 30 | 100 | 200
Costs |  |  |  |  | 
WP1 | NRE activities |  | 4840 | 4840 | 4840
WP2 | Etching |  | 14860 | 29340 | 45780
Total without WP2.1 |  |  | 19700 | 34180 | 50620
Cost per substrate without WP2.1 |  |  | 656,6667 | 341,8 | 253,1
Next steps
  Finalize design
  Determine order quantity
  Order

## Slide 3: Finalizing design
Substrate variants
  3 shapes
    Top connect: 40x36 [mm]
    Single side connect: 51x25 [mm]
    Double side connect: 60x25 [mm]
  If chipboard gets wider, it starts making less sense to connect on the side
  Redesign substrate and reorganize wafer??
Quantities
  Maximize number of substrates, or maximize number of test samples?

## Slide 4: Some other progress
Thermal simulation – Poor thermal conductivity of glass
  DT over the substrate is ~4,8°C
  Acceptable
Ceramic 3d printing
  Printed channels of 0,2 x 0.2 mm