## Slide 1: A comparison of amplitude and phase characteristics of ambient seismic noise between the EMR and Sardinian candidate site for hosting Einstein Telescope
S Koley et al.

## Slide 2: Stations used in the analysis
EMR station
  Terziet
    Latitude: N, Longitude: E
    Local depth: 250 m
    Elevation: 150 m
Sardinia stations
  P2 (Bitti)
    Latitude: N, Longitude: E
    Local dept: 264 m
    Elevation: 808 m
  P3 (Onani)
    Latitude: N, Longitude: E
    Local depth: 252 m
    Elevation: 758 m

## Slide 3: Terziet ASD characteristics – vertical component
Analysis window: Feb 01 – 28, 2023 (both for EMR and Sardinia)
ASDs calculated every 800 seconds (both for EMR & Sardinia), sampling frequency: 40 Hz
Attenuation increases with frequency, with percentile attenuation of a factor 150 at 10 Hz

## Slide 4: Terziet ASD characteristics – horizontal component (EW)
Attenuation increases sharply up to 4 Hz – due to 30 m soft layer (H/V peak at 4 Hz)
Borehole azimuthal correction of is applied to align the surface and underground data

## Slide 5: Terziet ASD characteristics – horizontal component (NS)
Surface-underground attenuation curve for seismic noise in the North-South component shows similar trend as the East-West component (previous slide)
Note the sharp peaks at 3.12 Hz, 6.19 Hz, 7.22 etc. which show lower attenuation due to difference in propagation type (diving waves)

## Slide 7: P2 near Bitti - ASD characteristics – vertical component
Mode attenuation curve shows attenuation factor of about 4
percentile attenuation of about 15 at 10 Hz, which is about a factor 10 lower than what is observed at Terziet

## Slide 8: P2 near Bitti - ASD characteristics – horizontal component (EW)
Attenuation in the same range as observed for the vertical component
Borehole azimuthal correction of is applied to align the surface and underground data

## Slide 9: P2 near Bitti - ASD characteristics – horizontal component (NS)
Surface-underground attenuation curve for seismic noise in the North-South component shows similar trend as the East-West component (previous slide)
Similar to Terziet we observe peaks at 8.27 Hz and 12.47 Hz which show lower attenuation

## Slide 10: P3 near Onani - ASD characteristics – vertical component
Mode attenuation curve shows attenuation factor of about 3 in the 4 – 10 Hz band
percentile attenuation of about 16 at 10 Hz which is about a factor 10 lower than what is observed at Terziet

## Slide 11: P3 near Onani - ASD characteristics – horizontal component (EW)
Attenuation factor of about 2 – 3; slightly lower than P2
Borehole azimuthal correction of is applied to align the surface and underground data

## Slide 12: P3 near Bitti - ASD characteristics – horizontal component (NS)
Surface-underground attenuation curve for seismic noise in the North-South component shows similar trend as the East-West component (previous slide)
Multiple peaks show even lower attenuation underground

## Slide 13: Cross-correlation analysis between surface and underground stations
Cross-correlations estimated every hour using window lengths of 100 s and an overlap of 50 s between consecutive windows; windows per hour
  Frequency domain cross-correlations estimated as
  , where represents the Fourier transform of signals , and ‘*’ represents complex conugation
  Cross-correlation significance = 0.11
What do the cross-correlations tell us:
  In the case the underground seismic field is composed as a superposition of plane waves as propagating from random directions , the resulting field over many realizations is a stochastic field
  If the underground field is stochastic in nature, for scalar displacement fields (avoid ), we know that the
  If we observe this behavior, a plane wave approach is suitable

## Slide 14: P3 near Onani - surface to underground horizontal component cross-correlations
Analysis window: Feb 01 – 28, 2023
Wavenumber is estimated as ,
Note the peaks at 4.79 Hz, 5.35 Hz, 9.07 Hz, 12.48 Hz that are due to directional sources of noise

## Slide 15: P2 near Bitti - surface to underground horizontal component cross-correlations
Analysis window: Feb 01 – 28, 2023
Wavenumber is estimated as ,
In the NN band below 10 Hz, the red curve matches the observed cross-correlations

## Slide 16: P2 and P3 - surface to underground vertical component cross-correlations
Wavenumber is estimated as ,
Strong deviations from the sinc function is observed beyond 6 Hz: possibly due to the vector nature of the displacement field, implying ainsotropy

## Slide 17: Terziet - surface to underground horizontal component cross-correlations
Wavenumber is estimated as ,
Note the peaks at 3.12 Hz which is directional (not polarized in NS component)
Above 4 Hz, the observed and plane wave correlation fields don’t match

## Slide 18: Terziet - surface to underground vertical component cross-correlations
Wavenumber is estimated as , – Such low P-wave velocity is a proof of the fact that the vertical component underground is dominated by SV waves compared to P-waves
Note the peaks at 3.12 Hz which is directional (polarized along Z - EW)
Above 5 Hz, the observed and plane wave correlation fields don’t match
  Implies a plane wave approach break down for Terziet
  Anisotropic illumination
  Inhomogeneous medium

## Slide 19: Thanks