## Slide 1
Cavity locking, thermal effects and the phase cameras
By Laura van der Schaaf
20.06.2017

## Slide 2
Overview
Cavity control
Effect of thermal effects on the cavity control
Thermal compensation system and the phase cameras

## Slide 3
Laser light – not an infinitesimal line
Complex amplitude
Time dependence
We will see that the sensitivity of AdV is affected
by this phase shift
Part of the laser light is made to oscillate at different frequencies: sidebands
Phase increases with propagation distance
Phase decreases with beam width
m
n
In case of plane wave:
6 MHz
131 MHz

## Slide 4
Simulating cavities - Finesse
It would be far too tedious (if not impossible) to compute something as complicated as a gravitational wave detector by hand. Therefore, several simulation tools are available, amongst which Finesse. All further computations in this presentation are done in Finesse.
Finesse can be downloaded (for free!) here: http://www.gwoptics.org/finesse/
The python wrapper can be found here (yes – again for free!): http://www.gwoptics.org/pykat/
Examples can be found here: http://www.gwoptics.org/finesse/examples/
To learn about some of the parameters the following slides follow roughly the Virgo arm example
(thus the parameters deviate slightly from AdV)

## Slide 5
Overview of exercise cavity that we want to control
I1: 6.5 W
1064 nm
nin
s1: 5 m
eom1
maxtem 0 sets the basis for the intensity distribution of the laser light:
nEO1
For now only this mode
f [Hz]
mod eom1 adds sidebands at the frequency fMI, with modulation index 0.1 and order 1:
6.264080 MHz
nEO2
1
0.1
s2: 5 m
nMI1
nMI2
nME2
nME1
s: 3000 m
sMI: 9.7 cm
sME: 9.6 cm
MI: reflective coating
R = 0.98621
T = 0.01378
ME: reflective coating
R = 0.999932
T = 50e-6
Rc = 3530 m

## Slide 6
Overview of exercise cavity that we want to control
I1: 6.5 W
1064 nm
nin
s1: 5 m
eom1
nEO1
nEO2
s2: 5 m
nMI1
nMI2
nME2
nME1
s: 3000 m
sMI: 9.7 cm
sME: 9.6 cm
MI: reflective coating
R = 0.98621
T = 0.01378
ME: reflective coating
R = 0.999932
T = 50e-6
Rc = 3530 m
Place some (virtual) photo detectors to see
the cavity response to changing arm length

## Slide 7
Overview of exercise cavity that we want to control
I1: 6.5 W
1064 nm
nin
s1: 5 m
eom1
nEO1
nEO2
s2: 5 m
nMI1
nMI2
nME2
nME1
s: 3000 m
sMI: 9.7 cm
sME: 9.6 cm
MI: reflective coating
R = 0.98621
T = 0.01378
ME: reflective coating
R = 0.999932
T = 50e-6
Rc = 3530 m
inside
reflected
transmitted
By scanning the length of the cavity resonances occur.
Resonance condition:
Wavenumber k different for the three frequency components.

## Slide 8
Locking the cavity – is the current information sufficient?
Power inside the cavity (and in the transmitted beam) drops when:
Cavity gets longer
Cavity gets shorter
Laser power fluctuates
Cavity cannot be locked to the working point by just monitoring the power at different ports.

## Slide 9
Demodulation
Construct an error signal which is zero at the locking point and has opposite signs for too long respectively too short cavities.
Method:
- measure the power of the beam with a fast diode:
Power in carrier
after EOM
Power in sideband
after EOM
Transfer function for location of interferometer where you are looking at the signal (example transmission)
DC contribution
RF contribution
Part we want to extract next – the error signal

## Slide 10
Demodulation
Demodulate to get the quantity X:
1. Multiply with local oscillator:
2. Low-pass filter to get the I and Q values (resp. X):

## Slide 11
(part of) X as error signal
By demodulating and low pass filtering at the sideband frequency X can be measured. In Finesse a detector for demodulation already exists, with the following code the I value (real part of X) is measured and can be used as an error signal.
With this signal we can lock the cavity such that the power in the cavity is maximized. The sign of the error signal differs for too long/too short cavity and is not affected by laser power fluctuations.

## Slide 12
Is there any thing that can affect the error signal in an unwanted manner?
Before only this mode
For a different mode the error signal looks different – might lock onto the 8 0 mode by mistake
→ problems with for example angular controls

## Slide 13
Laser light – not an infinitesimal line
Complex amplitude
Time dependence
We will see that the sensitivity of AdV is affected by this phase shift
Part of the laser light is made to oscillate at different frequencies: sidebands
Phase increases with propagation distance
Phase decreases with beam width
m
n
In case of plane wave:
6 MHz
131 MHz
Remember the statement from the beginning?

## Slide 14
The marginally stable power recycling cavity
Higher order modes:
Higher order modes (HOM) can cause unstable control signals and a reduction of the sensitivity of the interferometer
Power recycling cavity shorter than the arms with larger beam waist
→ more likely to harbor higher order modes

## Slide 15
The marginally stable power recycling cavity
Higher order modes:
Higher order modes (HOM) can cause unstable control signals and a reduction of the sensitivity of the interferometer
The IMC cleanes the input light → there should be no significant contributions from higher order modes at the input
IMC (input mode cleaner):
Filters out higher order modes from the input.

## Slide 16
Where do higher order modes come from?
Substrate inhomogeneities
Thermal lensing
Coating errors

## Slide 17
Plan of action against higher order modes
Compensation plates
CO2-lasers
(only one shown)
information
Phase cameras
(sensor)

## Slide 18
5
Scan the laser front with Archimedean spiral to get phase and amplitude maps.
Typical beam size 833 μm
PD aperture 55 μm

## Slide 19
Demodulation for PC
Add computation

## Slide 20
Amplitude maps
Example of amplitude maps for carrier and sideband from the Nikhef Prototype.

## Slide 21
Phase maps
Buried inside the phase maps is distance information – and thus information on the thermal effects that altered the effective path length.

## Slide 22
Phase images dominated by the scanner
Phase images are dominated by the scanner – either calibrate for scanner effect or work with relative phase images (phase of sideband – phase of carrier).

## Slide 23
Make a movie of the amplitude images over time for the two ports
Show phase movies if they look sensible

## Slide 24
Following slides wont be used

## Slide 25
Reminder of the working principle of a cavity
M1
M2
L
Einc
Eins
Etrans
Erefl
In interferometric gravitational wave detectors several cavities are employed. This slide is an overview of the basic physics involved in cavities. For simplicity plane waves are used.
Plugging values into the equations:
The electric field amplitude and thus
the power depend on the length of the cavity.
In principle cavities should be usable
to measure the distance between two mirrors.

## Slide 26
Already with this super simple model
we see that temperature effects can
alter the laser power at the different
locations in/outside the cavity.
Effect of temperature on the simple model
M1
M2
L
Einc
Eins
Etrans
Erefl
In interferometric gravitational wave detectors several cavities are employed. This slide is an overview of the basic physics involved in cavities. For simplicity plane waves are used.
Small note of warning:
In optics you have reflectivity and reflectance
Reflectivity: how much amplitude is reflected
Reflectance: how much power is reflected
And similarly for transmissivity and transmittance
Reflectivity and transmissivity given by the Fresnel equations, depend on:
Material
Polarization
Propagation direction
temperature
Plugging values into the equations:
n2 = 1.45
Temperature changes affect:
shape of mirror
(heating mirrors makes them bulge outwards)
refractive index:
- due to temperature
- due to bulging outwards